## Slide 1: Locate fuel demand alongside the infrastructure serving it
WEEK 1 | South Africa petrol and diesel outlook
Source: Natural Earth 1:50m; kickoff appendix / schematic networks; illustrative regional CSV. 6 Oct 2026.
Consolidated infrastructure + regional demand | illustrative, billion litres/year
N
0
500 km
NATREF
Sasol CTL
Astron
Cape Town
Gqeberha
Richards Bay
Durban
Lesedi*
Eastern / coastal
4.5 bn L
Inland
10.0 bn L
Western / coastal
4.0 bn L
Other regions
2.5 bn L
Demand to assess
Region | Petrol | Diesel
Eastern / coastal | 1.8 | 2.7
Inland | 4.2 | 5.8
Western / coastal | 2.0 | 2.0
Other | 1.0 | 1.5
National | 9.0 | 12.0
Seven infrastructure layers
Production, pipelines, ports, roads, rail, storage and corridors.
Marker area shows illustrative demand, not a catchment. Other operator storage sites remain to locate.
Production
Port
Vopak storage*
Road
Product pipe
Rail
*Approximate sites. LAEA / WGS84. Transport is schematic; capacities/access unverified.
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No network analysis, service-area polygon or measured cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson

## Slide 2: Map conditional market access from Durban and Lesedi
WEEK 1 | South Africa petrol and diesel outlook
Source: Existing appendix routes; illustrative candidate connections, not verified catchments. Natural Earth 1:50m.
Durban | coastal deliveries + inland transfers
Lesedi | inland dispatch + connected markets
N
0
500 km
Durban
Lesedi*
Illustrative routes; no service-area boundary
N
0
500 km
Durban
Lesedi*
Illustrative routes; no service-area boundary
Condition | Accessibility test
Existing road / pipe candidate | Capacity, compatible product, dispatch, access rights and delivered cost
Expanded-route candidate | A specified rail/road/pipeline intervention, timing, interfaces and customer access
Road candidate
Pipeline candidate
Intervention to assess
Observed customer catchments: not supplied. Physical reach is conditional; contracts and competitors determine commercial access.
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No network analysis, service-area polygon or measured cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson

## Slide 3: Separate demand, accessible volume and Vopak flows
WEEK 1 | South Africa petrol and diesel outlook
Source: Three illustrative story CSVs; annual petrol/diesel only. No actual Vopak throughput supplied.
ILLUSTRATIVE ONLY | billion litres/year | petrol + diesel; jet excluded
National demand 21.0 − domestic production 7.0 = required imports 14.0
Exports and stock movements are zero in this illustration only.
Market | Demand | Feasible flows | Commercial envelope | Current unique demand served | Additional candidate
Eastern coastal | 4.5 | 3.8 | 2.5 | 1.0 | 1.5
Inland | 10.0 | 8.2 | 6.0 | 2.0 | 4.0
Combined | 14.5 | 12.0 | 8.5 | 3.0 | 5.5
Count customer demand once
Durban receipts 2.8 + Lesedi receipts 2.0 − shared transfer 1.8 = unique demand served 3.0
Additional candidate volume is conditional, not forecast capture. The envelope includes domestic and imported supply. Western/other access remains unassessed.
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No network analysis, service-area polygon or measured cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson