## Slide 1
Liquid fuels
demand and supply
model
Manish hand-back
6 October | Sourced data, explicit gaps and levers
6 October 2026
Internal working discussion
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: Speaker note: Walk through four sections: the project question, the analytical
requirements, the model-build problem and the delivery approach. The purpose is to
connect the analyst's tasks to the decisions the engagement needs to support.
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.

## Slide 2: Five packages are back: three complete, two partial with stated gaps
Handback against the 6 October checklist | petrol and diesel; jet tracked separately
Source: evidence notes on manish-branch, 6 October 2026. Changes are the analyst's position, pending review.
Strictly Confidential
Work package | What came back | Status
1 Integrity | Every P1 flag traced to its source cell. Three extraction errors fixed, one of them ours (2013 sales read from a superseded sheet). Industry and agriculture baselines now sourced. | Complete; decisions with Nigel
2 Traceability | 45 datasets mapped from publisher to original, extract and consuming function. The engine still reads six files, all from the Reatile workbook. | Complete
3 Provincial demand | Nothing official exists after 2023-Q1; the department's own schedule promised data to end-2024. Estimate for 2023-24: petrol within 2-3%, diesel 5-11%. | Partial: no later data exists
4 Fuel balance | SARS customs data fetched by script, 2010 to August 2026. Petrol balances. Diesel does not: 3-4 bn litres a year is supplied but not in recorded sales. | Partial: no product split or stocks
5 Driver evidence | All seven categories sourced or marked. Prices to October 2026, quarterly GDP, mining, manufacturing, freight and CPI series added. | Complete; open rows listed
155 tests pass; lfm check passes with 52 open exceptions; both scenarios run. No change is on main.
1 Status
2 Findings
3 Levers
4 Decisions

## Slide 3: Five input changes are applied on the branch; one moves model results
Approved by Manish, awaiting Nigel | register reconciled, every changed row marked unreviewed
Source: evidence notes on manish-branch, 6 October 2026. Changes are the analyst's position, pending review.
Strictly Confidential
Change | Evidence | Effect on the model
2013 national sales: diesel 11.89 to 12.14, petrol 11.15 to 11.44 bn litres | Department's published sheet, both district workbooks and the Reatile history agree | None: reference data
Refinery file: 948 rows to 348 | Production_High range ran to row 13,102 and swept in seven other tables | None: supply identical every year
Jet history: 72 rows to 57 | Extraction ran into three regional tables below the national one | None
Industry baseline 2.5 to 1.50 bn litres; agriculture 0.7 to 1.06 | Department energy balance, 2021. Placeholders had no source | Diesel demand falls 0.63 bn litres a year
New reference data: SARS trade, operator output, prices, quarterly GDP, Stats SA monthly, power diesel | Each with an evidence record and register rows | None: not read by the engine
Left unchanged for Nigel: marine baseline, elasticities, road parameters, 2014 and 2018 provincial treatment.
1 Status
2 Findings
3 Levers
4 Decisions

## Slide 4: Customs data settles 2024 diesel imports and shows where fuel enters
SARS trade statistics, chapter 27 fuel lines | litres from 2014; fetched by script
Source: evidence notes on manish-branch, 6 October 2026. Changes are the analyst's position, pending review.
Strictly Confidential
2024, bn litres | SARS | FIASA | Trade report
Diesel imports | 10.793 | 14.793 | 10.8
Petrol imports | 4.001 | 4.000 | 4.0
Diesel exports | 0.796 | 0.821 | 0.79
Petrol exports | 0.920 | 0.939 | 0.92
Imports cleared at | 2024 | Share
Durban | 11.84 | 80%
Cape Town | 1.09 | 7%
Mossel Bay | 0.62 | 4%
East London | 0.53 | 4%
Richards Bay | 0.39 | 3%
01 | FIASA's figure is a misprint
FIASA's 14 793 is exactly 4 000 million litres above customs. In 2014-17, 2020 and 2025 the two agree to within 12 million litres.
02 | Durban clears four-fifths of imports
Petrol plus diesel, by customs office. This is a public proxy for entry port, not a terminal record. 98% of diesel imports arrive by sea.
03 | Botswana is sourcing less through South Africa
Its recorded imports from South Africa fell from 1.02 to 0.63 bn litres between 2023 and 2024; SARS exports show the same direction.
1 Status
2 Findings
3 Levers
4 Decisions

## Slide 5: More diesel is supplied than recorded sales explain
Four separate routes point to 3-4 bn litres a year | how to report it is left for Nigel and Henry
Source: evidence notes on manish-branch, 6 October 2026. Changes are the analyst's position, pending review.
Strictly Confidential
Route | What it shows | Size
Product balance | Sales less imports plus exports implies 1.1-1.8 bn litres of local diesel output in 2022-24, beside 4.5-6.0 bn of petrol. The plants made 0.85 litres of diesel per litre of petrol in 2017-19. | About 3 bn a year
Operators' output | Secunda, Natref and Astron report 13-14 bn litres of refined products; the balance needs 8.7 (2023) and 10.6 (2024). | 4.4 and 3.3 bn
Customs, both sides | SARS confirms the import and export figures. Nine neighbours report importing 1.8-2.0 bn litres from South Africa against 1.6-1.9 recorded as exported. | Exports do not explain it
Fuel levy volumes | SARS: levy declared on 24 bn litres in the eleven months to February 2024, against about 20 bn of recorded sales for the same months. | About 3.9 bn
Likeliest reading: the fuel is real, taxed and used, and the department's sales series undercounts. That is an inference; the levy figures are round and cover both fuels.
1 Status
2 Findings
3 Levers
4 Decisions

## Slide 6: Fuel prices have risen sharply in 2026 and the model has no price response
Regulated inland prices, rand per litre | department to February 2026, Central Energy Fund sheets after
Source: evidence notes on manish-branch, 6 October 2026. Changes are the analyst's position, pending review.
Strictly Confidential
Effective | 4 Feb | 4 Mar | 1 Apr | 6 May | 3 Jun | 1 Jul | 5 Aug | 2 Sep | 7 Oct
Petrol 95, retail | 20.10 | 20.30 | 23.36 | 26.63 | 28.06 | 26.10 | 25.58 | 26.92 | 30.25
Diesel 0.05%, wholesale | 17.92 | 18.54 | 25.91 | 31.18 | 27.93 | 24.79 | 26.17 | 29.11 | 31.95
01 | Diesel is up 78% and petrol 50% since February
Our price series stopped in April 2024 this morning. It now runs monthly from January 2011 to October 2026.
02 | One South African study gives the response
Boshoff (2012): a 10% rise in the real price lowers petrol demand by about 5% and diesel by about 1% in the long run.
03 | Coastal prices are no longer published
Coastal diesel has no value from December 2025; coastal petrol and paraffin none from March 2026. The fund prints Gauteng prices only.
04 | Power diesel: 0.31 litres per kWh
Three years of reported burn against turbine output agree. The workbook's efficiency implies 0.244, a fifth too low. Adoption is left for Nigel.
1 Status
2 Findings
3 Levers
4 Decisions

## Slide 7: The seven levers each have evidence and a proposed base case; none is calibrated
Draft for discussion | base case = things continue as they perform today
Source: evidence notes on manish-branch, 6 October 2026. Changes are the analyst's position, pending review.
Strictly Confidential
Lever | Evidence held | Proposed base case | Needed to reach litres
Road to rail | Rail 214 Mt (2019), 156 (2022), 168 (2025); road 895 to 975. Target 250 Mt by 2029/30 | Rail holds its present share | Haul distance; diesel per tonne-km
Electric vehicles | 2.8% of 2025 sales against a quoted 20% target; 0.2% battery electric. Peers: Brazil 6%, Southeast Asia near 20% | Continues from actual sales | AIA's view of the path; fleet turnover
Grid power | Turbine output FY2022-26; 0.31 litres per kWh | Eskom's own plan | Decision on the factor
Industry | Mining and manufacturing volumes 7% below 2019, flat | Flat, then with GDP | Litres per unit of output
Agriculture | Value added to 2025; diesel use to 2021 | With sector value added | Choice of driver
Vehicle fleet | 12.6 million vehicles, growing 1.4% a year | Present growth rate | Fuel split by class; distance after 2014
Growth | Treasury 1.6%, 1.8%, 2.0%; then 2% | As set on 5 October | Wiring into the model
1 Status
2 Findings
3 Levers
4 Decisions

## Slide 8: Five further levers are proposed, mostly where the model is silent
Additions to the seven | two do not sit on a high-low demand axis and would be shown as variants
Source: evidence notes on manish-branch, 6 October 2026. Changes are the analyst's position, pending review.
Strictly Confidential
Proposed lever | Why it belongs | Proposed base case
Fuel price level | Diesel up 78% and petrol 50% since February; the model has no price response | Prices settle at a stated level
Private backup generation | The power lever covers grid turbines only. SARS attributes a 3 bn litre fall in levy volumes to increased energy availability | No return of load-shedding
Neighbours' sourcing through South Africa | Throughput for Vopak, not South African demand. Botswana's imports via South Africa fell 38% in a year | Present volumes continue
Refinery events | Petrol and diesel must meet 10 ppm sulphur from 1 July 2027. Natref does not yet comply; Astron is investing R6 bn. A miss raises imports | Three plants run and comply
Passengers returning to rail | 503 million journeys in 2010, 19 million in 2022, 103 million in 2025. Probably small | Recovery continues
Grid turbines and backup generation move together; so do electric vehicles and fuel prices. A matrix should not treat them as independent.
1 Status
2 Findings
3 Levers
4 Decisions

## Slide 9: Decisions for Nigel before integration and lever calibration
Each has evidence in the notes under workstreams/WS1_data_validation and WS2_model_development
Source: evidence notes on manish-branch, 6 October 2026. Changes are the analyst's position, pending review.
Strictly Confidential
Decision | Evidence in brief | Suggestion
Confirm the five applied changes | Slide 3; flag log | Accept
2024 diesel imports and how to report the diesel gap | Customs 10.793 bn litres; four routes to 3-4 bn | Use 10.79; report the gap as a finding
Power diesel factor | 0.31 litres per kWh in three years against 0.244 | Adopt 0.31
Marine baseline | 2.2 bn litres equals the department's 2007 figure; trade press now about 1 bn | Hold until an official figure
Elasticities and road parameters | One study for diesel as a whole; 2018 paper for vehicles | Keep 1.0 for industry; review the vehicle mapping
Provincial 2023-24 in the pack; 2014 and 2018 treatment | Estimate and back-test; original cells | Petrol only, labelled; national stands
Implied petrol output after 2021; 2019-20 balances for trade | Balance note | Petrol only; stop using them
Remaining originals; register layout | 16 datasets held locally | Nigel's call
1 Status
2 Findings
3 Levers
4 Decisions

## Slide 10: Presentation palette | colours and HEX codes
Reference | colours used in this presentation
Core presentation colours
Vopak blue
#0A2373
Secondary blue
#546CA2
Text / ink
#000000
White
#FFFFFF
Unassessed / neutral
#EEEEEE
Header divider
#A0A0A0
Body divider
#B8B8B8
Frame divider
#B0B0B0
Sales-map colours | provincial totals, bn litres/year
Below 1
#E3EBF6
1 to below 2
#BACCE4
2 to below 4
#809CC7
4 to below 6
#3D619D
6 and above
#0A2373
Map background
#F5F8FB
Other template theme colours
Theme dark 2
#11151A
Theme light 2
#E7E6E6
Accent 3
#BDBEC1
Accent 4
#404040
Accent 5
#767676
Accent 6
#D9D9D9
Typeface: Lato. Sales colours show totals, not density or market share. Grey denotes unassessed demand.
Source: supplied Vopak template; pptx/brand_configs/vopak.py; provincial_demand_map.py.
Strictly Confidential
Notes: Reference appendix. Colour values are read from the theme and map palette; no evidence or model assumptions changed.