## Slide 1
Liquid fuels
demand and supply
model
Week 1 analytical pack
South Africa | Petrol and diesel
6 October 2026
Internal working discussion
Photo source: Royal Vopak | Terminal Durban | vopak.com
Notes: Speaker note: Walk through four sections: the project question, the analytical
requirements, the model-build problem and the delivery approach. The purpose is to
connect the analyst's tasks to the decisions the engagement needs to support.
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.

## Slide 2: Resolve the SA fuel outlook, then test Vopak’s accessible market
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: Partner SA storyboard pp.30-32; repository evidence and diagnostics, 6 Oct 2026. All gaps remain open.
Situation → Complication → Resolution | evidence, actions and delivery roadmap
SCR reference | Evidence and required next step | Proposed lead | Timing and output | Deep dives
S1 Situation | Demand baseline and regional market Have: provincial sales history and map. Reconcile six flagged years; refresh a complete year. | Manish Nigel review | W1–W2 Sourced demand baseline | 3 / 4
S2 Situation | Domestic supply, finished imports and entry ports Have: 2024 sales/trade; diesel imports conflict. Gap: matched output/stocks and product-specific port allocation. | Manish Nigel access | W1–W3 Fuel balance + port bridge | 5 / 6
C1 Complication | Demand drivers and levers Have: indexed passenger/freight stocks, agriculture/industry, power and road/rail. Source ICE splits and intensities; calibrate litres effects. | Manish Nigel review | W1 define; W2–W4 test Lever-to-demand bridge | 7
C2 Complication | Refinery and plant scenarios Have: published capacity history and conditional CEF case. Agree timing/yields; resolve repeated keys and plant mechanisms. | Manish Henry / Nigel | W1–W3 Plant output + imports | 8
C3 Complication | Economic accessibility and competing routes Cost map is illustrative. Compare Durban–NMPP–Lesedi, road/rail, Matola and Walvis Bay for the same product and destination. | Manish Nigel / Henry | W1 scope; W2–W4 test Delivered R/litre + access | 9 / 10
R1 Resolution | Actual Vopak share and contestable customer demand Share is unknown. Test each candidate increment against cost, physical capacity, commercial rights and unique deliveries. | Nigel client data Manish analysis | W1 request; W2–W4 test Served + contestable litres | 11 / 12 / 13
R2 Resolution | Storage and optional investment Partial published stocks are available. Verify usable product capacity; size additional service needs only after the incremental flow case. | Nigel priority Manish / Henry | W4–W6 if prioritised Flow-to-stock / investment | 14 / 15
Petrol + diesel; jet separate. Owners and weeks are proposed. Open gaps and illustrations remain explicitly labelled.
Notes: Partner storyboard pp30-32 supplied in chat and preserved under external/partner_story_20261006/. Partner propositions are hypotheses, not assertions that reversals or refinery projects have occurred. All gap records are open pending the stated evidence and review. Work windows/owners are planning targets. Fuel-model integration takes precedence over broad infrastructure or detailed service sizing. Jet remains separately tracked and excluded from client petrol/diesel totals. Detailed analyst review: workstreams/WS3_reporting_delivery/partner_story_alignment_2026-10-06.md.
{
"date": "2026-10-06",
"scope": "SA petrol/diesel; jet separate",
"status": "Review roadmap; not approval or forecast",
"partner_source": "external/partner_story_20261006 (received pp30-32 screenshots)",
"planning": "Week windows and analyst assignments proposed, not confirmed commitments",
"rows": [
{
"id": "SA01",
"story": "Situation",
"question": "SA demand history and regional market size",
"existing_work": "Pack pp2-3,7: quarterly provincial sales 2013-2022; national series 2005-2023; 2023 incomplete.",
"gap": "Later complete year; six provincial/national annual differences; historical driver contributions not quantified.",
"action": "Review 2013/14/15/17/18/21 against original workbooks; source later full years. Preserve 2022 historical label.",
"closure_evidence": "Old value, proposed value, source cell and reason for each correction; all province/product quarters; national tie.",
"owner": "Manish; Nigel review",
"timing": "W1 investigate; W2 reconcile",
"source_lead": "fuel_sales_department_by_province_quarterly.csv; fuel_sales_department.csv; DMPR index",
"refresh_method": "Manual workbook download and parser rerun; completeness and revisions checked.",
"model_connection": "pptx/scripts/provincial_demand_map.py::sales; reporting evidence, not approved model calibration.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA02",
"story": "Situation",
"question": "Economically reachable eastern/inland market",
"existing_work": "Working province groups p2; illustrative road-cost map p5; storage footprint.",
"gap": "Actual customer destinations, cost threshold, route capacity and commercial rights.",
"action": "Use delivered transport cost R/litre for actual destinations; qualify physical reach and customer access separately.",
"closure_evidence": "Reachable and commercially accessible volume by product/destination/year; sourced costs and explicit unassessed residual.",
"owner": "Manish route evidence; Nigel client access",
"timing": "W1 define contract; W2-W4 integrate",
"source_lead": "Regional membership CSV; client destinations; route tariffs and quotations",
"refresh_method": "Manual client/route evidence; refresh tariff, access or destination changes.",
"model_connection": "Illustrative accessibility module is presentation only; no operational routing engine.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA03",
"story": "Situation",
"question": "Domestic production versus finished imports",
"existing_work": "Pack page 5: 2024 FIASA sales and government imports/exports collected; explicit diesel-import disagreement. Latest staged domestic production remains 2021.",
"gap": "Matched recent demand, output, imports, exports and stocks; actual provincial origin unavailable.",
"action": "Reconcile national petrol/diesel first; retain provincial origin as unknown without evidence; separate crude and finished products.",
"closure_evidence": "Production + imports - exports - stock build = consumption by fuel/year; unit/coverage bridge and residual explained.",
"owner": "Manish; Nigel review",
"timing": "W1 mapping; W2 historical balance",
"source_lead": "energy_balance_department.csv; DMPR commodity flow; SARS trade data",
"refresh_method": "Manual annual energy workbook and monthly customs download; preserve revisions.",
"model_connection": "src/lfm/model/supply/flows.py::compute_balance currently demand less supply; exports/stocks not explicit.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA04",
"story": "Situation",
"question": "Import entry ports and origin",
"existing_work": "Pack page 5: national trade collected; TNPA liquid bulk is broader than petrol/diesel. Product-specific port allocation remains open.",
"gap": "Product-specific finished imports by port/year and source country; liquid bulk is not all fuel.",
"action": "Bridge SARS product/quantity data to TNPA port cargo; check port identifier availability and density conversion.",
"closure_evidence": "National finished imports tied to evidenced port allocations; unallocated remainder explicit.",
"owner": "Manish; Nigel source access",
"timing": "W2-W3",
"source_lead": "https://tools.sars.gov.za/tradestatsportal/data_download.aspx ; https://www.transnetnationalportsauthority.net/Commercial%20and%20Marketing/Pages/Port-Statistics.aspx",
"refresh_method": "Manual portal downloads; check HS coverage, revisions, tonnes/litres and crude/nonfuel exclusions.",
"model_connection": "No imported-volume allocation by port/destination in current engine.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA05",
"story": "Situation / Complication",
"question": "Power-generation diesel and potential reversal",
"existing_work": "Eskom OCGT observations 2022-2026 staged; engine capacity/load factor/efficiency path.",
"gap": "Eskom/IPP coverage, fiscal/calendar alignment, fuel conversion and forecast dispatch. No loadshedding does not mean no OCGT diesel.",
"action": "Reconcile generation and fuel burn by plant set; calibrate dispatch alternatives; avoid additive double-counting.",
"closure_evidence": "Historical GWh-to-litres tie; baseline/alternative dispatch, units, dates and incremental demand effect.",
"owner": "Manish; Nigel review",
"timing": "W1 lever; W2-W3 calibration",
"source_lead": "ocgt_generation_eskom.csv; generation.yaml; primary Eskom operating reports",
"refresh_method": "Manual quarterly/annual operating reports; scope and period checks.",
"model_connection": "src/lfm/model/demand/generation.py::compute_country_annual.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA06",
"story": "Situation / Complication",
"question": "Road-to-rail freight shift",
"existing_work": "Road vehicle cohort calculation and schematic rail context; no mode-shift source series found in current vintage.",
"gap": "Road/rail freight, tonne-km, distance, payload, empty running and feasible rail intervention.",
"action": "Use Stats SA P7162 and operator traffic evidence; distinguish tonnes/revenue/tonne-km; convert displaced truck work into diesel.",
"closure_evidence": "Specific intervention with baseline/alternative mode shares, dates and diesel-intensity bridge; no duplicate mileage reduction.",
"owner": "Manish; Nigel intervention; Henry review",
"timing": "W1 lever definition; W2-W4 integration",
"source_lead": "https://www.statssa.gov.za/?PPN=P7162&SCH=74110&page_id=1854 ; Transnet freight traffic/access evidence",
"refresh_method": "Manual monthly survey and annual operator reports; coverage/revision checks.",
"model_connection": "vehicles.py has no explicit rail-shift lever.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA07",
"story": "Situation / Complication",
"question": "BEV, hybrid, efficiency and charging effects",
"existing_work": "Naamsa NEV sales 2019-2025 staged; engine EV curve and efficiency parameters.",
"gap": "Sales versus stock, segment scope, BEV/HEV distinction, survival, mileage and charging intervention.",
"action": "Calibrate uptake and fleet turnover; retain hybrids as fuel users with separate efficiency; define charging policy/investment lever.",
"closure_evidence": "Opening-fleet/cohort tie; drivetrain-specific L/100km; dated uptake alternatives and litres effect.",
"owner": "Manish; Nigel review",
"timing": "W1 levers; W2-W3 calibration",
"source_lead": "nev_sales_naamsa.csv; vehicles.yaml; official registration evidence",
"refresh_method": "Manual quarterly/annual data; reconcile drivetrain taxonomy and scope.",
"model_connection": "src/lfm/model/demand/vehicles.py::compute_country_annual and _ev_penetration.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA08",
"story": "Situation / Complication",
"question": "GDP, fuel prices and kilometres travelled",
"existing_work": "Macro sources staged; price series 2011-2024-04; engine GDP/capita new-sales relationship.",
"gap": "Real-price basis, causal activity effect, elasticities and actual/forecast extension.",
"action": "Map GDP source into provider with population/base-price rules; propose price-to-km response separately from efficiency.",
"closure_evidence": "Explicit historical/forecast boundary and consuming function; calibrated sensitivity without duplicate activity reductions.",
"owner": "Manish; Nigel review",
"timing": "W1 mapping; W2-W3 validation",
"source_lead": "macro_statssa.csv; macro_worldbank.csv; gdp_growth_treasury.csv; fuel_prices_department.csv",
"refresh_method": "Stats SA/Treasury/DMPR manual downloads; World Bank API; independent vintage and freshness checks.",
"model_connection": "vehicles.py GDP new-sales path; no explicit fuel-price-to-mileage response.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA09",
"story": "Situation / Complication",
"question": "Refinery closures, availability and SAPREF proposal",
"existing_work": "Pack page 8: published 2016\u20132025 capacity footprint plus conditional CEF 400k bpd case. Existing refinery keys/output/yields remain unresolved.",
"gap": "Current output/yields/status; dated closures/restarts; SAPREF project evidence; 558 extra refinery rows unresolved.",
"action": "Resolve repeated keys against original named ranges; build refinery-year status and output; treat proposals as conditional scenarios.",
"closure_evidence": "Unique country/year/scenario keys with source cells; actual/proposed distinction; per-refinery output tie and import sensitivity.",
"owner": "Manish; Nigel review; Henry challenge",
"timing": "W1 duplicates; W2-W3 scenarios",
"source_lead": "supply.yaml; refinery_production.csv; original workbook; primary operator/CEF/PetroSA reports",
"refresh_method": "Manual reports; refresh outages, restart, ownership or sanctioned-project changes.",
"model_connection": "src/lfm/model/supply/flows.py::compute_supply.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA10",
"story": "Complication",
"question": "Secunda gas/MRG and Natref future",
"existing_work": "Generic Sasol/Natref capacities, yields and utilisation; no plant-level gas-liquid linkage.",
"gap": "MRG timing and causal liquid-fuel effect; Natref future not established; partner propositions untested.",
"action": "Check latest primary Sasol disclosures; technical reviewer specifies mechanism before any fuel-output change.",
"closure_evidence": "Documented plant-level mechanism and dated scenario; no gas-to-liquid displacement inferred without evidence.",
"owner": "Manish sources; Henry technical review; Nigel scenarios",
"timing": "W2-W3",
"source_lead": "https://www.sasol.com/sasol-suite-reports ; 2026 Sasol SEC 20-F",
"refresh_method": "Manual quarterly/annual operating guidance and plant/gas changes.",
"model_connection": "No gas-to-fuel mechanism; utilisation/yield changes need explicit sourced scenario.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA11",
"story": "Complication",
"question": "Durban-NMPP-Lesedi versus road/rail, Matola and Walvis Bay",
"existing_work": "Pack page 10: schematic Southern Africa corridor map; page 9 illustrative road-cost surface. No matched full delivered-cost or fuel-access allocation.",
"gap": "Comparable route costs, NMPP capacity/tariff, actual rail service and cross-border feasibility.",
"action": "Choose first product/customer destination; compare full handling/transport/transfer cost, border/FX where relevant, same period and basis.",
"closure_evidence": "Comparable delivered R/litre with cost components, capacity/access limits and dated sources; no national optimisation claim.",
"owner": "Manish evidence; Nigel corridor choice; Henry review",
"timing": "W1 comparison contract; W2-W4 first route",
"source_lead": "Client tariffs/quotes; current pipeline, port, road/rail and border operator evidence",
"refresh_method": "Manual published tariffs and dated quotes; tariff-year, FX and access refresh.",
"model_connection": "No operational route allocation or delivered-cost engine.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA12",
"story": "Resolution",
"question": "Vopak market share at Durban and Lesedi",
"existing_work": "Pack page 13: illustrative 3.0 / 4.5 / 8.5 bn L milestones and required conditions; sourced regional sales page 12. Actual client flows and share remain unknown.",
"gap": "Unique customer deliveries, receipts, shared transfers, destinations and matched period.",
"action": "Nigel requests client flow extract; Manish reconciles receipt/transfer/final-delivery records and counts final demand once.",
"closure_evidence": "Separate terminal throughput and unique served-demand shares; matched-year/product denominator; traceable records, no capacity-as-share.",
"owner": "Nigel client request; Manish reconciliation",
"timing": "W1 request/schema; W2+ on receipt",
"source_lead": "Vopak operational/customer data; public unique-throughput data not established",
"refresh_method": "Client-approved monthly/annual extract with product/destination coverage and transfer IDs.",
"model_connection": "Current p6 flow volumes illustrative; future shared flow contract.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA13",
"story": "Resolution",
"question": "Additional commercially contestable market",
"existing_work": "Pack page 13: delivered-cost, physical-capacity, customer-rights and volume-accounting gates. All candidate increments remain unassessed.",
"gap": "Usable product-compatible tanks, spare routes, contracts, switching, customer overlap and Northern Cape inventory.",
"action": "Combine customer destinations with evidenced routes and rights; separate physical reach, commercial envelope and potential capture.",
"closure_evidence": "Accessible demand by product/region/period; explicit assumptions and unassessed residual; competitors volume is not automatically capturable.",
"owner": "Manish evidence; Nigel commercial review",
"timing": "W2-W4",
"source_lead": "Storage/competitor CSVs; NERSA licences; client contracts and operator notices",
"refresh_method": "Manual licences/notices; refresh contractual period, site changes and lease milestones.",
"model_connection": "No validated commercial customer-flow allocation.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA14",
"story": "Resolution",
"question": "New storage and investment scope",
"existing_work": "Partial gross/lease stocks, without client handling/inventory profile.",
"gap": "Incremental accessible flows, turnover/peak inventory, product compatibility, cost and commercial return criteria.",
"action": "Establish flow/access case first; then test service requirements and a separately scoped investment case.",
"closure_evidence": "Throughput-to-usable-stock bridge with seasonality, inventory days and dispatch limits; downside sensitivity; no investment claim from import deficit alone.",
"owner": "Nigel commercial gate; Manish; Henry review",
"timing": "W4-W6 only if prioritised",
"source_lead": "Client service/stock profiles and scoped cost evidence",
"refresh_method": "Manual client data; refresh on demand/access case changes.",
"model_connection": "Detailed service sizing deferred; infrastructure secondary to fuel integration.",
"priority": "P2",
"status": "Open; existing evidence does not establish closure"
}
]
}
SCR delivery order: page 2 of 16. Gap IDs and original evidence references retained in notes.
Master SCR rows: [('S1\nSituation', 'Demand baseline and regional market\nHave: provincial sales history and map. Reconcile six flagged years; refresh a complete year.', 'Manish\nNigel review', 'W1–W2\nSourced demand baseline', [3, 4]), ('S2\nSituation', 'Domestic supply, finished imports and entry ports\nHave: 2024 sales/trade; diesel imports conflict. Gap: matched output/stocks and product-specific port allocation.', 'Manish\nNigel access', 'W1–W3\nFuel balance + port bridge', [5, 6]), ('C1\nComplication', 'Demand drivers and levers\nHave: indexed passenger/freight stocks, agriculture/industry, power and road/rail. Source ICE splits and intensities; calibrate litres effects.', 'Manish\nNigel review', 'W1 define; W2–W4 test\nLever-to-demand bridge', [7]), ('C2\nComplication', 'Refinery and plant scenarios\nHave: published capacity history and conditional CEF case. Agree timing/yields; resolve repeated keys and plant mechanisms.', 'Manish\nHenry / Nigel', 'W1–W3\nPlant output + imports', [8]), ('C3\nComplication', 'Economic accessibility and competing routes\nCost map is illustrative. Compare Durban–NMPP–Lesedi, road/rail, Matola and Walvis Bay for the same product and destination.', 'Manish\nNigel / Henry', 'W1 scope; W2–W4 test\nDelivered R/litre + access', [9, 10]), ('R1\nResolution', 'Actual Vopak share and contestable customer demand\nShare is unknown. Test each candidate increment against cost, physical capacity, commercial rights and unique deliveries.', 'Nigel client data\nManish analysis', 'W1 request; W2–W4 test\nServed + contestable litres', [11, 12, 13]), ('R2\nResolution', 'Storage and optional investment\nPartial published stocks are available. Verify usable product capacity; size additional service needs only after the incremental flow case.', 'Nigel priority\nManish / Henry', 'W4–W6 if prioritised\nFlow-to-stock / investment', [14, 15])]
Slide links connect each roadmap row to its deep dives; the overview chevron provides the return link. No visible SCR breadcrumb.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 3: Locate fuel demand alongside the infrastructure serving it
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: DMPR 2022 sales; geoBoundaries/OCHA/MDB 2020 provinces (CC BY 3.0 IGO); operator sources on slide 12.
Petrol + diesel sales by province | 2022, bn litres/year
N
0
500 km
Durban
Vopak / Bidvest
Richards Bay
Bidvest
Cape Town
Burgan Cape
Lesedi / inland storage
Vopak / Bidvest
Sasol / Transnet
1
2
3
4
5
Transnet lease offers
1 Ladysmith | 2 Standerton
3 Kroonstad | 4 Bethlehem
5 Magdala*
EC
1.74
FS
1.37
GP
6.81
KZN
4.28
LP
0.50
MP
1.76
NW
1.07
NC
0.45
WC
3.93
<1
1-2
2-4
4-6
6+
bn L/year; darker = more sales
Production
Port
Vopak
Other storage
Lines: road / pipe / rail; heavy outlines: working regions
Lease offers are not operating capacity. *Magdala RFP location narrative conflicts; briefing coordinate used. Jet excluded.
Evidence and implications
01 | Demand is concentrated
Gauteng, KwaZulu-Natal and Western Cape account for 68.6% of reported 2022 petrol/diesel sales.
02 | Regions are working groups
Province boundaries define reporting groups; they do not establish terminal catchments.
03 | Sales are historical demand evidence
The map is sourced provincial sales, rather than a current-year outlook or commercial accessibility result.
Next steps | proposed owners
Manish: source a later complete year and test actual destinations, route costs and customer access.
Notes: Observed historical sales, separate from the illustrative market figures on slide 6.
Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
Historical sales are a demand-location proxy, not 2026 demand or customer delivery destinations. All 18 province/product series have four quarters in 2022; provincial sum matches national sales within 1 litre. No district-level smoothing or within-province hotspot is inferred. Colour measures total annual provincial volume, not litres per km2. Region borders use the authored province membership, not a service area. Eastern coastal=EC+KZN; Inland=GP+FS+LP+MP+NW; Western coastal=WC; Other=NC. The observed totals and regions are separate from the illustrative market figures on slide 6. Source CSV C:\Users\ITafr\Desktop\Insights\liquid_fuels_model\assumptions\2026\timeseries\fuel_sales_department_by_province_quarterly.csv; SHA256 aec82481b33f70429b6b8e7c9c02767d62a6e8c7bf6bda09e21123a5bc56c9d6; original workbook(s) ['2022-Quarter4-Magisterial-Districts-data.xlsx']. Department index: https://www.dmpr.gov.za/Portals/0/Energy_Website/files/media/media_SAVolumes.html. Boundary metadata/source/license: assets/maps/geoboundaries_zaf_adm1_metadata.json. Reporting evidence remains provisional pending analyst review; owner Manish, Nigel review. Refresh when the source supplies a later complete year; check every province/product quarter and reconcile national totals.
SCR delivery order: page 3 of 16. Gap IDs and original evidence references retained in notes.
SCR master row S1; linked roadmap page 2. Deep-dive page 3.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 4: Track petrol and diesel sales by province over time
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: DMPR quarterly provincial sales extract; complete calendar years only. Petrol + diesel; jet excluded.
Annual provincial sales | 2013–2022, bn litres/year
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Gauteng | 6.9574 | 7.0981 | 7.2798 | 7.1303 | 7.2139 | 7.3171 | 7.6415 | 6.0857 | 6.646 | 6.8094
KwaZulu-Natal | 4.065 | 3.8521 | 3.9126 | 3.9426 | 4.1854 | 4.0067 | 4.2545 | 4.0587 | 4.2743 | 4.2845
Western Cape | 3.7114 | 4.0928 | 4.6965 | 3.7212 | 3.6273 | 3.5434 | 3.7198 | 3.1569 | 4.0101 | 3.9308
Mpumalanga | 2.3205 | 2.3412 | 2.4544 | 2.6606 | 2.5088 | 2.4566 | 2.2367 | 1.9979 | 1.9372 | 1.7572
Eastern Cape | 1.5859 | 1.6267 | 1.7991 | 1.7859 | 1.769 | 1.7703 | 1.7921 | 1.6156 | 1.7712 | 1.7355
Free State | 2.2595 | 2.1859 | 2.1803 | 1.9397 | 1.7441 | 1.9779 | 1.8837 | 1.7547 | 1.7203 | 1.3693
North West | 1.2664 | 1.1583 | 1.1888 | 1.1649 | 1.1013 | 0.99173 | 1.0073 | 0.84795 | 0.94562 | 1.0681
Limpopo | 0.82767 | 0.79082 | 0.78174 | 0.66642 | 0.63051 | 0.66217 | 0.61976 | 0.49264 | 0.48667 | 0.49563
Northern Cape | 0.58731 | 0.62826 | 0.66862 | 0.53308 | 0.53862 | 0.52173 | 0.52641 | 0.44129 | 0.45501 | 0.45181
Gauteng
KwaZulu-Natal
Western Cape
Mpumalanga
Eastern Cape
Free State
North West
Limpopo
Northern Cape
Evidence and implications
01 | History ends in 2022
The latest complete provincial year in this extract is 2022.
02 | 2023 is incomplete
Only Q1 is present; it is excluded from annual comparisons.
03 | Six years are flagged
Provincial sums differ from national sales in 2013, 2014, 2015, 2017, 2018 and 2021.
Next steps | proposed owners
Manish: reconcile each flagged value to its original workbook cell and log old value, proposed value and reason.
Notes: Annual reporting sums four quarters separately for each province/product. Missing or incomplete years are gaps, never zeros or extrapolations. 2023 has Q1 only and is excluded. Source: assumptions/2026/timeseries/fuel_sales_department_by_province_quarterly.csv. Reported sales are a demand proxy; historical reporting requires analyst review, not a forecast.
Provincial sum minus national petrol/diesel sales (bn L), mechanical flag tolerance 1 litre, not a materiality or validation threshold:
{
"2013": 0.5379449579999971,
"2014": 0.2688237130000033,
"2015": -0.034042841268004054,
"2016": -7.105427357601002e-15,
"2017": -0.0023669540000135214,
"2018": -0.4327551978270243,
"2019": -1.7763568394002505e-14,
"2020": -1.0658141036401503e-14,
"2021": -0.0007647352630151261,
"2022": -1.7763568394002505e-14
}
SCR delivery order: page 4 of 16. Gap IDs and original evidence references retained in notes.
SCR master row S1; linked roadmap page 2. Deep-dive page 4.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 5: Collect the national fuel balance and expose source disagreements
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: Government Energy Trade Report 2024, printed pp.12–13; FIASA 2025, pp.47–49; energy balance 2021. Rounded trade figures.
National petrol/diesel | 2024, billion litres
COLLECTED | trade and sales; production/stock reconciliation remains open
Product | Reported sales | Imports | Exports | Net imports
Petrol | 9.029 | 4.000 | 0.920 | 3.080
Diesel | 11.734 | 10.800 | 0.790 | 10.010
Combined | 20.763 | 14.800 | 1.710 | 13.090
Source flag | 2024 diesel imports
FIASA staged: 14.793 | Government report: 10.800
Difference: -3.993 bn L. Preserve both; investigate scope and vintage.
Domestic production remains a dated observation
Latest staged balance: 2021 petrol 6.35; diesel 5.31 bn L.
Do not combine 2021 output with 2024 sales/trade to close a balance.
Evidence and implications
01 | Public figures are collectable
2024 petrol/diesel imports total 14.8 bn L in the government report. Exports total 1.71 bn L; these are rounded reported figures.
02 | The sources disagree
FIASA reports 14.793 bn L of diesel imports for 2024 versus 10.8 bn L in the government report. Neither value has been silently replaced.
03 | Port cargo has wider coverage
TNPA publishes liquid-bulk cargo by port, but it includes crude and other liquids. It does not establish petrol/diesel import allocation.
Next steps | proposed owners
Manish: reconcile raw SARS product codes and units, then source matched-year production and stocks. Nigel: confirm access to product-specific port data.
Notes: [
{
"id": "SA03",
"story": "Situation",
"question": "Domestic production versus finished imports",
"existing_work": "Pack page 5: 2024 FIASA sales and government imports/exports collected; explicit diesel-import disagreement. Latest staged domestic production remains 2021.",
"gap": "Matched recent demand, output, imports, exports and stocks; actual provincial origin unavailable.",
"action": "Reconcile national petrol/diesel first; retain provincial origin as unknown without evidence; separate crude and finished products.",
"closure_evidence": "Production + imports - exports - stock build = consumption by fuel/year; unit/coverage bridge and residual explained.",
"owner": "Manish; Nigel review",
"timing": "W1 mapping; W2 historical balance",
"source_lead": "energy_balance_department.csv; DMPR commodity flow; SARS trade data",
"refresh_method": "Manual annual energy workbook and monthly customs download; preserve revisions.",
"model_connection": "src/lfm/model/supply/flows.py::compute_balance currently demand less supply; exports/stocks not explicit.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA04",
"story": "Situation",
"question": "Import entry ports and origin",
"existing_work": "Pack page 5: national trade collected; TNPA liquid bulk is broader than petrol/diesel. Product-specific port allocation remains open.",
"gap": "Product-specific finished imports by port/year and source country; liquid bulk is not all fuel.",
"action": "Bridge SARS product/quantity data to TNPA port cargo; check port identifier availability and density conversion.",
"closure_evidence": "National finished imports tied to evidenced port allocations; unallocated remainder explicit.",
"owner": "Manish; Nigel source access",
"timing": "W2-W3",
"source_lead": "https://tools.sars.gov.za/tradestatsportal/data_download.aspx ; https://www.transnetnationalportsauthority.net/Commercial%20and%20Marketing/Pages/Port-Statistics.aspx",
"refresh_method": "Manual portal downloads; check HS coverage, revisions, tonnes/litres and crude/nonfuel exclusions.",
"model_connection": "No imported-volume allocation by port/destination in current engine.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 5 of 16. Gap IDs and original evidence references retained in notes.
{
"retrieved": "2026-10-06",
"status": "staged reporting evidence; unreviewed; not consumed by engine",
"sources": [
{
"file": "trade2024.pdf",
"url": "https://www.dmpr.gov.za/Portals/0/Resources/Publications/Reports/Energy%20Sector%20Reports/SA%20Energy%20Trade%20Report/2024-South-African-Energy-Trade-Report.pdf",
"status": 200,
"sha256": "ad2c612c95e5ff3db7ce8b8280b1d30ac7ce13173f7c95a5e1ded3025c2d157d",
"retrieved": "2026-10-06",
"bytes": 1737491
},
{
"file": "trade2025_preliminary.pdf",
"url": "https://www.dmpr.gov.za/Portals/0/Resources/Publications/Reports/Energy%20Sector%20Reports/SA%20Energy%20Trade%20Report/2025-South-African-Energy-Preliminary-Trade-Report.pdf",
"error": "HTTP Error 404: Not Found",
"retrieved": "2026-10-06"
},
{
"file": "sector2025_preliminary.pdf",
"url": "https://www.dmpr.gov.za/Portals/0/Resources/Publications/Reports/Energy%20Sector%20Reports/SA%20Energy%20Sector%20Report/2025-South-African-Energy-Sector-Preliminary-Report.pdf",
"error": "HTTP Error 404: Not Found",
"retrieved": "2026-10-06"
},
{
"file": "tnpa_mar2025.pdf",
"url": "https://www.transnetnationalportsauthority.net/Commercial%20and%20Marketing/Port%20Cargo%20Statistics/Cargo%20-%20MAR%202025.pdf",
"error": "<urlopen error [WinError 10060] A connection attempt failed because the connected party did not properly respond after a period of time, or established connection failed because connected host has failed to respond>",
"retrieved": "2026-10-06"
},
{
"file": "energy_balance_index.html",
"url": "https://www.dmpr.gov.za/Portals/0/Energy_Website/files/media/Energy_Balances.html",
"status": 200,
"sha256": "0ac165e3575eb6b1b9540f4cbdd27462455608eff07f8520ac72ab765de65e12",
"retrieved": "2026-10-06",
"bytes": 23560
},
{
"file": "cef_refinery_update.html",
"url": "https://cefgroup.co.za/2026/09/23/cef-group-presents-five-year-financial-performance-governance-outcomes-and-sanpc-development-progress-to-parliament/",
"status": 200,
"sha256": "7c7804cd3d80dddb666da1507106aa2b6dcf48316dbf3ee9244a32a34be475d5",
"retrieved": "2026-10-06",
"bytes": 236086
},
{
"file": "trade2025_preliminary.pdf",
"url": "https://www.dmre.gov.za/Portals/0/Resources/Publications/Reports/Energy%20Sector%20Reports/SA%20Energy%20Trade%20Report/2025-South-African-Energy-Preliminary-Trade-Report.pdf?ver=2mpclUkL_LUiTkST4yWRNw%3D%3D",
"error": "<urlopen error [WinError 10060] A connection attempt failed because the connected party did not properly respond after a period of time, or established connection failed because connected host has failed to respond>",
"retrieved": "2026-10-06"
},
{
"file": "sector2025_preliminary.pdf",
"url": "https://www.dmre.gov.za/Portals/0/Resources/Publications/Reports/Energy%20Sector%20Reports/SA%20Energy%20Sector%20Report/2025-South-African-Energy-Sector-Preliminary-Report.pdf?ver=vj8mIFbD608QxnJWxaV2xw%3D%3D",
"error": "<urlopen error [WinError 10060] A connection attempt failed because the connected party did not properly respond after a period of time, or established connection failed because connected host has failed to respond>",
"retrieved": "2026-10-06"
}
],
"capacity_source": {
"file": "annual-report-2025.pdf",
"pdf_page": 49,
"index": "https://fuelsindustry.org.za/publications/annual-reports/",
"sha256": "a37e04143fd3e2eb672cd79d16c26e8b7a027171172b38d689949e6b0b502ef7"
},
"refresh": "Download the next government trade report and FIASA annual report; rerun this extractor. Source changes require deliberate register reconciliation.",
"limitations": [
"Trade values are rounded narrative figures.",
"Capacity table includes crude-equivalent synthetic plants and idle nameplate capacity; not actual production or usable annual capacity.",
"2024 source disagreement is retained; no adoption decision or validation inferred.",
"Official balance index ends at 2021; no recent complete production/export/stock reconciliation established.",
"2025 preliminary reports and TNPA raw PDF downloads failed in this collection; see manifest."
]
}
Trade source flag: [['Product', 'Reported\nsales', 'Imports', 'Exports', 'Net imports'], ['Petrol', '9.029', '4.000', '0.920', '3.080'], ['Diesel', '11.734', '10.800', '0.790', '10.010'], ['Combined', '20.763', '14.800', '1.710', '13.090']]
SCR master row S2; linked roadmap page 2. Deep-dive page 5.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 6: Shape the provincial split between domestic fuel and imports
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: DMPR 2022 provincial sales totals; source mix from the existing illustrative national-balance CSV. Not observed origin.
2022 sales totals | ILLUSTRATIVE domestic/import allocation
0
2
4
6
8
Gauteng
6.81
KwaZulu-Natal
4.28
Western Cape
3.93
Mpumalanga
1.76
Eastern Cape
1.74
Free State
1.37
North West
1.07
Limpopo
0.50
Northern Cape
0.45
Illustrative domestic fuel
Illustrative finished-product imports
Units: bn litres/year. Imported/domestic segments are a scenario illustration, not measured provincial flows.
Evidence and implications
01 | Demand totals are sourced
The provincial bars use reported 2022 petrol/diesel sales.
02 | Origin shares are illustrative
Domestic/import fractions are authored examples; no actual provincial origin allocation is established.
03 | Imports need a national balance
Exports and stock movements must be reconciled before a sourced import requirement can be presented.
Next steps | proposed owners
Manish: populate the matched-year national balance first; retain provincial origin as unknown until supported.
Notes: {
"status": "Illustrative allocation only; not observed provincial supply",
"demand_year": 2022,
"demand_source": "assumptions/2026/timeseries/fuel_sales_department_by_province_quarterly.csv",
"mix_source": "pptx/story/illustrative_national_balance.csv",
"method": "Apply the example domestic_supply/demand share separately for petrol and diesel to each province's reported sales; remaining volume is illustrative finished-product imports",
"geographic_assumption": "Uniform source shares by product across provinces; provincial product mix may differ",
"scope": "Finished petrol and diesel; domestically refined output counts as domestic even when crude is imported",
"owner": "Manish / Nigel review",
"replacement_trigger": "Matched-year reviewed national balance plus evidenced refinery/import-to-province flows, exports and stock reconciliation"
}
No provincial origin dataset was found in the reviewed source extract. Demand totals are reported 2022 sales; domestic/import segments are illustrative, not observed 2022 supply. The same example product-specific shares apply to every province. Imports mean finished products, not imported crude. Do not infer these flows from refinery locations or customs clearance province.
SCR delivery order: page 6 of 16. Gap IDs and original evidence references retained in notes.
SCR master row S2; linked roadmap page 2. Deep-dive page 6.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 7: Track passenger, freight and sector activity driving fuel demand
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: NaTIS Dec snapshots; Stats SA P0441 Q2 2026 / P7162 Dec 2025; Eskom integrated reports; naamsa Q2 2026. Series and scope in notes.
Demand-driver dashboard | every series indexed to 2024 = 100
Common 0–120 scale. Activity proxies; vehicle ICE split unresolved.
Passenger stock | all fuels; Dec
Chart: 
| 2021 | 2022 | 2023 | 2024 | 2025
Cars | 96.2613 | 96.6774 | 98.0487 | 100 | 102.9542
Minibuses | 98.4603 | 98.3657 | 100.027 | 100 | 100.0017
Cars
Minibuses
Freight stock | all fuels; Dec
Chart: 
| 2021 | 2022 | 2023 | 2024 | 2025
Trucks | 97.6339 | 96.8141 | 98.4461 | 100 | 101.5582
Light commercial | 98.0081 | 97.5349 | 98.6683 | 100 | 101.8584
Trucks
Light commercial
Agriculture | real value added, CY
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Agriculture / forestry / fishing | 91.2826 | 107.0375 | 112.3628 | 114.7911 | 109.5434 | 100 | 117.4273
Agriculture / forestry / fishing
Industry | real value added, CY
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Manufacturing | 106.914 | 93.9398 | 100.3353 | 99.9885 | 100.3523 | 100 | 98.8215
Mining | 108.275 | 95.0562 | 107.0738 | 99.672 | 99.5626 | 100 | 100.1653
Manufacturing
Mining
Power | OCGT generation, FY
Chart: 
| 2023 | 2024 | 2025 | 2026
Eskom + IPP | 80.0311 | 100 | 55.1818 | 20.98
Eskom + IPP
Freight activity | payload, CY
Chart: 
| 2024 | 2025
Road | 100 | 99.6601
Rail | 100 | 104.677
Road
Rail
FY ends March; CY is calendar year. Stock is December snapshot. ICE = internal combustion engine.
Evidence and implications
01 | Passenger and freight ICE need a split
NaTIS separates cars/minibuses and trucks/light commercial, but not petrol, diesel or electric. Stocks are all fuels; kilometres and efficiency remain open.
02 | Sector activity is now explicit
2025 versus 2024: agriculture +17.4%; manufacturing -1.2%. Value added is an activity proxy, not direct fuel consumption.
03 | Uptake and modal levers remain distinct
2025 sales: 1,088 BEVs; 12,818 hybrids. Rail payload +4.7%; road -0.3%. Hybrids still use fuel; payload is not tonne-km.
Next steps | proposed owners
Manish: source ICE fuel splits, vehicle-km, freight tonne-km and sector fuel intensities. Keep the freight revision flag; refresh prices (annual extract ends 2023). Nigel: agree lever alternatives.
Notes: [
{
"id": "SA05",
"story": "Situation / Complication",
"question": "Power-generation diesel and potential reversal",
"existing_work": "Eskom OCGT observations 2022-2026 staged; engine capacity/load factor/efficiency path.",
"gap": "Eskom/IPP coverage, fiscal/calendar alignment, fuel conversion and forecast dispatch. No loadshedding does not mean no OCGT diesel.",
"action": "Reconcile generation and fuel burn by plant set; calibrate dispatch alternatives; avoid additive double-counting.",
"closure_evidence": "Historical GWh-to-litres tie; baseline/alternative dispatch, units, dates and incremental demand effect.",
"owner": "Manish; Nigel review",
"timing": "W1 lever; W2-W3 calibration",
"source_lead": "ocgt_generation_eskom.csv; generation.yaml; primary Eskom operating reports",
"refresh_method": "Manual quarterly/annual operating reports; scope and period checks.",
"model_connection": "src/lfm/model/demand/generation.py::compute_country_annual.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA06",
"story": "Situation / Complication",
"question": "Road-to-rail freight shift",
"existing_work": "Road vehicle cohort calculation and schematic rail context; no mode-shift source series found in current vintage.",
"gap": "Road/rail freight, tonne-km, distance, payload, empty running and feasible rail intervention.",
"action": "Use Stats SA P7162 and operator traffic evidence; distinguish tonnes/revenue/tonne-km; convert displaced truck work into diesel.",
"closure_evidence": "Specific intervention with baseline/alternative mode shares, dates and diesel-intensity bridge; no duplicate mileage reduction.",
"owner": "Manish; Nigel intervention; Henry review",
"timing": "W1 lever definition; W2-W4 integration",
"source_lead": "https://www.statssa.gov.za/?PPN=P7162&SCH=74110&page_id=1854 ; Transnet freight traffic/access evidence",
"refresh_method": "Manual monthly survey and annual operator reports; coverage/revision checks.",
"model_connection": "vehicles.py has no explicit rail-shift lever.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA07",
"story": "Situation / Complication",
"question": "BEV, hybrid, efficiency and charging effects",
"existing_work": "Naamsa NEV sales 2019-2025 staged; engine EV curve and efficiency parameters.",
"gap": "Sales versus stock, segment scope, BEV/HEV distinction, survival, mileage and charging intervention.",
"action": "Calibrate uptake and fleet turnover; retain hybrids as fuel users with separate efficiency; define charging policy/investment lever.",
"closure_evidence": "Opening-fleet/cohort tie; drivetrain-specific L/100km; dated uptake alternatives and litres effect.",
"owner": "Manish; Nigel review",
"timing": "W1 levers; W2-W3 calibration",
"source_lead": "nev_sales_naamsa.csv; vehicles.yaml; official registration evidence",
"refresh_method": "Manual quarterly/annual data; reconcile drivetrain taxonomy and scope.",
"model_connection": "src/lfm/model/demand/vehicles.py::compute_country_annual and _ev_penetration.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA08",
"story": "Situation / Complication",
"question": "GDP, fuel prices and kilometres travelled",
"existing_work": "Macro sources staged; price series 2011-2024-04; engine GDP/capita new-sales relationship.",
"gap": "Real-price basis, causal activity effect, elasticities and actual/forecast extension.",
"action": "Map GDP source into provider with population/base-price rules; propose price-to-km response separately from efficiency.",
"closure_evidence": "Explicit historical/forecast boundary and consuming function; calibrated sensitivity without duplicate activity reductions.",
"owner": "Manish; Nigel review",
"timing": "W1 mapping; W2-W3 validation",
"source_lead": "macro_statssa.csv; macro_worldbank.csv; gdp_growth_treasury.csv; fuel_prices_department.csv",
"refresh_method": "Stats SA/Treasury/DMPR manual downloads; World Bank API; independent vintage and freshness checks.",
"model_connection": "vehicles.py GDP new-sales path; no explicit fuel-price-to-mileage response.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 7 of 16. Gap IDs and original evidence references retained in notes.
{
"base_year": 2024,
"formula": "100 * observed value / own 2024 value",
"series": [
[
"Passenger stock | all fuels; Dec",
[
[
"Cars",
{
"2021": 7652077.0,
"2022": 7685153.0,
"2023": 7794164.0,
"2024": 7949275.0,
"2025": 8184111.0
}
],
[
"Minibuses",
{
"2021": 349671.0,
"2022": 349335.0,
"2023": 355235.0,
"2024": 355139.0,
"2025": 355145.0
}
]
]
],
[
"Freight stock | all fuels; Dec",
[
[
"Trucks",
{
"2021": 389112.0,
"2022": 385845.0,
"2023": 392349.0,
"2024": 398542.0,
"2025": 404752.0
}
],
[
"Light commercial",
{
"2021": 2671314.0,
"2022": 2658416.0,
"2023": 2689310.0,
"2024": 2725606.0,
"2025": 2776258.0
}
]
]
],
[
"Agriculture | real value added, CY",
[
[
"Agriculture / forestry / fishing",
{
"2019": 104784757699.11429,
"2020": 122870099075.34619,
"2021": 128983089561.3611,
"2022": 131770642145.0265,
"2023": 125746642145.02654,
"2024": 114791642145.02654,
"2025": 134796746981.71317
}
]
]
],
[
"Industry | real value added, CY",
[
[
"Manufacturing",
{
"2019": 559321509886.0238,
"2020": 491446551169.8276,
"2021": 524904832402.9977,
"2022": 523090754064.8606,
"2023": 524993754064.86096,
"2024": 523150754064.86096,
"2025": 516985652975.0193
}
],
[
"Mining",
{
"2019": 222100060478.9847,
"2020": 194984856273.23434,
"2021": 219635997902.62903,
"2022": 204452922719.6744,
"2023": 204228699966.27374,
"2024": 205125829591.8731,
"2025": 205464886014.25735
}
]
]
],
[
"Power | OCGT generation, FY",
[
[
"Eskom + IPP",
{
"2023": 4116.0,
"2024": 5143.0,
"2025": 2838.0,
"2026": 1079.0
}
]
]
],
[
"Freight activity | payload, CY",
[
[
"Road",
{
"2024": 979798.0,
"2025": 976468.0
}
],
[
"Rail",
{
"2024": 160745.0,
"2025": 168263.0
}
]
]
]
],
"status": "descriptive evidence; not causal contributions or forecast demand",
"price": "Annual extract stops 2023; no 2024 base available. Diesel prices are wholesale, petrol retail; no real-price elasticity calibrated.",
"freight_revision": {
"retrieved": "2026-10-06",
"status": "staged reporting; no diesel displacement inferred",
"refresh": "Download next P7162 December report; rerun extractor and compare overlapping years before adoption.",
"sources": [
{
"file": "P7162December2024.pdf",
"url": "https://www.statssa.gov.za/publications/P7162/P7162December2024.pdf",
"sha256": "ba0941c72c8f84b5dfbd2799e73b053ca45b421009c03eb286dbaaa9f271d9a6"
},
{
"file": "P7162December2025.pdf",
"url": "https://www.statssa.gov.za/publications/P7162/P7162December2025.pdf",
"sha256": "d6285729813c880a13582c9cda057c8f3c4c8ce0fe5788a93c84747dd33bcf51"
}
],
"overlap_2024": [
{
"mode": "rail",
"old_value": 160993,
"new_value": 160745,
"delta": -248,
"status": "source revision; do not splice vintages"
},
{
"mode": "road",
"old_value": 790611,
"new_value": 979798,
"delta": 189187,
"status": "source revision; do not splice vintages"
}
]
},
"fleet": "BEV and conventional-hybrid new sales; PHEVs omitted from chart; stocks, survival, mileage and efficiency not inferred.",
"vehicle_stock_scope": "NaTIS all-fuel national December snapshots. Cars/minibuses do not cover buses/motorcycles; trucks/light-commercial do not establish diesel-only freight usage. No ICE mix or fuel demand is inferred.",
"sector_scope": "Real gross value added: agriculture includes forestry/fishing; industry shows manufacturing and mining separately, not all industrial fuel consumption.",
"power_change_percent": -79.02002722146607,
"uptake_observations": {
"BEV_new_sales": {
"2019": 154.0,
"2020": 92.0,
"2021": 218.0,
"2022": 502.0,
"2023": 929.0,
"2024": 1257.0,
"2025": 1088.0
},
"conventional_hybrid_new_sales": {
"2019": 181.0,
"2020": 155.0,
"2021": 627.0,
"2022": 4070.0,
"2023": 6485.0,
"2024": 13616.0,
"2025": 12818.0
}
}
}
SCR master row C1; linked roadmap page 2. Deep-dive page 7.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 8: Compare the capacity history with a conditional redevelopment case
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: FIASA Annual Report 2025, p.49; CEF statement 23 Sep 2026. Nameplate / crude-equivalent capacity; not actual fuel output.
Published footprint + illustrative scenarios | thousand bbl/day
History 2016–2025 is sourced; 2026 onward is illustrative, not a forecast
A | No new refinery capacity
Chart: 
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036
Reported footprint / held flat | 718 | 718 | 718 | 718 | 718 | 538 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358
Conditional addition | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2036: 358 thousand bbl/day
B | Conditional CEF redevelopment
Chart: 
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036
Reported footprint / held flat | 718 | 718 | 718 | 718 | 718 | 538 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358 | 358
Conditional addition | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 400 | 400 | 400 | 400
2036: 758 thousand bbl/day
B adds 400 from 2033; darker navy = existing footprint; lighter blue = conditional addition.
B assumes illustrative FID 2029 + 48 months; no sanctioned date. Both hold existing capacity flat.
Evidence and implications
01 | History shows a structural decline
Published total falls from 718 in 2016–2020 to 538 in 2021 and 358 from 2022–2025. Capacity does not measure realised output.
02 | Redevelopment is conditional
CEF proposes approximately 400 thousand bbl/day after FID. Construction is approximately 48 months; the 2029 FID here is authored for comparison.
03 | Product output still needs modelling
Source utilisation, downtime and product yields before translating capacity into domestic supply. Secunda/Natref cases remain open.
Next steps | proposed owners
Nigel: agree scenario timing. Manish: reconcile plant capacity and output/yields. Henry: review technical feasibility and the Sasol gas-to-liquids mechanism.
Notes: [
{
"id": "SA09",
"story": "Situation / Complication",
"question": "Refinery closures, availability and SAPREF proposal",
"existing_work": "Pack page 8: published 2016\u20132025 capacity footprint plus conditional CEF 400k bpd case. Existing refinery keys/output/yields remain unresolved.",
"gap": "Current output/yields/status; dated closures/restarts; SAPREF project evidence; 558 extra refinery rows unresolved.",
"action": "Resolve repeated keys against original named ranges; build refinery-year status and output; treat proposals as conditional scenarios.",
"closure_evidence": "Unique country/year/scenario keys with source cells; actual/proposed distinction; per-refinery output tie and import sensitivity.",
"owner": "Manish; Nigel review; Henry challenge",
"timing": "W1 duplicates; W2-W3 scenarios",
"source_lead": "supply.yaml; refinery_production.csv; original workbook; primary operator/CEF/PetroSA reports",
"refresh_method": "Manual reports; refresh outages, restart, ownership or sanctioned-project changes.",
"model_connection": "src/lfm/model/supply/flows.py::compute_supply.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA10",
"story": "Complication",
"question": "Secunda gas/MRG and Natref future",
"existing_work": "Generic Sasol/Natref capacities, yields and utilisation; no plant-level gas-liquid linkage.",
"gap": "MRG timing and causal liquid-fuel effect; Natref future not established; partner propositions untested.",
"action": "Check latest primary Sasol disclosures; technical reviewer specifies mechanism before any fuel-output change.",
"closure_evidence": "Documented plant-level mechanism and dated scenario; no gas-to-liquid displacement inferred without evidence.",
"owner": "Manish sources; Henry technical review; Nigel scenarios",
"timing": "W2-W3",
"source_lead": "https://www.sasol.com/sasol-suite-reports ; 2026 Sasol SEC 20-F",
"refresh_method": "Manual quarterly/annual operating guidance and plant/gas changes.",
"model_connection": "No gas-to-fuel mechanism; utilisation/yield changes need explicit sourced scenario.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 8 of 16. Gap IDs and original evidence references retained in notes.
Capacity series: {2016: 718.0, 2017: 718.0, 2018: 718.0, 2019: 718.0, 2020: 718.0, 2021: 538.0, 2022: 358.0, 2023: 358.0, 2024: 358.0, 2025: 358.0}
Illustrative assumptions: {"start_year": 2026, "horizon_year": 2036, "illustrative_fid_year": 2029, "construction_months": 48, "proposed_addition_bpd": 400000}
CEF proposal is not FID or a committed restart. FIASA Enref 135k differs from workbook/Engen 120k; no engine parameter changed.
SCR master row C2; linked roadmap page 2. Deep-dive page 8.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 9: Map conditional market access from Durban and Lesedi
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: Existing appendix routes; illustrative candidate connections, not verified catchments. Natural Earth 1:50m.
N
0
500 km
Durban
Lesedi*
≤0.75
0.75–1.25
1.25–1.75
1.75–2.25
>2.25
Unassessed
Example rate: R0.15/L dispatch + R0.002/L/km. Grey = unassessed.
Illustrative road cost only. Pipeline/rail access and commercial rights are not priced.
1
2
3
4
5
Transnet lease offers
1 Ladysmith | 2 Standerton
3 Kroonstad | 4 Bethlehem
5 Magdala*
Evidence and implications
01 | Darker cells mean lower example cost
The surface shows illustrative delivered road-transport cost in R/litre.
02 | Other modes remain context
Pipeline and rail costs, capacity and access are not evaluated in this surface.
03 | Physical proximity is insufficient
No operational or commercial catchment is validated by this illustration.
Next steps | proposed owners
Manish and Nigel: select the first destination and obtain dated route tariffs, quotations and access evidence.
Road-delivery accessibility | illustrative transport cost, R/litre
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No operational service-area polygon or evidence-calibrated cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. The graduated surface is illustrative delivered road transport cost: R0.15/litre dispatch plus R0.002/litre/km times shortest schematic-road distance and straight-line terminal/grid connections. These are authored example parameters, not carrier quotes or validated cost evidence. 25 km cells; cost classes <=0.75, 0.75-1.25, 1.25-1.75, 1.75-2.25 and >2.25 R/litre. Cells more than 100 km from the sampled road geometry or without a connected path remain unassessed. Fuel purchase price, tax, storage and pipeline tariffs are excluded. Operational speeds, capacity, permissions and commercial access are not evaluated. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson
Transnet lease offers are context only, not cost-model origins or available supply.
Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
SCR delivery order: page 9 of 16. Gap IDs and original evidence references retained in notes.
SCR master row C3; linked roadmap page 2. Deep-dive page 9.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 10: Locate alternative gateways to the same inland customers
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: WBCG Trans-Kalahari; TRAC N4/Maputo corridor; kickoff NMPP schematic; Natural Earth 1:50m. Locations approximate.
Durban, Matola and Walvis Bay | schematic corridor comparison
NAMIBIA
BOTSWANA
SOUTH AFRICA
MOZAMBIQUE
Walvis Bay
Windhoek
Gaborone
Matola / Maputo
Mbombela
Gauteng
Lesedi*
Durban
N
0
500 km
Solid: Durban / N4 candidates | Dashed: Trans-Kalahari / NMPP
LAEA / WGS84; routes schematic. No cost, available capacity, fuel rights or catchment is inferred.
Evidence and implications
01 | Compare the same inland destination
Gauteng is the common comparison market. Lesedi is a Vopak facility, not a destination every competing route must pass through.
02 | Matola approaches from the east
N4/Maputo connects Mozambique to Gauteng via Komatipoort and Mpumalanga. Fuel-compatible terminal access and road/rail service need testing.
03 | Walvis is an inland comparator
Trans-Kalahari links Walvis Bay via Namibia and Botswana to Gauteng. Its competitiveness for specific inland customers is unassessed.
Next steps | proposed owners
Nigel: select the customer destination. Manish: compare handling, transport, border/FX costs and access on the same R/litre basis; keep unevidenced routes unassessed.
Notes: [
{
"id": "SA11",
"story": "Complication",
"question": "Durban-NMPP-Lesedi versus road/rail, Matola and Walvis Bay",
"existing_work": "Pack page 10: schematic Southern Africa corridor map; page 9 illustrative road-cost surface. No matched full delivered-cost or fuel-access allocation.",
"gap": "Comparable route costs, NMPP capacity/tariff, actual rail service and cross-border feasibility.",
"action": "Choose first product/customer destination; compare full handling/transport/transfer cost, border/FX where relevant, same period and basis.",
"closure_evidence": "Comparable delivered R/litre with cost components, capacity/access limits and dated sources; no national optimisation claim.",
"owner": "Manish evidence; Nigel corridor choice; Henry review",
"timing": "W1 comparison contract; W2-W4 first route",
"source_lead": "Client tariffs/quotes; current pipeline, port, road/rail and border operator evidence",
"refresh_method": "Manual published tariffs and dated quotes; tariff-year, FX and access refresh.",
"model_connection": "No operational route allocation or delivered-cost engine.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 10 of 16. Gap IDs and original evidence references retained in notes.
{
"status": "Geographic explanation; schematic candidate corridors, not validated fuel routes or catchments",
"projection": "+proj=laea +lat_0=-27 +lon_0=24 +datum=WGS84 +units=m +no_defs",
"extent": [
12.5,
-35.5,
35.5,
-17.0
],
"sources": [
"https://www.wbcg.com.na/trans-kalahari-corridor/",
"https://tracn4.co.za/about-history/",
"Kickoff appendix: Durban-NMPP-Lesedi schematic"
],
"points": {
"Walvis Bay": [
14.505,
-22.95
],
"Windhoek": [
17.08,
-22.57
],
"Gaborone": [
25.91,
-24.65
],
"Matola / Maputo": [
32.47,
-25.96
],
"Mbombela": [
30.99,
-25.47
],
"Gauteng": [
28.04,
-26.2
],
"Lesedi*": [
28.39,
-26.44
],
"Durban": [
31.03,
-29.88
],
"Komatipoort": [
31.95,
-25.44
],
"Rustenburg": [
27.24,
-25.67
]
},
"routes": [
{
"name": "Walvis: Trans-Kalahari candidate",
"style": "west",
"waypoints": [
[
14.505,
-22.95
],
[
17.08,
-22.57
],
[
18.97,
-22.45
],
[
21.65,
-21.7
],
[
23.96,
-24.4
],
[
25.91,
-24.65
],
[
25.7,
-25.25
],
[
27.24,
-25.67
],
[
28.04,
-26.2
]
]
},
{
"name": "Matola: N4 candidate",
"style": "east",
"waypoints": [
[
32.47,
-25.96
],
[
31.95,
-25.44
],
[
30.99,
-25.47
],
[
29.24,
-25.87
],
[
28.04,
-26.2
]
]
},
{
"name": "Durban: N3 / inland link",
"style": "vopak",
"waypoints": [
[
31.03,
-29.88
],
[
29.6,
-29.6
],
[
29.79,
-28.54
],
[
28.98,
-28.27
],
[
28.39,
-26.44
],
[
28.04,
-26.2
]
]
},
{
"name": "Durban: NMPP schematic",
"style": "pipe",
"waypoints": [
[
31.03,
-29.88
],
[
29.9,
-29.45
],
[
29.8,
-28.5
],
[
28.7,
-27.2
],
[
28.39,
-26.44
]
]
}
],
"limitations": "Named-place coordinates and line geometry are approximate authored cartography. No shortest-path distances, route tariff, pipeline allocation, rail service, border permit or customer right is inferred. Walvis is a comparator for selected inland destinations, not an established Vopak catchment. Matola fuel-compatible receipt and dispatch still need verification."
}
SCR master row C3; linked roadmap page 2. Deep-dive page 10.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 11: Separate demand, accessible volume and Vopak flows
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: Illustrative CSVs and road transport rates; no actual Vopak throughput or quoted transport costs supplied.
N
0
500 km
Durban
Lesedi*
Inland market | illustrative
Demand 10.0 | envelope 6.0
Current 2.0 | candidate 4.0
Eastern/coastal | illustrative
Demand 4.5 | envelope 2.5
Current 1.0 | candidate 1.5
≤0.75
0.75–1.25
1.25–1.75
1.75–2.25
>2.25
Unassessed
Receipts 2.8 + 2.0 − transfer 1.8 = unique demand 3.0
Example rates: R0.15/L + R0.002/L/km. Grey = unassessed. Volumes: bn L/year.
1
2
3
4
5
Transnet lease offers
1 Ladysmith | 2 Standerton
3 Kroonstad | 4 Bethlehem
5 Magdala*
Evidence and implications
01 | Balance arithmetic is illustrative
Example demand 21.0 less domestic production 7.0 gives imports 14.0, before exports and stocks.
02 | Transfers count once
Example Durban receipts 2.8 plus Lesedi receipts 2.0 less shared transfer 1.8 gives unique served demand 3.0.
03 | Candidate volume is conditional
The example envelope is 8.5 and additional candidate volume 5.5; neither is forecast capture.
Next steps | proposed owners
Nigel: request client flows. Manish: replace examples with matched-year product and destination records.
Illustrative road cost (R/litre) and market volumes
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No operational service-area polygon or evidence-calibrated cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. The graduated surface is illustrative delivered road transport cost: R0.15/litre dispatch plus R0.002/litre/km times shortest schematic-road distance and straight-line terminal/grid connections. These are authored example parameters, not carrier quotes or validated cost evidence. 25 km cells; cost classes <=0.75, 0.75-1.25, 1.25-1.75, 1.75-2.25 and >2.25 R/litre. Cells more than 100 km from the sampled road geometry or without a connected path remain unassessed. Fuel purchase price, tax, storage and pipeline tariffs are excluded. Operational speeds, capacity, permissions and commercial access are not evaluated. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson
Transnet lease offers are context only, not cost-model origins or available supply.
Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
SCR delivery order: page 11 of 16. Gap IDs and original evidence references retained in notes.
SCR master row R1; linked roadmap page 2. Deep-dive page 11.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 12: Size each regional market and locate competing storage
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: DMPR 2022 provincial petrol/diesel sales; public operator sources [1-7], checked 6 Oct 2026. Share not established.
All four regions | reported 2022 demand, bn litres/year
Regional competitor evidence
National total 21.90 bn L | petrol + diesel; jet excluded
Region / provinces
Reported demand
Vopak
served
Additional
contestable
0
4
8
12
Eastern coast
EC/KZN
6.02
Not
established
Not
established
Inland
GP/FS/LP/MP/NW
11.50
Not
established
Not
established
Western coast
WC
3.93
Not
established
Not
established
Other
Northern Cape
0.45
Not
established
Not
established
To calculate share: unique Vopak customer deliveries / same-year regional demand.
Contestable demand needs route cost, compatible tanks, contracts and switching evidence.
Count Durban-Lesedi transfers once. Region boundaries are working groupings, not catchments.
01 Eastern coast
Vopak: Durban [1]. Bidvest: Durban and Richards Bay [2]; mixed-product capacity.
Transnet: Ladysmith lease tanks [7].
02 Inland
Vopak: Lesedi [1]. Bidvest: Isando [2].
Sasol: Alrode, Pretoria West, Waltloo, Sasolburg [6]. Transnet: Tarlton / Jameson Park + four lease sites [7].
03 Western coast
Burgan Cape: Cape Town petrol/diesel terminal [3]. Confirm current tank availability and customer access.
04 Other / Northern Cape
Operator coverage incomplete. Check Shell site notices [4] and NERSA licences/access records [5].
[1] Vopak
[2] Bidvest
[3] Burgan
[4] Shell
[5] NERSA
[6] Sasol
[7] Transnet
Notes: Regional demand uses reported 2022 petrol/diesel sales, aggregated from all four quarters for nine provinces. Historical sales are a demand proxy, not current terminal catchments. No actual Vopak deliveries or contestable customer volumes were supplied for any region. No share percentage is calculated or imputed; unknown is not zero. The earlier illustrative 22.2/20.0% shares have been removed from this page. Other operators are potential competing or complementary storage providers, not confirmed direct competitors for every customer. Footprint is a starting inventory, not exhaustive. Storage capacities are stocks, not deliveries, and may include ineligible products. Obtain matched-year unique Vopak deliveries, customer destinations, transfer reconciliation, route costs, product-compatible capacity and contracts before calculating shares. Owner Manish; Nigel review. Refresh the source when a later complete provincial year is available. Sales file: C:\Users\ITafr\Desktop\Insights\liquid_fuels_model\assumptions\2026\timeseries\fuel_sales_department_by_province_quarterly.csv; SHA256 aec82481b33f70429b6b8e7c9c02767d62a6e8c7bf6bda09e21123a5bc56c9d6; received workbooks: ['2022-Quarter4-Magisterial-Districts-data.xlsx']. Regional totals (bn litres): {'Eastern coastal': 6.019977323334999, 'Inland': 11.499633855183989, 'Western coastal': 3.9307750071499967, 'Other / Northern Cape': 0.4518100489230001}.
Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
[1] Vopak: https://www.vopak.com/system/files/Vopak_Annual_Report_2025.pdf | 2025 reporting year | Not matched petrol/diesel terminal throughput
[2] Bidvest Tank Terminals: https://www.bidtanks.com/pages/1562/about-us | Publication date not stated | Site capacities imply 955603 m3 versus homepage 868000 m3; includes non-petrol/diesel products
[3] VTTI Burgan Cape Terminal: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; download published 2025-06-25 | Storage stock not throughput; available-capacity notice needs period confirmation
[4] Shell: https://www.shell.co.za/motorists/shell-fuels/fuel-storage-facilities.html | Publication date not stated | Does not establish current independent terminal capacity or market share
[5] NERSA: https://www.nersa.org.za/petroleum-pipelines/third-party-access | Index entries dated 2020-09-25 | Historical mechanisms are not current contracted customer volumes or a complete competitor census
[6] Sasol: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Notice period ends March 2026; current access and site ownership need confirmation
[7] Transnet Pipelines: https://www.transnet.net/TPL-Leasing-Opportunities | 2026-10-05 RFPs; manual commencement 2024-09-01 | Lease assets are not available operating supply; refurbishment licensing and award conditional; unknown capacity at Bethlehem/Magdala
SCR delivery order: page 12 of 16. Gap IDs and original evidence references retained in notes.
SCR master row R1; linked roadmap page 2. Deep-dive page 12.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 13: Show what must hold to reach each candidate volume
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: Existing illustrative catchment CSV; conditions authored for review. No actual Vopak share, cost threshold or forecast capture established.
Accessibility gates and volume milestones | illustrative bn L/year
ILLUSTRATIVE | each increment requires evidence; not cumulative terminal receipts
Current example
3.0
+ coastal candidate
4.5
+ inland candidate
8.5
What must be true for the additional volume?
Gate | Coastal +1.5 | Inland +4.0
Delivered cost | ≤ agreed customer threshold | Competitive full route R/litre
Physical access | Compatible receipt / dispatch | NMPP or alternative route capacity
Commercial rights | Customer access / switching | Destination / contract access
Volume accounting | Unique final deliveries | Remove shared Durban–Lesedi transfers
Evidence and implications
01 | Reach is necessary, not sufficient
Accessibility map p9 and competing routes p10 locate candidate access. Neither currently links a verified cost threshold to customer litres.
02 | Example milestones are conditional
The current example is 3.0. Coastal candidate 1.5 raises it to 4.5; inland candidate 4.0 raises it to 8.5. These are authored volumes.
03 | Every increment needs four gates
Evidence cost, route/tank capacity, customer rights and unique deliveries for the same product and period. Unassessed litres remain explicit.
Next steps | proposed owners
Nigel: agree destinations and acceptable delivered cost. Manish: build a customer-by-route gate table; record passed, failed and unassessed litres, with sources and conditions.
Notes: [
{
"id": "SA12",
"story": "Resolution",
"question": "Vopak market share at Durban and Lesedi",
"existing_work": "Pack page 13: illustrative 3.0 / 4.5 / 8.5 bn L milestones and required conditions; sourced regional sales page 12. Actual client flows and share remain unknown.",
"gap": "Unique customer deliveries, receipts, shared transfers, destinations and matched period.",
"action": "Nigel requests client flow extract; Manish reconciles receipt/transfer/final-delivery records and counts final demand once.",
"closure_evidence": "Separate terminal throughput and unique served-demand shares; matched-year/product denominator; traceable records, no capacity-as-share.",
"owner": "Nigel client request; Manish reconciliation",
"timing": "W1 request/schema; W2+ on receipt",
"source_lead": "Vopak operational/customer data; public unique-throughput data not established",
"refresh_method": "Client-approved monthly/annual extract with product/destination coverage and transfer IDs.",
"model_connection": "Current p6 flow volumes illustrative; future shared flow contract.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA13",
"story": "Resolution",
"question": "Additional commercially contestable market",
"existing_work": "Pack page 13: delivered-cost, physical-capacity, customer-rights and volume-accounting gates. All candidate increments remain unassessed.",
"gap": "Usable product-compatible tanks, spare routes, contracts, switching, customer overlap and Northern Cape inventory.",
"action": "Combine customer destinations with evidenced routes and rights; separate physical reach, commercial envelope and potential capture.",
"closure_evidence": "Accessible demand by product/region/period; explicit assumptions and unassessed residual; competitors volume is not automatically capturable.",
"owner": "Manish evidence; Nigel commercial review",
"timing": "W2-W4",
"source_lead": "Storage/competitor CSVs; NERSA licences; client contracts and operator notices",
"refresh_method": "Manual licences/notices; refresh contractual period, site changes and lease milestones.",
"model_connection": "No validated commercial customer-flow allocation.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 13 of 16. Gap IDs and original evidence references retained in notes.
Volume milestones derive only from the existing illustrative catchment CSV. Gates specify required evidence, not calculated allocation. No threshold assigned and no new model volume invented.
SCR master row R1; linked roadmap page 2. Deep-dive page 13.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 14: Compare published storage capacity by location
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: Vopak; Bidvest; VTTI Burgan Cape; Transnet lease RFPs (5 Oct 2026), pp. 2-3. Checked 6 Oct 2026.
Published storage by location | thousand m³; mixed capacity bases
One shared scale for every location
0
200
400
600
800
Durban
799.55
Richards Bay
483.80
Lesedi
140.00
Cape Town
122.00
Isando
32.50
Ladysmith*
8.54
Kroonstad
3.30
Standerton
2.35
Vopak
Bidvest
Burgan Cape
Transnet (lease)
Small lease bars reflect smaller tank volumes; they are not operating supply.
*Ladysmith excludes 0.474 intermixture. Unquantified: Bethlehem, Magdala, Sasol, Tarlton, Jameson Park.
Evidence and implications
01 | Capacity is a stock
Published tank volumes are not annual fuel deliveries or market share.
02 | The inventory is partial
Missing capacities are unknown, rather than zero; mixed product scopes limit comparison.
03 | Leases are conditional
Transnet lease tanks are not counted as currently available operating supply.
Next steps | proposed owners
Manish: verify product compatibility, capacity basis and operating status. Nigel: confirm usable client capacity.
Notes: Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
All eight locations use one linear axis, 0-850 thousand m3; no enlarged inset, axis break or minimum visual bar width. Location/value labels all use 12pt; ticks and legend 11pt. Gross stocks and RFP-stated lease tanks are not like-for-like usable operating capacity; no national total is inferred. Ladysmith: 8540 m3 petrol/diesel working, excluding 474 m3 intermixture; total working 9014 m3. Standerton: (1350000+220000+783000)/1000=2353 m3, basis unspecified. Kroonstad: approximately 3300 m3, basis unspecified. Bethlehem/Magdala petroleum storage is unquantified. Lease offers are excluded from operating supply and cost-model origins. Primary RFPs retained under external/data/raw/transnet_leasing_20261006/. https://www.transnet.net/TPL-Leasing-Opportunities
SCR delivery order: page 14 of 16. Gap IDs and original evidence references retained in notes.
SCR master row R2; linked roadmap page 2. Deep-dive page 14.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 15: Gate investment on evidenced incremental customer flows
1 SCR overview
2 Situation
3 Complication
4 Resolution
Source: Partner SA storyboard; open evidence register, 6 Oct 2026. Placeholder; no forecast or actual share inferred.
Resolution | optional service and investment assessment
EVIDENCE GAP | analysis specification, not a populated result
New storage and investment scope
Incremental accessible flows, turnover/peak inventory, product compatibility, cost and commercial return criteria.
Output: Throughput-to-usable-stock bridge with seasonality, inventory days and dispatch limits; downside sensitivity; no investment claim from import deficit alone.
Evidence required before quantification
Partial gross/lease stocks, without client handling/inventory profile.
Detailed service sizing deferred; infrastructure secondary to fuel integration.
Evidence and implications
01 | Evidence status
These topics remain open. Existing calculations or public source leads do not establish calibration or closure.
02 | What is already available
Partial gross/lease stocks, without client handling/inventory profile.
03 | What this page will resolve
A traceable petrol/diesel result with source, period, units and explicit unassessed residual. Jet stays separate.
Next steps | proposed owners
Nigel: decide whether to prioritise investment analysis after the flow case. Manish and Henry: bridge incremental flows to usable stock and service constraints.
Notes: [
{
"id": "SA14",
"story": "Resolution",
"question": "New storage and investment scope",
"existing_work": "Partial gross/lease stocks, without client handling/inventory profile.",
"gap": "Incremental accessible flows, turnover/peak inventory, product compatibility, cost and commercial return criteria.",
"action": "Establish flow/access case first; then test service requirements and a separately scoped investment case.",
"closure_evidence": "Throughput-to-usable-stock bridge with seasonality, inventory days and dispatch limits; downside sensitivity; no investment claim from import deficit alone.",
"owner": "Nigel commercial gate; Manish; Henry review",
"timing": "W4-W6 only if prioritised",
"source_lead": "Client service/stock profiles and scoped cost evidence",
"refresh_method": "Manual client data; refresh on demand/access case changes.",
"model_connection": "Detailed service sizing deferred; infrastructure secondary to fuel integration.",
"priority": "P2",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 15 of 16. Gap IDs and original evidence references retained in notes.
SCR master row R2; linked roadmap page 2. Deep-dive page 15.
Clickable story chevrons: overview p2; Situation p3; Complication p7; Resolution p11.

## Slide 16
Agree priorities
and next steps
Confirm demand, routes and access
6 October 2026
Internal working discussion
Photo source: Royal Vopak | Terminal Lesedi | vopak.com
Notes: Source note: Closing cover photograph: Royal Vopak, Terminal Lesedi. https://www.vopak.com/terminals/vopak-terminal-lesedi
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.