## Slide 1
South Africa
liquid fuels
market outlook
Demand, supply and routes — implications for Vopak
Durban and Lesedi | Market-sizing framework
11 October 2026
Planning estimates and illustrative capture. Customer access and usable capacity remain to be established.
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: South Africa fuel market outlook. Sources and assumptions are stated on the analytical pages. Cover photograph: Royal Vopak, Terminal Durban.

## Slide 2: 2025 production and imports broadly cover consumption and exports
Analytical workbook v02, Balance; SARS calendar-2025 customs. Demand estimated; production assumed; trade recorded. Stock change and statistical/scope differences unresolved. Values rounded; the 0.034bn L gap uses unrounded data.
Strictly Confidential
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Billion litres | calendar 2025
Supply: 5.80bn L assumed production + 16.70bn L recorded imports. Uses: 20.99bn L estimated consumption + 1.55bn L recorded exports. Supply is 0.034bn L below uses. Stock change is unmeasured; the gap remains a reconciliation item. Petrol and diesel differences offset: −2.00bn L and +1.97bn L respectively.
Production + imports − exports = 20.95bn L available, versus 20.99bn L estimated consumption.
2025 petrol and diesel balance
Reported trade; estimated domestic balance
Chart: 
| Supply | Consumption + exports
Production (assumed) | 5.8 | 0
Imports (recorded) | 16.7022 | 0
Consumption (estimated) | 0 | 20.9874
Exports (recorded) | 0 | 1.5485
Production
Imports
Consumption
Exports
Notes: Department national sales; SARS 2025 trade; analytical workbook v02. 2025 demand is estimated; 5.8bn L production is a planning assumption. Gross import need includes exports and assumes no stock change.
Figures reused from South Africa market story v37; no new model assumptions.

## Slide 3: Changes in demand, domestic supply and import routes could reduce flows through Durban
Demand baseline: p4. Driver evidence: pp5–11. Restored import outlook: p14. Stats SA; Eskom; Sasol; Glencore; Galp; Petromoc; naamsa. Scenario outcomes are separate from observed evidence.
Strictly Confidential
Complication | Driver | What changes for fuel demand and Durban flows
Baseline | Baseline demand ¦ p4 | Estimated 21.0bn-litre market in 2025; petrol/diesel history and the end-use split establish the starting point.
1 Demand | Sector activity ¦ p5 | Mining, manufacturing and agriculture drive equipment and freight demand along different growth paths.
 | Eskom recovery ¦ p6 | Reliable electricity reduces peaking and backup diesel at utilities, mines, factories and farms.
 | Road-to-rail ¦ p7 | Freight shifted from trucks reduces road diesel use; net savings depend on rail traction.
 | Vehicle sales p8 ¦ Efficiency p9 | Lower fuel consumption per kilometre reduces demand at a given level of road activity.
2 Domestic supply | Refinery history p10 ¦ Outlook p14 | Higher production displaces imports; outages or lower output increase import dependence.
3 Import routes | Ports and inland connections ¦ p11 | Matola competes for inland supply. Assess Walvis Bay, pipeline access and delivered cost; Walvis Bay diversion is unquantified.
A large national import market does not automatically translate into growth for Vopak.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Notes: Stats SA sector activity and freight; Eskom Integrated Report 2025 p141; Sasol and Glencore production disclosures; Galp and Petromoc infrastructure disclosures. Detailed evidence: South Africa story v37 pp7–11.
Figures reused from South Africa market story v37; no new model assumptions.

## Slide 4: South Africa’s estimated 21bn-litre fuel market is dominated by road demand
Department annual sales, 2013–2023. Estimated 2024–2025: analytical workbook v02. The Department series is used consistently. Segment split: analytical workbook v02, Segments. Displayed figures rounded; other diesel remains unallocated.
Strictly Confidential
Billion litres
Billion litres | legend shows 2025 values
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024E | 2025E
Petrol | 11.4399 | 10.8902 | 11.4757 | 11.4623 | 11.1741 | 11.1416 | 10.7732 | 8.7615 | 9.3016 | 9.1849 | 9.037 | 8.9459 | 8.8558
Diesel | 12.1413 | 12.615 | 13.5201 | 12.0824 | 12.1472 | 12.5387 | 12.9086 | 11.69 | 12.9458 | 12.7173 | 12.9075 | 13.1352 | 12.1316
Totals: 21.94, 22.08 and 20.99bn litres. Allocations are estimates; manufacturing is an industry residual.
Demand is estimated at 20.99bn litres in 2025; road uses account for most allocated demand.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Petrol and diesel demand, 2013–2025
Estimated demand by use, 2023–2025
Chart: 
| 2023E | 2024E | 2025E
Petrol road 8.59 | 8.7658 | 8.6775 | 8.5901
Other petrol 0.27 | 0.27111 | 0.26838 | 0.26567
Freight diesel 4.82 | 4.8414 | 4.8653 | 4.8245
Other road diesel 1.61 | 1.6138 | 1.6218 | 1.6082
Mining 1.41 | 1.396 | 1.4037 | 1.4063
Agriculture 1.13 | 1.0553 | 0.96334 | 1.1312
Manufacturing 0.17 | 0.1679 | 0.16721 | 0.16508
Power 1.08 | 2.0779 | 2.1973 | 1.0843
Other diesel 1.91 | 1.7553 | 1.9165 | 1.9119
Notes: Department annual sales, 2013–2023. Estimated 2024–2025: analytical workbook v02. The Department series is used consistently. Segment split: analytical workbook v02, Segments. Displayed figures rounded; other diesel remains unallocated.
Demand is estimated at 20.99bn litres in 2025; road uses account for most allocated demand.

## Slide 5: Agricultural fuel demand rebounds while mining and manufacturing remain broadly flat
Stats SA mining/manufacturing indices and agriculture real GVA; mean 2018–2021 fuel intensity. Sector diesel values after 2021 are estimates.
Strictly Confidential
Billion litres
Chart: 
| 2023E | 2024E | 2025E
Mining | 1.396 | 1.4037 | 1.4063
Agriculture | 1.0553 | 0.96334 | 1.1312
Manufacturing | 0.1679 | 0.16721 | 0.16508
Mining: 1.40 → 1.41bn L
Agriculture: 1.06 → 1.13bn L
Manufacturing: about 0.17bn L
Manufacturing covers the energy-balance industry residual, not a complete industrial census.
Sector activity produces different demand paths; applying one GDP growth rate would hide these differences.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Estimated sector diesel demand
Estimated diesel use
Notes: Stats SA mining/manufacturing indices and agriculture real GVA; mean 2018–2021 fuel intensity. Sector diesel values after 2021 are estimates.
Sector activity produces different demand paths; applying one GDP growth rate would hide these differences.

## Slide 6: Eskom’s fuel use fell by 40% in FY2025 as electricity supply improved
Eskom Integrated Report 2025, p141. Fiscal years end in March. Reported series includes diesel and kerosene; private backup consumption is outside this series. Analytical workbook v02, Segments: IPP conversion and private-backup assumptions.
Strictly Confidential
Billion litres
Chart: 
| FY2023 | FY2024 | FY2025
Eskom diesel + kerosene, bn litres | 0.9375 | 1.1295 | 0.6791
Eskom: 1.130bn L in FY2024 → 0.679bn L in FY2025 (diesel + kerosene).
2025 utility + private power estimate: 1.08bn L, including 0.20bn L assumed private backup.
IPP conversion and fiscal-year proxies are estimates; private use is not measured by Eskom.
Improved electricity supply reduces peaking and backup fuel use; the private-backup contribution remains estimated.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Eskom diesel and kerosene use
Power fuel use
Notes: Eskom Integrated Report 2025, p141. Fiscal years end in March. Reported series includes diesel and kerosene; private backup consumption is outside this series. Analytical workbook v02, Segments: IPP conversion and private-backup assumptions.
Improved electricity supply reduces peaking and backup fuel use; the private-backup contribution remains estimated.

## Slide 7: Rail volumes are recovering, creating scope to reduce road diesel use
Stats SA P7162 December 2025 p7; all reported freight. Analytical workbook v02, Evidence.
Strictly Confidential
Million tonnes
Chart: 
| 2024 | 2025
Road, million tonnes | 979.798 | 976.468
Rail, million tonnes | 160.745 | 168.263
Rail: 160.7m tonnes in 2024 to 168.3m in 2025. Road: 979.8m to 976.5m tonnes.
A shift of mining, agricultural and manufactured goods to rail can reduce truck fuel use.
Rail growth alone does not prove road displacement; distance, cargo and traction mix matter.
Road remains the dominant freight mode; sustained rail recovery could change the diesel required to move goods.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Reported road and rail freight
Recovery and displacement
Notes: Stats SA P7162 December 2025 p7; all reported freight. Analytical workbook v02, Evidence.
Road remains the dominant freight mode; sustained rail recovery could change the diesel required to move goods.

## Slide 8: Hybrids dominate electrified new-vehicle sales; fleet fuel savings emerge as vehicles turn over
naamsa new energy vehicle sales, 2019–2025 (Quarterly Review of Business Conditions: Q3 2024 for 2019; Q2 2026 for 2020–2025); master workbook Vehicle history. Analytical workbook v02: efficiency is a planning assumption; avoid double-counting hybrid savings.
Strictly Confidential
Vehicles sold
Electrified sales rose from 407 in 2019 to 16,716 in 2025; conventional hybrids are 77% of them.
BEV: 1,088 sales in 2025, or 0.18% of all new vehicles, down from 1,257 in 2024.
PHEVs and conventional hybrids still consume fuel; savings depend on usage.
New sales are not fleet penetration. Efficiency and mileage must be modelled separately.
The model’s fuel-efficiency path is a planning assumption; new-vehicle sales alone do not quantify national fuel savings.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Electrified vehicle sales, 2019–2025
Different fuel-use effects
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
BEV | 154 | 92 | 218 | 502 | 929 | 1257 | 1088
Plug-in hybrid | 72 | 77 | 51 | 122 | 368 | 738 | 2810
Conventional hybrid | 181 | 155 | 627 | 4070 | 6485 | 13616 | 12818
Notes: naamsa all-market sales 2025; master workbook Vehicle history S31:S36; evidence retained in market story v27 p11. Analytical workbook v02: efficiency is a planning assumption; avoid double-counting hybrid savings.
The model’s fuel-efficiency path is a planning assumption; new-vehicle sales alone do not quantify national fuel savings.

## Slide 9: Improving vehicle efficiency partly offsets growth in fuel demand
Chart: figures taken from the review screenshot of 12 October 2026 (miles per US gallon by model year, converted at 235.2 ÷ MPG). SOURCE NOT IDENTIFIED: they resemble, but do not match, the US EPA Automotive Trends Report, which has no petrol/diesel split; not South African data. Analytical workbook v02, Driver bridge (Base): modelled effects, not observed savings.
Strictly Confidential
Litres per 100 km | converted from miles per gallon; source to be confirmed
Fuel use per 100 km has roughly halved since 1975: petrol from 17.4 to 8.8 litres, diesel from 13.4 to 7.6. The base case assumes 1% annual improvement in road-fuel efficiency, saving 0.79bn L by 2030. Activity adds 1.54bn L across non-power uses. Rail and power effects are accounted for separately.
The efficiency effect is a planning assumption; new-vehicle sales do not measure fleet-wide fuel savings.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Fuel use of petrol and diesel vehicles, 1975–2025
Less fuel for each kilometre travelled
Chart: 
| 1975 | 1980 | 1985 | 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025
Petrol | 17.4 | 15.1 | 13.4 | 12.8 | 12.2 | 11.8 | 11 | 10.5 | 9.7 | 9.2 | 8.8
Diesel | 13.4 | 11.8 | 10.6 | 10.1 | 9.6 | 9.2 | 8.7 | 8.3 | 7.8 | 7.7 | 7.6
Get source from Nigel
Notes: Analytical workbook v02: Driver bridge (Base), Assumptions (Base: efficiency). Effects are modelled, not observed savings. Efficiency applies to road fuel after activity growth; rail is applied afterwards. Do not add a separate EV saving to the same efficiency allowance.

## Slide 10: Reported fuel production declined through 2021; the 2025 baseline assumes 5.8bn litres
Department energy balances 2014–2021; consolidated review workbook, DR01 national balance rows 8/17. Sasol FY2025/FY2026; Glencore 2024/2025. 2025: 5.8bn L planning assumption. Historical production ends in 2021; no interpolated observations.
Strictly Confidential
Billion litres | reported history, 2014–2021
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Petrol | 10.8282 | 10.4578 | 10.3931 | 9.4344 | 9.9746 | 10.4245 | 7.895 | 6.3513
Diesel | 9.5877 | 9.3685 | 9.0142 | 7.9217 | 8.4253 | 9.0804 | 6.4478 | 5.315
5.8bn litres
Petrol/diesel planning assumption; not a reported national observation. Reported combined production fell from 20.42bn L in 2014 to 11.67bn L in 2021. SAPREF and PetroSA contribute no refining output in the 2025 assessment. Operating output and product yields determine import displacement.
Plant context: Secunda 27.6m barrels in FY2025 → 30.6m in FY2026. Natref reporting scope changes; Astron reports in energy units. These disclosures cannot be summed directly.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Reported petrol and diesel production
2025 planning baseline
Notes: Department energy balances 2014–2021; consolidated review workbook, DR01 national balance rows 8/17. Sasol FY2025/FY2026; Glencore 2024/2025. 2025: 5.8bn L planning assumption. Historical production ends in 2021; no interpolated observations.

## Slide 11: Durban’s inland share depends on competing gateways and reliable onward connections
SARS 2022/2025; Galp Matola, 3 Dec 2020; Petromoc logistics; market-sizing workbook. Map: © OpenStreetMap contributors / Geofabrik; Natural Earth; geoBoundaries. Routes show connectivity, not validated tanker access. Compare the same product and destination.
Strictly Confidential
Mapped road and rail connectivity; tanker access and operating services require confirmation. The NMPP trunk line (Durban to Jameson Park, about 560 km) is the established inland connection. Walvis Bay is a potential alternative.
Durban and other SA ports
2025 Durban customs: 13.16bn L. Allocate national imports across ports before sizing inland reach.
Durban–NMPP–Lesedi
Existing inland connection; customer/product access, receipt and dispatch constraints determine serviceable flows.
Matola infrastructure
Galp/IPG: 60,000m³ petrol/diesel; Petromoc: 390,000m³ across fuels. Do not add overlapping capacities or equate storage with SA throughput.
Mozambique flows
Komatipoort imports: 0.303bn L in 2022 → 0.086bn L in 2025. Observed flows anchor route volumes.
Walvis Bay
Comparable delivered cost, access and SA flows remain unestablished. No quantified diversion or capture is assigned.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Competing inland supply corridors
Evidence and implications
Notes: SARS 2022/2025; Galp Matola, 3 Dec 2020; Petromoc logistics; market-sizing workbook. Map: © OpenStreetMap contributors / Geofabrik; Natural Earth; geoBoundaries. Routes show connectivity, not validated tanker access. Compare the same product and destination.

## Slide 12: Durban and Lesedi market sizing and investment issue tree
Analytical workbook v02; SARS 2025; provincial demand 2022; Transnet Pipelines FY2025. Production is a planning assumption; capture is illustrative. Shared Durban–Lesedi fuel is counted once. Historical catchments retain their stated years.
Strictly Confidential
1 NATIONAL DEMAND
2 SUPPLY AND DELIVERY
3 VOPAK OPPORTUNITY
4 INVESTMENT
National consumption 2025 estimate 21.0bn litres
Demand by product Petrol 8.9bn L Diesel 12.1bn L
Demand by use Road, mining, agriculture Manufacturing and power
Demand parameters
GDP and sectors
EVs, fleet, efficiency
Freight, prices, power
Gross imports, 2025
Petrol 4.45B L
Diesel 12.25B L
Domestic production 5.8bn L in 2025 Planning assumption
Ports and alternatives Durban, Matola Assess Walvis Bay
Inland delivery
NMPP trunk line
Road and rail
Coastal demand
KZN, WC, EC
Port-adjacent markets
Inland demand
Gauteng and interior
Six inland provinces
Supply and route parameters
Refinery closures, restarts, gas
Delivered cost, routes, contracts
Port, pipeline, rail capacity
Market context
2025 Durban customs 13.16B L
Catchments and gateway overlap
Durban context
Imports 13.16B L
KZN sales 4.28B L
Lesedi catchments
Gauteng 6.81B L
Inland 11.95B L
Conditional base capture
Total 2.22B L: Durban 0.86, Lesedi 1.36
20% of KZN and Gauteng sales
Incremental opportunity
Needs existing throughput baseline
Access and commitments unverified
Additional capture
Customers, contracts
Competition
Existing assets
Tanks and turns
Receipt and dispatch
New investment
Volume, capex, returns
Alternatives, downside
Resolution
Vopak share by site
Scope for investment
2025 demand estimate
2025 estimates
2025 segment estimates
2025 gross 16.70B L
5.8bn L planning baseline
2025 · Durban 13.2B L
FY25 use 5.46B L/yr
2022 · 10.0B L · proxy
2022 · 12.0B L · proxy
Gateway proxy; capture not observed
2025 / 2022 context
2022 nested demand
Illustrative capture
Pending · DR02/05
Pending · DR02/05
Pending · DR03
Pending · DR06
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Notes: Market-sizing issue tree reused from market-sizing v2000, slide 3. National demand/product estimates and production assumption aligned to analytical workbook v02. Provincial catchments retain 2022 source periods. Capture remains illustrative; Walvis Bay diversion unquantified.

## Slide 13: How the national fuel market translates into Vopak’s addressable volume
Analytical workbook v02 (demand, imports); SARS customs, Durban office, 2025; Department provincial sales 2022; market-sizing workbook. Bars are drawn to scale. Step 4: 2022 sales beside 2025 imports; Gauteng is also supplied by Secunda, Natref and Matola. Step 6: 146,000 m³ working fuel tanks (estimate) at Vopak’s stated target of 2–3 turns a month. Capture is an illustrative 20%, not a contracted share. Walvis Bay is a route to assess; no diversion volume is assigned.
Strictly Confidential
Step 6: Vopak’s Durban tanks handle about 3.5bn litres a year at two turns a month; volumes above that need new tanks.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Sizing step
Billion litres a year, 2025
Basis
21.0
1 National demand
Petrol and diesel, estimated from the Department’s 2023 sales.
16.7
2 Import requirement
80% of demand is imported; domestic production is 5.8bn L.
13.2
3 Ports and inland routes
Landed at Durban: 79% of imports. Other ports and Matola take the rest.
4.3
6.8
= 11.1
4 Addressable market
The two markets the sites serve: KwaZulu-Natal (4.3) and Gauteng (6.8). Department sales, 2022.
2.2
5 Achievable capture
Illustrative 20% of step 4: 0.86 at Durban, 1.36 through Lesedi. Vopak’s actual share is not published.
Notes: Framework: analytical workbook v02 and market-sizing workbook. Gateway shares and customer access require validation. Walvis Bay is a route to assess; no diversion volume is assigned. Stock build increases import need; stock draw reduces it.
Figures reused from South Africa market story v37; no new model assumptions.

## Slide 14: Refinery recovery could materially reduce imports from the 16.6bn-litre base case
Restored from South Africa story v37; analytical workbook v02, Scenarios and Driver bridge. Gross imports = demand − domestic supply + fixed 2025 exports; zero stock change. 2025 production: 5.8bn L assumption. Restart volumes and timing are scenario assumptions.
Strictly Confidential
Billion litres | existing combined scenarios
Baseline demand stays near 21bn L (20.86bn L in 2030). 2030 imports: base 16.61bn L; low-import case 8.26bn L; high-import case 19.68bn L. The low-import case adds 0.87bn L of operating output and 5.67bn L from assumed restarts. Demand assumptions also vary across these cases. The chart is not an isolated refinery sensitivity or a probability forecast.
Higher domestic output displaces imports; restart timing, utilisation and product yields determine the effect.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Gross import requirement and baseline demand, 2025–2030
Domestic supply drives the largest reduction
Chart: 
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Low imports | 16.7359 | 16.165 | 15.5984 | 15.0359 | 11.6443 | 8.2568
Base | 16.7359 | 16.708 | 16.681 | 16.6549 | 16.6295 | 16.6051
High imports | 16.7359 | 17.3083 | 17.8888 | 18.4777 | 19.0749 | 19.6808
Base demand | 20.9874 | 20.9596 | 20.9326 | 20.9064 | 20.8811 | 20.8566
Check with Nigel
Notes: Restored from South Africa story v37; analytical workbook v02, Scenarios and Driver bridge. Gross imports = demand − domestic supply + fixed 2025 exports; zero stock change. 2025 production: 5.8bn L assumption. Restart volumes and timing are scenario assumptions.

## Slide 15: Substantial imports sustain the market, while customer capture determines Vopak’s expansion
Analytical workbook v02 base scenario; market-sizing workbook and working-capacity assessment. Capture is illustrative; Lesedi is included within Durban flow. Contracted share, product balance and usable capacity remain to be established. Capture base: Department sales 2022, KwaZulu-Natal 4.28bn L and Gauteng 6.81bn L.
Strictly Confidential
16.6bn L
2030 national imports
Base-case imports across all gateways. Activity growth broadly offsets power, rail and efficiency reductions; domestic production stays at 5.8bn litres.
2.22bn L
Illustrative capture, Durban and Lesedi
Assumes 20% of the 11.1bn litres sold in KwaZulu-Natal and Gauteng, the markets the two sites serve: 0.86bn litres at Durban and 1.36bn litres through Lesedi.
Illustrative share; no explicit deduction for Matola or Walvis Bay diversion.
Expansion follows
secured incremental flow
The illustrative flow fits the preliminary working-tank calculation.
Secure additional customer volumes, establish usable capacity, and identify the constraint that investment would solve.
Invest where secured additional volumes create a demonstrated capacity shortfall.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Notes: Analytical workbook v02 base scenario; market-sizing workbook and working-capacity assessment. Capture is illustrative; Lesedi is included within Durban flow. Contracted share, product balance and usable capacity remain to be established.
Figures reused from South Africa market story v37; no new model assumptions.

## Slide 16
Thank you
South Africa fuel market and Vopak opportunity
Discussion
11 October 2026
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: Closing discussion. Cover photograph: Royal Vopak, Terminal Durban.