## Slide 1
Liquid fuels
demand and supply
model
Week 1 analytical pack
South Africa | Petrol and diesel
6 October 2026
Internal working discussion
Photo source: Royal Vopak | Terminal Durban | vopak.com
Notes: Speaker note: Walk through four sections: the project question, the analytical
requirements, the model-build problem and the delivery approach. The purpose is to
connect the analyst's tasks to the decisions the engagement needs to support.
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.

## Slide 2: Connect the SA market story to evidence and next actions
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Partner SA storyboard pp.30-32; repository evidence and diagnostics, 6 Oct 2026. All gaps remain open.
Situation - Complication - Resolution | evidence and gaps
01 Situation | establish the market baseline
Have: demand history, regions and operators (pp.3-4,12,14).
Gap: recent fuel balance, finished imports and entry ports.
Close: matched-year balance and exact data reconciliation. W1-W2.
02 Complication | quantify what could change
Have: provisional vehicle, power-diesel and supply calculations.
Gap: calibrated driver reversals, refinery cases and route costs.
Close: define levers in W1; test their litres/import effects in W2-W4.
03 Resolution | establish Vopak opportunity
Have: regional competitor footprint and published tank stocks.
Gap: actual share, customer access and additional contestable volume.
Close: client flows + cost/access tests; investment follows the flow case.
Week windows are targets. Partner propositions require testing; they are not established findings.
Evidence and implications
01 | Situation
Establish demand, domestic output and finished imports; locate the economically reachable market.
02 | Complication
Test demand-driver reversals, refinery cases and the relative cost and feasibility of competing routes.
03 | Resolution
Establish actual Vopak share and additional contestable customer flows. Investment follows the flow case.
Next steps | proposed owners
Manish: close baseline/source flags and define levers. Nigel: obtain client flows and choose the first corridor. Week windows remain proposed.
Notes: Partner storyboard pp30-32 supplied in chat and preserved under external/partner_story_20261006/. Partner propositions are hypotheses, not assertions that reversals or refinery projects have occurred. All gap records are open pending the stated evidence and review. Work windows/owners are planning targets. Fuel-model integration takes precedence over broad infrastructure or detailed service sizing. Jet remains separately tracked and excluded from client petrol/diesel totals. Detailed analyst review: workstreams/WS3_reporting_delivery/partner_story_alignment_2026-10-06.md.
{
"date": "2026-10-06",
"scope": "SA petrol/diesel; jet separate",
"status": "Review roadmap; not approval or forecast",
"partner_source": "external/partner_story_20261006 (received pp30-32 screenshots)",
"planning": "Week windows and analyst assignments proposed, not confirmed commitments",
"rows": [
{
"id": "SA01",
"story": "Situation",
"question": "SA demand history and regional market size",
"existing_work": "Pack pp2-3,7: quarterly provincial sales 2013-2022; national series 2005-2023; 2023 incomplete.",
"gap": "Later complete year; six provincial/national annual differences; historical driver contributions not quantified.",
"action": "Review 2013/14/15/17/18/21 against original workbooks; source later full years. Preserve 2022 historical label.",
"closure_evidence": "Old value, proposed value, source cell and reason for each correction; all province/product quarters; national tie.",
"owner": "Manish; Nigel review",
"timing": "W1 investigate; W2 reconcile",
"source_lead": "fuel_sales_department_by_province_quarterly.csv; fuel_sales_department.csv; DMPR index",
"refresh_method": "Manual workbook download and parser rerun; completeness and revisions checked.",
"model_connection": "pptx/scripts/provincial_demand_map.py::sales; reporting evidence, not approved model calibration.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA02",
"story": "Situation",
"question": "Economically reachable eastern/inland market",
"existing_work": "Working province groups p2; illustrative road-cost map p5; storage footprint.",
"gap": "Actual customer destinations, cost threshold, route capacity and commercial rights.",
"action": "Use delivered transport cost R/litre for actual destinations; qualify physical reach and customer access separately.",
"closure_evidence": "Reachable and commercially accessible volume by product/destination/year; sourced costs and explicit unassessed residual.",
"owner": "Manish route evidence; Nigel client access",
"timing": "W1 define contract; W2-W4 integrate",
"source_lead": "Regional membership CSV; client destinations; route tariffs and quotations",
"refresh_method": "Manual client/route evidence; refresh tariff, access or destination changes.",
"model_connection": "Illustrative accessibility module is presentation only; no operational routing engine.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA03",
"story": "Situation",
"question": "Domestic production versus finished imports",
"existing_work": "Energy balance 2007-2021 staged; provisional supply engine; p4 provincial source illustration.",
"gap": "Matched recent demand, output, imports, exports and stocks; actual provincial origin unavailable.",
"action": "Reconcile national petrol/diesel first; retain provincial origin as unknown without evidence; separate crude and finished products.",
"closure_evidence": "Production + imports - exports - stock build = consumption by fuel/year; unit/coverage bridge and residual explained.",
"owner": "Manish; Nigel review",
"timing": "W1 mapping; W2 historical balance",
"source_lead": "energy_balance_department.csv; DMPR commodity flow; SARS trade data",
"refresh_method": "Manual annual energy workbook and monthly customs download; preserve revisions.",
"model_connection": "src/lfm/model/supply/flows.py::compute_balance currently demand less supply; exports/stocks not explicit.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA04",
"story": "Situation",
"question": "Import entry ports and origin",
"existing_work": "Ports and schematic corridors from kickoff appendix.",
"gap": "Product-specific finished imports by port/year and source country; liquid bulk is not all fuel.",
"action": "Bridge SARS product/quantity data to TNPA port cargo; check port identifier availability and density conversion.",
"closure_evidence": "National finished imports tied to evidenced port allocations; unallocated remainder explicit.",
"owner": "Manish; Nigel source access",
"timing": "W2-W3",
"source_lead": "https://tools.sars.gov.za/tradestatsportal/data_download.aspx ; https://www.transnetnationalportsauthority.net/Commercial%20and%20Marketing/Pages/Port-Statistics.aspx",
"refresh_method": "Manual portal downloads; check HS coverage, revisions, tonnes/litres and crude/nonfuel exclusions.",
"model_connection": "No imported-volume allocation by port/destination in current engine.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA05",
"story": "Situation / Complication",
"question": "Power-generation diesel and potential reversal",
"existing_work": "Eskom OCGT observations 2022-2026 staged; engine capacity/load factor/efficiency path.",
"gap": "Eskom/IPP coverage, fiscal/calendar alignment, fuel conversion and forecast dispatch. No loadshedding does not mean no OCGT diesel.",
"action": "Reconcile generation and fuel burn by plant set; calibrate dispatch alternatives; avoid additive double-counting.",
"closure_evidence": "Historical GWh-to-litres tie; baseline/alternative dispatch, units, dates and incremental demand effect.",
"owner": "Manish; Nigel review",
"timing": "W1 lever; W2-W3 calibration",
"source_lead": "ocgt_generation_eskom.csv; generation.yaml; primary Eskom operating reports",
"refresh_method": "Manual quarterly/annual operating reports; scope and period checks.",
"model_connection": "src/lfm/model/demand/generation.py::compute_country_annual.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA06",
"story": "Situation / Complication",
"question": "Road-to-rail freight shift",
"existing_work": "Road vehicle cohort calculation and schematic rail context; no mode-shift source series found in current vintage.",
"gap": "Road/rail freight, tonne-km, distance, payload, empty running and feasible rail intervention.",
"action": "Use Stats SA P7162 and operator traffic evidence; distinguish tonnes/revenue/tonne-km; convert displaced truck work into diesel.",
"closure_evidence": "Specific intervention with baseline/alternative mode shares, dates and diesel-intensity bridge; no duplicate mileage reduction.",
"owner": "Manish; Nigel intervention; Henry review",
"timing": "W1 lever definition; W2-W4 integration",
"source_lead": "https://www.statssa.gov.za/?PPN=P7162&SCH=74110&page_id=1854 ; Transnet freight traffic/access evidence",
"refresh_method": "Manual monthly survey and annual operator reports; coverage/revision checks.",
"model_connection": "vehicles.py has no explicit rail-shift lever.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA07",
"story": "Situation / Complication",
"question": "BEV, hybrid, efficiency and charging effects",
"existing_work": "Naamsa NEV sales 2019-2025 staged; engine EV curve and efficiency parameters.",
"gap": "Sales versus stock, segment scope, BEV/HEV distinction, survival, mileage and charging intervention.",
"action": "Calibrate uptake and fleet turnover; retain hybrids as fuel users with separate efficiency; define charging policy/investment lever.",
"closure_evidence": "Opening-fleet/cohort tie; drivetrain-specific L/100km; dated uptake alternatives and litres effect.",
"owner": "Manish; Nigel review",
"timing": "W1 levers; W2-W3 calibration",
"source_lead": "nev_sales_naamsa.csv; vehicles.yaml; official registration evidence",
"refresh_method": "Manual quarterly/annual data; reconcile drivetrain taxonomy and scope.",
"model_connection": "src/lfm/model/demand/vehicles.py::compute_country_annual and _ev_penetration.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA08",
"story": "Situation / Complication",
"question": "GDP, fuel prices and kilometres travelled",
"existing_work": "Macro sources staged; price series 2011-2024-04; engine GDP/capita new-sales relationship.",
"gap": "Real-price basis, causal activity effect, elasticities and actual/forecast extension.",
"action": "Map GDP source into provider with population/base-price rules; propose price-to-km response separately from efficiency.",
"closure_evidence": "Explicit historical/forecast boundary and consuming function; calibrated sensitivity without duplicate activity reductions.",
"owner": "Manish; Nigel review",
"timing": "W1 mapping; W2-W3 validation",
"source_lead": "macro_statssa.csv; macro_worldbank.csv; gdp_growth_treasury.csv; fuel_prices_department.csv",
"refresh_method": "Stats SA/Treasury/DMPR manual downloads; World Bank API; independent vintage and freshness checks.",
"model_connection": "vehicles.py GDP new-sales path; no explicit fuel-price-to-mileage response.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA09",
"story": "Situation / Complication",
"question": "Refinery closures, availability and SAPREF proposal",
"existing_work": "Refinery assumptions and utilisation 2008-2050; provisional supply engine; duplicate-row diagnostics.",
"gap": "Current output/yields/status; dated closures/restarts; SAPREF project evidence; 558 extra refinery rows unresolved.",
"action": "Resolve repeated keys against original named ranges; build refinery-year status and output; treat proposals as conditional scenarios.",
"closure_evidence": "Unique country/year/scenario keys with source cells; actual/proposed distinction; per-refinery output tie and import sensitivity.",
"owner": "Manish; Nigel review; Henry challenge",
"timing": "W1 duplicates; W2-W3 scenarios",
"source_lead": "supply.yaml; refinery_production.csv; original workbook; primary operator/CEF/PetroSA reports",
"refresh_method": "Manual reports; refresh outages, restart, ownership or sanctioned-project changes.",
"model_connection": "src/lfm/model/supply/flows.py::compute_supply.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA10",
"story": "Complication",
"question": "Secunda gas/MRG and Natref future",
"existing_work": "Generic Sasol/Natref capacities, yields and utilisation; no plant-level gas-liquid linkage.",
"gap": "MRG timing and causal liquid-fuel effect; Natref future not established; partner propositions untested.",
"action": "Check latest primary Sasol disclosures; technical reviewer specifies mechanism before any fuel-output change.",
"closure_evidence": "Documented plant-level mechanism and dated scenario; no gas-to-liquid displacement inferred without evidence.",
"owner": "Manish sources; Henry technical review; Nigel scenarios",
"timing": "W2-W3",
"source_lead": "https://www.sasol.com/sasol-suite-reports ; 2026 Sasol SEC 20-F",
"refresh_method": "Manual quarterly/annual operating guidance and plant/gas changes.",
"model_connection": "No gas-to-fuel mechanism; utilisation/yield changes need explicit sourced scenario.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA11",
"story": "Complication",
"question": "Durban-NMPP-Lesedi versus road/rail, Matola and Walvis Bay",
"existing_work": "Schematic appendix routes and illustrative Durban/Lesedi road-cost map.",
"gap": "Comparable route costs, NMPP capacity/tariff, actual rail service and cross-border feasibility.",
"action": "Choose first product/customer destination; compare full handling/transport/transfer cost, border/FX where relevant, same period and basis.",
"closure_evidence": "Comparable delivered R/litre with cost components, capacity/access limits and dated sources; no national optimisation claim.",
"owner": "Manish evidence; Nigel corridor choice; Henry review",
"timing": "W1 comparison contract; W2-W4 first route",
"source_lead": "Client tariffs/quotes; current pipeline, port, road/rail and border operator evidence",
"refresh_method": "Manual published tariffs and dated quotes; tariff-year, FX and access refresh.",
"model_connection": "No operational route allocation or delivered-cost engine.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA12",
"story": "Resolution",
"question": "Vopak market share at Durban and Lesedi",
"existing_work": "Sourced regional sales p7; published capacity p8; illustrative transfer arithmetic p6.",
"gap": "Unique customer deliveries, receipts, shared transfers, destinations and matched period.",
"action": "Nigel requests client flow extract; Manish reconciles receipt/transfer/final-delivery records and counts final demand once.",
"closure_evidence": "Separate terminal throughput and unique served-demand shares; matched-year/product denominator; traceable records, no capacity-as-share.",
"owner": "Nigel client request; Manish reconciliation",
"timing": "W1 request/schema; W2+ on receipt",
"source_lead": "Vopak operational/customer data; public unique-throughput data not established",
"refresh_method": "Client-approved monthly/annual extract with product/destination coverage and transfer IDs.",
"model_connection": "Current p6 flow volumes illustrative; future shared flow contract.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA13",
"story": "Resolution",
"question": "Additional commercially contestable market",
"existing_work": "Competitor footprint and partial published storage; lease sites explicitly conditional.",
"gap": "Usable product-compatible tanks, spare routes, contracts, switching, customer overlap and Northern Cape inventory.",
"action": "Combine customer destinations with evidenced routes and rights; separate physical reach, commercial envelope and potential capture.",
"closure_evidence": "Accessible demand by product/region/period; explicit assumptions and unassessed residual; competitors volume is not automatically capturable.",
"owner": "Manish evidence; Nigel commercial review",
"timing": "W2-W4",
"source_lead": "Storage/competitor CSVs; NERSA licences; client contracts and operator notices",
"refresh_method": "Manual licences/notices; refresh contractual period, site changes and lease milestones.",
"model_connection": "No validated commercial customer-flow allocation.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA14",
"story": "Resolution",
"question": "New storage and investment scope",
"existing_work": "Partial gross/lease stocks, without client handling/inventory profile.",
"gap": "Incremental accessible flows, turnover/peak inventory, product compatibility, cost and commercial return criteria.",
"action": "Establish flow/access case first; then test service requirements and a separately scoped investment case.",
"closure_evidence": "Throughput-to-usable-stock bridge with seasonality, inventory days and dispatch limits; downside sensitivity; no investment claim from import deficit alone.",
"owner": "Nigel commercial gate; Manish; Henry review",
"timing": "W4-W6 only if prioritised",
"source_lead": "Client service/stock profiles and scoped cost evidence",
"refresh_method": "Manual client data; refresh on demand/access case changes.",
"model_connection": "Detailed service sizing deferred; infrastructure secondary to fuel integration.",
"priority": "P2",
"status": "Open; existing evidence does not establish closure"
}
]
}
SCR delivery order: page 2 of 16. Gap IDs and original evidence references retained in notes.

## Slide 3: Locate fuel demand alongside the infrastructure serving it
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: DMPR 2022 sales; geoBoundaries/OCHA/MDB 2020 provinces (CC BY 3.0 IGO); operator sources on slide 12.
Petrol + diesel sales by province | 2022, bn litres/year
N
0
500 km
Durban
Vopak / Bidvest
Richards Bay
Bidvest
Cape Town
Burgan Cape
Lesedi / inland storage
Vopak / Bidvest
Sasol / Transnet
1
2
3
4
5
Transnet lease offers
1 Ladysmith | 2 Standerton
3 Kroonstad | 4 Bethlehem
5 Magdala*
EC
1.74
FS
1.37
GP
6.81
KZN
4.28
LP
0.50
MP
1.76
NW
1.07
NC
0.45
WC
3.93
<1
1-2
2-4
4-6
6+
bn L/year; darker = more sales
Production
Port
Vopak
Other storage
Lines: road / pipe / rail; heavy outlines: working regions
Lease offers are not operating capacity. *Magdala RFP location narrative conflicts; briefing coordinate used. Jet excluded.
Evidence and implications
01 | Demand is concentrated
Gauteng, KwaZulu-Natal and Western Cape account for 68.6% of reported 2022 petrol/diesel sales.
02 | Regions are working groups
Province boundaries define reporting groups; they do not establish terminal catchments.
03 | Sales are historical demand evidence
The map is sourced provincial sales, rather than a current-year outlook or commercial accessibility result.
Next steps | proposed owners
Manish: source a later complete year and test actual destinations, route costs and customer access.
Notes: Observed historical sales, separate from the illustrative market figures on slide 6.
Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
Historical sales are a demand-location proxy, not 2026 demand or customer delivery destinations. All 18 province/product series have four quarters in 2022; provincial sum matches national sales within 1 litre. No district-level smoothing or within-province hotspot is inferred. Colour measures total annual provincial volume, not litres per km2. Region borders use the authored province membership, not a service area. Eastern coastal=EC+KZN; Inland=GP+FS+LP+MP+NW; Western coastal=WC; Other=NC. The observed totals and regions are separate from the illustrative market figures on slide 6. Source CSV C:\Users\ITafr\Desktop\Insights\liquid_fuels_model\assumptions\2026\timeseries\fuel_sales_department_by_province_quarterly.csv; SHA256 aec82481b33f70429b6b8e7c9c02767d62a6e8c7bf6bda09e21123a5bc56c9d6; original workbook(s) ['2022-Quarter4-Magisterial-Districts-data.xlsx']. Department index: https://www.dmpr.gov.za/Portals/0/Energy_Website/files/media/media_SAVolumes.html. Boundary metadata/source/license: assets/maps/geoboundaries_zaf_adm1_metadata.json. Reporting evidence remains provisional pending analyst review; owner Manish, Nigel review. Refresh when the source supplies a later complete year; check every province/product quarter and reconcile national totals.
SCR delivery order: page 3 of 16. Gap IDs and original evidence references retained in notes.

## Slide 4: Track petrol and diesel sales by province over time
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: DMPR quarterly provincial sales extract; complete calendar years only. Petrol + diesel; jet excluded.
Annual provincial sales | 2013–2022, bn litres/year
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Gauteng | 6.9574 | 7.0981 | 7.2798 | 7.1303 | 7.2139 | 7.3171 | 7.6415 | 6.0857 | 6.646 | 6.8094
KwaZulu-Natal | 4.065 | 3.8521 | 3.9126 | 3.9426 | 4.1854 | 4.0067 | 4.2545 | 4.0587 | 4.2743 | 4.2845
Western Cape | 3.7114 | 4.0928 | 4.6965 | 3.7212 | 3.6273 | 3.5434 | 3.7198 | 3.1569 | 4.0101 | 3.9308
Mpumalanga | 2.3205 | 2.3412 | 2.4544 | 2.6606 | 2.5088 | 2.4566 | 2.2367 | 1.9979 | 1.9372 | 1.7572
Eastern Cape | 1.5859 | 1.6267 | 1.7991 | 1.7859 | 1.769 | 1.7703 | 1.7921 | 1.6156 | 1.7712 | 1.7355
Free State | 2.2595 | 2.1859 | 2.1803 | 1.9397 | 1.7441 | 1.9779 | 1.8837 | 1.7547 | 1.7203 | 1.3693
North West | 1.2664 | 1.1583 | 1.1888 | 1.1649 | 1.1013 | 0.99173 | 1.0073 | 0.84795 | 0.94562 | 1.0681
Limpopo | 0.82767 | 0.79082 | 0.78174 | 0.66642 | 0.63051 | 0.66217 | 0.61976 | 0.49264 | 0.48667 | 0.49563
Northern Cape | 0.58731 | 0.62826 | 0.66862 | 0.53308 | 0.53862 | 0.52173 | 0.52641 | 0.44129 | 0.45501 | 0.45181
Gauteng
KwaZulu-Natal
Western Cape
Mpumalanga
Eastern Cape
Free State
North West
Limpopo
Northern Cape
Evidence and implications
01 | History ends in 2022
The latest complete provincial year in this extract is 2022.
02 | 2023 is incomplete
Only Q1 is present; it is excluded from annual comparisons.
03 | Six years are flagged
Provincial sums differ from national sales in 2013, 2014, 2015, 2017, 2018 and 2021.
Next steps | proposed owners
Manish: reconcile each flagged value to its original workbook cell and log old value, proposed value and reason.
Notes: Annual reporting sums four quarters separately for each province/product. Missing or incomplete years are gaps, never zeros or extrapolations. 2023 has Q1 only and is excluded. Source: assumptions/2026/timeseries/fuel_sales_department_by_province_quarterly.csv. Reported sales are a demand proxy; historical reporting requires analyst review, not a forecast.
Provincial sum minus national petrol/diesel sales (bn L), mechanical flag tolerance 1 litre, not a materiality or validation threshold:
{
"2013": 0.5379449579999971,
"2014": 0.2688237130000033,
"2015": -0.034042841268004054,
"2016": -7.105427357601002e-15,
"2017": -0.0023669540000135214,
"2018": -0.4327551978270243,
"2019": -1.7763568394002505e-14,
"2020": -1.0658141036401503e-14,
"2021": -0.0007647352630151261,
"2022": -1.7763568394002505e-14
}
SCR delivery order: page 4 of 16. Gap IDs and original evidence references retained in notes.

## Slide 5: Reconcile domestic supply and finished imports
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Partner SA storyboard; open evidence register, 6 Oct 2026. Placeholder; no forecast or actual share inferred.
Situation | national balance and import entry ports
EVIDENCE GAP | analysis specification, not a populated result
Domestic production versus finished imports
Matched recent demand, output, imports, exports and stocks; actual provincial origin unavailable.
Output: Production + imports - exports - stock build = consumption by fuel/year; unit/coverage bridge and residual explained.
Import entry ports and origin
Product-specific finished imports by port/year and source country; liquid bulk is not all fuel.
Output: National finished imports tied to evidenced port allocations; unallocated remainder explicit.
Evidence and implications
01 | Evidence status
These topics remain open. Existing calculations or public source leads do not establish calibration or closure.
02 | What is already available
Energy balance 2007-2021 staged; provisional supply engine; p6 provincial source illustration.
03 | What this page will resolve
A traceable petrol/diesel result with source, period, units and explicit unassessed residual. Jet stays separate.
Next steps | proposed owners
Manish: reconcile the national fuel balance, then bridge finished imports to entry ports. Nigel: secure source access. Explain all unit conversions and unallocated volumes.
Notes: [
{
"id": "SA03",
"story": "Situation",
"question": "Domestic production versus finished imports",
"existing_work": "Energy balance 2007-2021 staged; provisional supply engine; p6 provincial source illustration.",
"gap": "Matched recent demand, output, imports, exports and stocks; actual provincial origin unavailable.",
"action": "Reconcile national petrol/diesel first; retain provincial origin as unknown without evidence; separate crude and finished products.",
"closure_evidence": "Production + imports - exports - stock build = consumption by fuel/year; unit/coverage bridge and residual explained.",
"owner": "Manish; Nigel review",
"timing": "W1 mapping; W2 historical balance",
"source_lead": "energy_balance_department.csv; DMPR commodity flow; SARS trade data",
"refresh_method": "Manual annual energy workbook and monthly customs download; preserve revisions.",
"model_connection": "src/lfm/model/supply/flows.py::compute_balance currently demand less supply; exports/stocks not explicit.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA04",
"story": "Situation",
"question": "Import entry ports and origin",
"existing_work": "Ports and schematic corridors from kickoff appendix.",
"gap": "Product-specific finished imports by port/year and source country; liquid bulk is not all fuel.",
"action": "Bridge SARS product/quantity data to TNPA port cargo; check port identifier availability and density conversion.",
"closure_evidence": "National finished imports tied to evidenced port allocations; unallocated remainder explicit.",
"owner": "Manish; Nigel source access",
"timing": "W2-W3",
"source_lead": "https://tools.sars.gov.za/tradestatsportal/data_download.aspx ; https://www.transnetnationalportsauthority.net/Commercial%20and%20Marketing/Pages/Port-Statistics.aspx",
"refresh_method": "Manual portal downloads; check HS coverage, revisions, tonnes/litres and crude/nonfuel exclusions.",
"model_connection": "No imported-volume allocation by port/destination in current engine.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 5 of 16. Gap IDs and original evidence references retained in notes.

## Slide 6: Shape the provincial split between domestic fuel and imports
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: DMPR 2022 provincial sales totals; source mix from the existing illustrative national-balance CSV. Not observed origin.
2022 sales totals | ILLUSTRATIVE domestic/import allocation
0
2
4
6
8
Gauteng
6.81
KwaZulu-Natal
4.28
Western Cape
3.93
Mpumalanga
1.76
Eastern Cape
1.74
Free State
1.37
North West
1.07
Limpopo
0.50
Northern Cape
0.45
Illustrative domestic fuel
Illustrative finished-product imports
Units: bn litres/year. Imported/domestic segments are a scenario illustration, not measured provincial flows.
Evidence and implications
01 | Demand totals are sourced
The provincial bars use reported 2022 petrol/diesel sales.
02 | Origin shares are illustrative
Domestic/import fractions are authored examples; no actual provincial origin allocation is established.
03 | Imports need a national balance
Exports and stock movements must be reconciled before a sourced import requirement can be presented.
Next steps | proposed owners
Manish: populate the matched-year national balance first; retain provincial origin as unknown until supported.
Notes: {
"status": "Illustrative allocation only; not observed provincial supply",
"demand_year": 2022,
"demand_source": "assumptions/2026/timeseries/fuel_sales_department_by_province_quarterly.csv",
"mix_source": "pptx/story/illustrative_national_balance.csv",
"method": "Apply the example domestic_supply/demand share separately for petrol and diesel to each province's reported sales; remaining volume is illustrative finished-product imports",
"geographic_assumption": "Uniform source shares by product across provinces; provincial product mix may differ",
"scope": "Finished petrol and diesel; domestically refined output counts as domestic even when crude is imported",
"owner": "Manish / Nigel review",
"replacement_trigger": "Matched-year reviewed national balance plus evidenced refinery/import-to-province flows, exports and stock reconciliation"
}
No provincial origin dataset was found in the reviewed source extract. Demand totals are reported 2022 sales; domestic/import segments are illustrative, not observed 2022 supply. The same example product-specific shares apply to every province. Imports mean finished products, not imported crude. Do not infer these flows from refinery locations or customs clearance province.
SCR delivery order: page 6 of 16. Gap IDs and original evidence references retained in notes.

## Slide 7: Translate demand drivers into explicit fuel levers
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Partner SA storyboard; open evidence register, 6 Oct 2026. Placeholder; no forecast or actual share inferred.
Complication | power, freight, fleet and economic activity
EVIDENCE GAP | analysis specification, not a populated result
Power-generation diesel and potential reversal
Historical GWh-to-litres tie; baseline/alternative dispatch, units, dates and incremental demand effect.
Road-to-rail freight shift
Specific intervention with baseline/alternative mode shares, dates and diesel-intensity bridge; no duplicate mileage reduction.
BEV, hybrid, efficiency and charging effects
Opening-fleet/cohort tie; drivetrain-specific L/100km; dated uptake alternatives and litres effect.
GDP, fuel prices and kilometres travelled
Explicit historical/forecast boundary and consuming function; calibrated sensitivity without duplicate activity reductions.
Evidence and implications
01 | Evidence status
These topics remain open. Existing calculations or public source leads do not establish calibration or closure.
02 | What is already available
Eskom OCGT observations 2022-2026 staged; engine capacity/load factor/efficiency path.
03 | What this page will resolve
A traceable petrol/diesel result with source, period, units and explicit unassessed residual. Jet stays separate.
Next steps | proposed owners
Manish: define baseline, alternatives, units, dates and consuming equation for each lever. Nigel reviews; calibrate against source observations.
Notes: [
{
"id": "SA05",
"story": "Situation / Complication",
"question": "Power-generation diesel and potential reversal",
"existing_work": "Eskom OCGT observations 2022-2026 staged; engine capacity/load factor/efficiency path.",
"gap": "Eskom/IPP coverage, fiscal/calendar alignment, fuel conversion and forecast dispatch. No loadshedding does not mean no OCGT diesel.",
"action": "Reconcile generation and fuel burn by plant set; calibrate dispatch alternatives; avoid additive double-counting.",
"closure_evidence": "Historical GWh-to-litres tie; baseline/alternative dispatch, units, dates and incremental demand effect.",
"owner": "Manish; Nigel review",
"timing": "W1 lever; W2-W3 calibration",
"source_lead": "ocgt_generation_eskom.csv; generation.yaml; primary Eskom operating reports",
"refresh_method": "Manual quarterly/annual operating reports; scope and period checks.",
"model_connection": "src/lfm/model/demand/generation.py::compute_country_annual.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA06",
"story": "Situation / Complication",
"question": "Road-to-rail freight shift",
"existing_work": "Road vehicle cohort calculation and schematic rail context; no mode-shift source series found in current vintage.",
"gap": "Road/rail freight, tonne-km, distance, payload, empty running and feasible rail intervention.",
"action": "Use Stats SA P7162 and operator traffic evidence; distinguish tonnes/revenue/tonne-km; convert displaced truck work into diesel.",
"closure_evidence": "Specific intervention with baseline/alternative mode shares, dates and diesel-intensity bridge; no duplicate mileage reduction.",
"owner": "Manish; Nigel intervention; Henry review",
"timing": "W1 lever definition; W2-W4 integration",
"source_lead": "https://www.statssa.gov.za/?PPN=P7162&SCH=74110&page_id=1854 ; Transnet freight traffic/access evidence",
"refresh_method": "Manual monthly survey and annual operator reports; coverage/revision checks.",
"model_connection": "vehicles.py has no explicit rail-shift lever.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA07",
"story": "Situation / Complication",
"question": "BEV, hybrid, efficiency and charging effects",
"existing_work": "Naamsa NEV sales 2019-2025 staged; engine EV curve and efficiency parameters.",
"gap": "Sales versus stock, segment scope, BEV/HEV distinction, survival, mileage and charging intervention.",
"action": "Calibrate uptake and fleet turnover; retain hybrids as fuel users with separate efficiency; define charging policy/investment lever.",
"closure_evidence": "Opening-fleet/cohort tie; drivetrain-specific L/100km; dated uptake alternatives and litres effect.",
"owner": "Manish; Nigel review",
"timing": "W1 levers; W2-W3 calibration",
"source_lead": "nev_sales_naamsa.csv; vehicles.yaml; official registration evidence",
"refresh_method": "Manual quarterly/annual data; reconcile drivetrain taxonomy and scope.",
"model_connection": "src/lfm/model/demand/vehicles.py::compute_country_annual and _ev_penetration.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA08",
"story": "Situation / Complication",
"question": "GDP, fuel prices and kilometres travelled",
"existing_work": "Macro sources staged; price series 2011-2024-04; engine GDP/capita new-sales relationship.",
"gap": "Real-price basis, causal activity effect, elasticities and actual/forecast extension.",
"action": "Map GDP source into provider with population/base-price rules; propose price-to-km response separately from efficiency.",
"closure_evidence": "Explicit historical/forecast boundary and consuming function; calibrated sensitivity without duplicate activity reductions.",
"owner": "Manish; Nigel review",
"timing": "W1 mapping; W2-W3 validation",
"source_lead": "macro_statssa.csv; macro_worldbank.csv; gdp_growth_treasury.csv; fuel_prices_department.csv",
"refresh_method": "Stats SA/Treasury/DMPR manual downloads; World Bank API; independent vintage and freshness checks.",
"model_connection": "vehicles.py GDP new-sales path; no explicit fuel-price-to-mileage response.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 7 of 16. Gap IDs and original evidence references retained in notes.

## Slide 8: Test refinery availability and plant-specific scenarios
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Partner SA storyboard; open evidence register, 6 Oct 2026. Placeholder; no forecast or actual share inferred.
Complication | refinery closures, restart proposals and Sasol / Natref
EVIDENCE GAP | analysis specification, not a populated result
Refinery closures, availability and SAPREF proposal
Current output/yields/status; dated closures/restarts; SAPREF project evidence; 558 extra refinery rows unresolved.
Output: Unique country/year/scenario keys with source cells; actual/proposed distinction; per-refinery output tie and import sensitivity.
Secunda gas/MRG and Natref future
MRG timing and causal liquid-fuel effect; Natref future not established; partner propositions untested.
Output: Documented plant-level mechanism and dated scenario; no gas-to-liquid displacement inferred without evidence.
Evidence and implications
01 | Evidence status
These topics remain open. Existing calculations or public source leads do not establish calibration or closure.
02 | What is already available
Refinery assumptions and utilisation 2008-2050; provisional supply engine; duplicate-row diagnostics.
03 | What this page will resolve
A traceable petrol/diesel result with source, period, units and explicit unassessed residual. Jet stays separate.
Next steps | proposed owners
Manish: resolve duplicate refinery keys and source plant status. Henry: review the gas/liquid mechanism. Nigel: agree conditional refinery scenarios.
Notes: [
{
"id": "SA09",
"story": "Situation / Complication",
"question": "Refinery closures, availability and SAPREF proposal",
"existing_work": "Refinery assumptions and utilisation 2008-2050; provisional supply engine; duplicate-row diagnostics.",
"gap": "Current output/yields/status; dated closures/restarts; SAPREF project evidence; 558 extra refinery rows unresolved.",
"action": "Resolve repeated keys against original named ranges; build refinery-year status and output; treat proposals as conditional scenarios.",
"closure_evidence": "Unique country/year/scenario keys with source cells; actual/proposed distinction; per-refinery output tie and import sensitivity.",
"owner": "Manish; Nigel review; Henry challenge",
"timing": "W1 duplicates; W2-W3 scenarios",
"source_lead": "supply.yaml; refinery_production.csv; original workbook; primary operator/CEF/PetroSA reports",
"refresh_method": "Manual reports; refresh outages, restart, ownership or sanctioned-project changes.",
"model_connection": "src/lfm/model/supply/flows.py::compute_supply.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA10",
"story": "Complication",
"question": "Secunda gas/MRG and Natref future",
"existing_work": "Generic Sasol/Natref capacities, yields and utilisation; no plant-level gas-liquid linkage.",
"gap": "MRG timing and causal liquid-fuel effect; Natref future not established; partner propositions untested.",
"action": "Check latest primary Sasol disclosures; technical reviewer specifies mechanism before any fuel-output change.",
"closure_evidence": "Documented plant-level mechanism and dated scenario; no gas-to-liquid displacement inferred without evidence.",
"owner": "Manish sources; Henry technical review; Nigel scenarios",
"timing": "W2-W3",
"source_lead": "https://www.sasol.com/sasol-suite-reports ; 2026 Sasol SEC 20-F",
"refresh_method": "Manual quarterly/annual operating guidance and plant/gas changes.",
"model_connection": "No gas-to-fuel mechanism; utilisation/yield changes need explicit sourced scenario.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 8 of 16. Gap IDs and original evidence references retained in notes.

## Slide 9: Map conditional market access from Durban and Lesedi
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Existing appendix routes; illustrative candidate connections, not verified catchments. Natural Earth 1:50m.
Road-delivery accessibility | illustrative transport cost, R/litre
N
0
500 km
Durban
Lesedi*
≤0.75
0.75–1.25
1.25–1.75
1.75–2.25
>2.25
Unassessed
Example rate: R0.15/L dispatch + R0.002/L/km. Grey = unassessed.
Illustrative road cost only. Pipeline/rail access and commercial rights are not priced.
1
2
3
4
5
Transnet lease offers
1 Ladysmith | 2 Standerton
3 Kroonstad | 4 Bethlehem
5 Magdala*
Evidence and implications
01 | Darker cells mean lower example cost
The surface shows illustrative delivered road-transport cost in R/litre.
02 | Other modes remain context
Pipeline and rail costs, capacity and access are not evaluated in this surface.
03 | Physical proximity is insufficient
No operational or commercial catchment is validated by this illustration.
Next steps | proposed owners
Manish and Nigel: select the first destination and obtain dated route tariffs, quotations and access evidence.
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No operational service-area polygon or evidence-calibrated cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. The graduated surface is illustrative delivered road transport cost: R0.15/litre dispatch plus R0.002/litre/km times shortest schematic-road distance and straight-line terminal/grid connections. These are authored example parameters, not carrier quotes or validated cost evidence. 25 km cells; cost classes <=0.75, 0.75-1.25, 1.25-1.75, 1.75-2.25 and >2.25 R/litre. Cells more than 100 km from the sampled road geometry or without a connected path remain unassessed. Fuel purchase price, tax, storage and pipeline tariffs are excluded. Operational speeds, capacity, permissions and commercial access are not evaluated. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson
Transnet lease offers are context only, not cost-model origins or available supply.
Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
SCR delivery order: page 9 of 16. Gap IDs and original evidence references retained in notes.

## Slide 10: Compare routes on the same delivered-cost basis
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Partner SA storyboard; open evidence register, 6 Oct 2026. Placeholder; no forecast or actual share inferred.
Complication | Durban-NMPP-Lesedi, road / rail, Matola and Walvis Bay
EVIDENCE GAP | analysis specification, not a populated result
Durban-NMPP-Lesedi versus road/rail, Matola and Walvis Bay
Comparable route costs, NMPP capacity/tariff, actual rail service and cross-border feasibility.
Output: Comparable delivered R/litre with cost components, capacity/access limits and dated sources; no national optimisation claim.
Evidence required before quantification
Schematic appendix routes and illustrative Durban/Lesedi road-cost map.
No operational route allocation or delivered-cost engine.
Evidence and implications
01 | Evidence status
These topics remain open. Existing calculations or public source leads do not establish calibration or closure.
02 | What is already available
Schematic appendix routes and illustrative Durban/Lesedi road-cost map.
03 | What this page will resolve
A traceable petrol/diesel result with source, period, units and explicit unassessed residual. Jet stays separate.
Next steps | proposed owners
Nigel: choose the first product and customer destination. Manish: compare dated route costs, capacity and access on the same R/litre basis. Henry reviews.
Notes: [
{
"id": "SA11",
"story": "Complication",
"question": "Durban-NMPP-Lesedi versus road/rail, Matola and Walvis Bay",
"existing_work": "Schematic appendix routes and illustrative Durban/Lesedi road-cost map.",
"gap": "Comparable route costs, NMPP capacity/tariff, actual rail service and cross-border feasibility.",
"action": "Choose first product/customer destination; compare full handling/transport/transfer cost, border/FX where relevant, same period and basis.",
"closure_evidence": "Comparable delivered R/litre with cost components, capacity/access limits and dated sources; no national optimisation claim.",
"owner": "Manish evidence; Nigel corridor choice; Henry review",
"timing": "W1 comparison contract; W2-W4 first route",
"source_lead": "Client tariffs/quotes; current pipeline, port, road/rail and border operator evidence",
"refresh_method": "Manual published tariffs and dated quotes; tariff-year, FX and access refresh.",
"model_connection": "No operational route allocation or delivered-cost engine.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 10 of 16. Gap IDs and original evidence references retained in notes.

## Slide 11: Separate demand, accessible volume and Vopak flows
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Illustrative CSVs and road transport rates; no actual Vopak throughput or quoted transport costs supplied.
Illustrative road cost (R/litre) and market volumes
N
0
500 km
Durban
Lesedi*
Inland market | illustrative
Demand 10.0 | envelope 6.0
Current 2.0 | candidate 4.0
Eastern/coastal | illustrative
Demand 4.5 | envelope 2.5
Current 1.0 | candidate 1.5
≤0.75
0.75–1.25
1.25–1.75
1.75–2.25
>2.25
Unassessed
Receipts 2.8 + 2.0 − transfer 1.8 = unique demand 3.0
Example rates: R0.15/L + R0.002/L/km. Grey = unassessed. Volumes: bn L/year.
1
2
3
4
5
Transnet lease offers
1 Ladysmith | 2 Standerton
3 Kroonstad | 4 Bethlehem
5 Magdala*
Evidence and implications
01 | Balance arithmetic is illustrative
Example demand 21.0 less domestic production 7.0 gives imports 14.0, before exports and stocks.
02 | Transfers count once
Example Durban receipts 2.8 plus Lesedi receipts 2.0 less shared transfer 1.8 gives unique served demand 3.0.
03 | Candidate volume is conditional
The example envelope is 8.5 and additional candidate volume 5.5; neither is forecast capture.
Next steps | proposed owners
Nigel: request client flows. Manish: replace examples with matched-year product and destination records.
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No operational service-area polygon or evidence-calibrated cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. The graduated surface is illustrative delivered road transport cost: R0.15/litre dispatch plus R0.002/litre/km times shortest schematic-road distance and straight-line terminal/grid connections. These are authored example parameters, not carrier quotes or validated cost evidence. 25 km cells; cost classes <=0.75, 0.75-1.25, 1.25-1.75, 1.75-2.25 and >2.25 R/litre. Cells more than 100 km from the sampled road geometry or without a connected path remain unassessed. Fuel purchase price, tax, storage and pipeline tariffs are excluded. Operational speeds, capacity, permissions and commercial access are not evaluated. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson
Transnet lease offers are context only, not cost-model origins or available supply.
Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
SCR delivery order: page 11 of 16. Gap IDs and original evidence references retained in notes.

## Slide 12: Size each regional market and locate competing storage
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: DMPR 2022 provincial petrol/diesel sales; public operator sources [1-7], checked 6 Oct 2026. Share not established.
All four regions | reported 2022 demand, bn litres/year
Regional competitor evidence
National total 21.90 bn L | petrol + diesel; jet excluded
Region / provinces
Reported demand
Vopak
served
Additional
contestable
0
4
8
12
Eastern coast
EC/KZN
6.02
Not
established
Not
established
Inland
GP/FS/LP/MP/NW
11.50
Not
established
Not
established
Western coast
WC
3.93
Not
established
Not
established
Other
Northern Cape
0.45
Not
established
Not
established
To calculate share: unique Vopak customer deliveries / same-year regional demand.
Contestable demand needs route cost, compatible tanks, contracts and switching evidence.
Count Durban-Lesedi transfers once. Region boundaries are working groupings, not catchments.
01 Eastern coast
Vopak: Durban [1]. Bidvest: Durban and Richards Bay [2]; mixed-product capacity.
Transnet: Ladysmith lease tanks [7].
02 Inland
Vopak: Lesedi [1]. Bidvest: Isando [2].
Sasol: Alrode, Pretoria West, Waltloo, Sasolburg [6]. Transnet: Tarlton / Jameson Park + four lease sites [7].
03 Western coast
Burgan Cape: Cape Town petrol/diesel terminal [3]. Confirm current tank availability and customer access.
04 Other / Northern Cape
Operator coverage incomplete. Check Shell site notices [4] and NERSA licences/access records [5].
[1] Vopak
[2] Bidvest
[3] Burgan
[4] Shell
[5] NERSA
[6] Sasol
[7] Transnet
Notes: Regional demand uses reported 2022 petrol/diesel sales, aggregated from all four quarters for nine provinces. Historical sales are a demand proxy, not current terminal catchments. No actual Vopak deliveries or contestable customer volumes were supplied for any region. No share percentage is calculated or imputed; unknown is not zero. The earlier illustrative 22.2/20.0% shares have been removed from this page. Other operators are potential competing or complementary storage providers, not confirmed direct competitors for every customer. Footprint is a starting inventory, not exhaustive. Storage capacities are stocks, not deliveries, and may include ineligible products. Obtain matched-year unique Vopak deliveries, customer destinations, transfer reconciliation, route costs, product-compatible capacity and contracts before calculating shares. Owner Manish; Nigel review. Refresh the source when a later complete provincial year is available. Sales file: C:\Users\ITafr\Desktop\Insights\liquid_fuels_model\assumptions\2026\timeseries\fuel_sales_department_by_province_quarterly.csv; SHA256 aec82481b33f70429b6b8e7c9c02767d62a6e8c7bf6bda09e21123a5bc56c9d6; received workbooks: ['2022-Quarter4-Magisterial-Districts-data.xlsx']. Regional totals (bn litres): {'Eastern coastal': 6.019977323334999, 'Inland': 11.499633855183989, 'Western coastal': 3.9307750071499967, 'Other / Northern Cape': 0.4518100489230001}.
Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
[1] Vopak: https://www.vopak.com/system/files/Vopak_Annual_Report_2025.pdf | 2025 reporting year | Not matched petrol/diesel terminal throughput
[2] Bidvest Tank Terminals: https://www.bidtanks.com/pages/1562/about-us | Publication date not stated | Site capacities imply 955603 m3 versus homepage 868000 m3; includes non-petrol/diesel products
[3] VTTI Burgan Cape Terminal: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; download published 2025-06-25 | Storage stock not throughput; available-capacity notice needs period confirmation
[4] Shell: https://www.shell.co.za/motorists/shell-fuels/fuel-storage-facilities.html | Publication date not stated | Does not establish current independent terminal capacity or market share
[5] NERSA: https://www.nersa.org.za/petroleum-pipelines/third-party-access | Index entries dated 2020-09-25 | Historical mechanisms are not current contracted customer volumes or a complete competitor census
[6] Sasol: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Notice period ends March 2026; current access and site ownership need confirmation
[7] Transnet Pipelines: https://www.transnet.net/TPL-Leasing-Opportunities | 2026-10-05 RFPs; manual commencement 2024-09-01 | Lease assets are not available operating supply; refurbishment licensing and award conditional; unknown capacity at Bethlehem/Magdala
SCR delivery order: page 12 of 16. Gap IDs and original evidence references retained in notes.

## Slide 13: Establish actual share and additional contestable demand
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Partner SA storyboard; open evidence register, 6 Oct 2026. Placeholder; no forecast or actual share inferred.
Resolution | unique deliveries, reachable customers and commercial access
EVIDENCE GAP | analysis specification, not a populated result
Vopak market share at Durban and Lesedi
Unique customer deliveries, receipts, shared transfers, destinations and matched period.
Output: Separate terminal throughput and unique served-demand shares; matched-year/product denominator; traceable records, no capacity-as-share.
Additional commercially contestable market
Usable product-compatible tanks, spare routes, contracts, switching, customer overlap and Northern Cape inventory.
Output: Accessible demand by product/region/period; explicit assumptions and unassessed residual; competitors volume is not automatically capturable.
Evidence and implications
01 | Evidence status
These topics remain open. Existing calculations or public source leads do not establish calibration or closure.
02 | What is already available
Sourced regional sales p12; published capacity p14; illustrative transfer arithmetic p11.
03 | What this page will resolve
A traceable petrol/diesel result with source, period, units and explicit unassessed residual. Jet stays separate.
Next steps | proposed owners
Nigel: request client flow and destination records. Manish: reconcile transfers, calculate unique served demand, then test additional customer access and competing storage.
Notes: [
{
"id": "SA12",
"story": "Resolution",
"question": "Vopak market share at Durban and Lesedi",
"existing_work": "Sourced regional sales p12; published capacity p14; illustrative transfer arithmetic p11.",
"gap": "Unique customer deliveries, receipts, shared transfers, destinations and matched period.",
"action": "Nigel requests client flow extract; Manish reconciles receipt/transfer/final-delivery records and counts final demand once.",
"closure_evidence": "Separate terminal throughput and unique served-demand shares; matched-year/product denominator; traceable records, no capacity-as-share.",
"owner": "Nigel client request; Manish reconciliation",
"timing": "W1 request/schema; W2+ on receipt",
"source_lead": "Vopak operational/customer data; public unique-throughput data not established",
"refresh_method": "Client-approved monthly/annual extract with product/destination coverage and transfer IDs.",
"model_connection": "Current p6 flow volumes illustrative; future shared flow contract.",
"priority": "P0",
"status": "Open; existing evidence does not establish closure"
},
{
"id": "SA13",
"story": "Resolution",
"question": "Additional commercially contestable market",
"existing_work": "Competitor footprint and partial published storage; lease sites explicitly conditional.",
"gap": "Usable product-compatible tanks, spare routes, contracts, switching, customer overlap and Northern Cape inventory.",
"action": "Combine customer destinations with evidenced routes and rights; separate physical reach, commercial envelope and potential capture.",
"closure_evidence": "Accessible demand by product/region/period; explicit assumptions and unassessed residual; competitors volume is not automatically capturable.",
"owner": "Manish evidence; Nigel commercial review",
"timing": "W2-W4",
"source_lead": "Storage/competitor CSVs; NERSA licences; client contracts and operator notices",
"refresh_method": "Manual licences/notices; refresh contractual period, site changes and lease milestones.",
"model_connection": "No validated commercial customer-flow allocation.",
"priority": "P1",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 13 of 16. Gap IDs and original evidence references retained in notes.

## Slide 14: Compare published storage capacity by location
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Vopak; Bidvest; VTTI Burgan Cape; Transnet lease RFPs (5 Oct 2026), pp. 2-3. Checked 6 Oct 2026.
Published storage by location | thousand m³; mixed capacity bases
One shared scale for every location
0
200
400
600
800
Durban
799.55
Richards Bay
483.80
Lesedi
140.00
Cape Town
122.00
Isando
32.50
Ladysmith*
8.54
Kroonstad
3.30
Standerton
2.35
Vopak
Bidvest
Burgan Cape
Transnet (lease)
Small lease bars reflect smaller tank volumes; they are not operating supply.
*Ladysmith excludes 0.474 intermixture. Unquantified: Bethlehem, Magdala, Sasol, Tarlton, Jameson Park.
Evidence and implications
01 | Capacity is a stock
Published tank volumes are not annual fuel deliveries or market share.
02 | The inventory is partial
Missing capacities are unknown, rather than zero; mixed product scopes limit comparison.
03 | Leases are conditional
Transnet lease tanks are not counted as currently available operating supply.
Next steps | proposed owners
Manish: verify product compatibility, capacity basis and operating status. Nigel: confirm usable client capacity.
Notes: Storage footprint is a public-evidence starting inventory, not a complete census. Coordinates are approximate except Tarlton and five Transnet RFP briefing coordinates. Lease symbols indicate offers, not operating assets. Magdala RFP location narrative is inconsistent; verify independently. Symbols do not encode capacity. Lesedi and Transnet Jameson Park are distinct assets represented by the same approximate area; the national map cannot separate their actual boundaries. Capacity is a stock, not throughput. Mixed-product tanks cannot establish petrol/diesel share.
V1 Vopak / Durban: https://www.vopak.com/terminals/vopak-terminal-durban | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current available petrol/diesel capacity unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
V2 Vopak / Lesedi: https://www.vopak.com/terminals/vopak-terminal-lesedi | Terminal page publication date not stated; checked 2026-10-06 | Operator terminal page publishes cbm capacity; independent usable-capacity review pending | Current contracts and throughput unknown | owner Manish / Nigel review | next: Confirm usable petrol/diesel capacity product split and unique customer deliveries
B1 Bidvest Tank Terminals / Durban: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator lists Island View and Maydon Wharf sites | Capacity scope and total-vintage discrepancy; no access assumed | owner Manish / Nigel review | next: Split sites and products; reconcile total against homepage 868000 m3
B2 Bidvest Tank Terminals / Richards Bay: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | Includes gases; no petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Confirm tank-level eligible fuel scope and present ownership/access
B3 Bidvest Tank Terminals / Isando: https://www.bidtanks.com/pages/1562/about-us | Page publication date not stated | Operator site listing | No petrol/diesel capacity or access assumed | owner Manish / Nigel review | next: Verify exact terminal location and product mix
S1 Sasol / Alrode: https://sasol.com/our-businesses/energy | Page date not stated; linked notice reporting year 2025/26 | Operator Energy locations page | Notice ends March 2026; current access and joint ownership require confirmation | owner Manish / Nigel review | next: Refresh expired capacity notice and confirm site/operator ownership
S2 Sasol / Pretoria West: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S3 Sasol / Waltloo: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Available capacity and access unknown | owner Manish / Nigel review | next: Obtain licence exact coordinates and product-specific usable capacity
S4 Sasol / Sasolburg: https://sasol.com/our-businesses/energy | Page publication date not stated | Operator Energy locations page | Not treated as independent merchant terminal capacity | owner Manish / Nigel review | next: Separate refinery production from logistics and usable storage assets
T1 Transnet Pipelines / Tarlton: https://transnetetenders.azurewebsites.net/Home/TenderDetails?Id=70943 | 2025-04-16 tender publication | 2025 facility tender; 2024 manual documents delivery and reprocessing | No current spare capacity or open merchant access inferred | owner Manish / Nigel review | next: Confirm present operation usable tanks and access/tariff conditions
T2 Transnet Pipelines / Jameson Park: https://www.transnet.net/getFile.ashx?id=5330 | 2024-09-01 commencement; pp 19-20 and 62 | 2024 Shippers Manual names terminal and accumulation function | Separate asset from Vopak Lesedi; available capacity unknown | owner Manish / Nigel review | next: Geocode separately from Lesedi and verify accumulation tanks
G1 VTTI Burgan Cape Terminal / Cape Town: https://www.vtti.com/location/cape-town-south-africa-bct/ | Page date not stated; notice published 2025-06-25 | Operator terminal page | 2025-2026 availability notice requires current-period confirmation | owner Manish / Nigel review | next: Verify current tank availability routes and customer overlap
X1 Transnet Pipelines / Ladysmith: https://www.transnet.net/getFile.ashx?id=30047 | 2026-10-05 | Stranded tanks out of service since March 2018; no NMPP link or existing road/rail decanting system | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X2 Transnet Pipelines / Standerton: https://www.transnet.net/getFile.ashx?id=30045 | 2026-10-05 | Stranded after DWP decommissioning; lease proposal requires operational and regulatory readiness | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X3 Transnet Pipelines / Kroonstad: https://www.transnet.net/getFile.ashx?id=30044 | 2026-10-05 | Isolated after pipeline service ended; reactivation requires receipt/dispatch improvements and storage licence | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X4 Transnet Pipelines / Bethlehem: https://www.transnet.net/getFile.ashx?id=30048 | 2026-10-05 | Stranded after DJP decommissioning; storage licence and receipt/dispatch improvements required | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
X5 Transnet Pipelines / Magdala: https://www.transnet.net/getFile.ashx?id=30046 | 2026-10-05 | Stranded after DJP decommissioning; RFP location narrative conflicts; briefing coordinate retained | Lease opportunity only; not available operating capacity or model supply | owner Manish / Nigel review | next: Manish: verify tank condition, product eligibility, NERSA licence, lease award and delivered cost before activation; refresh at 2026-12-04 RFP close or earlier amendment
All eight locations use one linear axis, 0-850 thousand m3; no enlarged inset, axis break or minimum visual bar width. Location/value labels all use 12pt; ticks and legend 11pt. Gross stocks and RFP-stated lease tanks are not like-for-like usable operating capacity; no national total is inferred. Ladysmith: 8540 m3 petrol/diesel working, excluding 474 m3 intermixture; total working 9014 m3. Standerton: (1350000+220000+783000)/1000=2353 m3, basis unspecified. Kroonstad: approximately 3300 m3, basis unspecified. Bethlehem/Magdala petroleum storage is unquantified. Lease offers are excluded from operating supply and cost-model origins. Primary RFPs retained under external/data/raw/transnet_leasing_20261006/. https://www.transnet.net/TPL-Leasing-Opportunities
SCR delivery order: page 14 of 16. Gap IDs and original evidence references retained in notes.

## Slide 15: Gate investment on evidenced incremental customer flows
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Partner SA storyboard; open evidence register, 6 Oct 2026. Placeholder; no forecast or actual share inferred.
Resolution | optional service and investment assessment
EVIDENCE GAP | analysis specification, not a populated result
New storage and investment scope
Incremental accessible flows, turnover/peak inventory, product compatibility, cost and commercial return criteria.
Output: Throughput-to-usable-stock bridge with seasonality, inventory days and dispatch limits; downside sensitivity; no investment claim from import deficit alone.
Evidence required before quantification
Partial gross/lease stocks, without client handling/inventory profile.
Detailed service sizing deferred; infrastructure secondary to fuel integration.
Evidence and implications
01 | Evidence status
These topics remain open. Existing calculations or public source leads do not establish calibration or closure.
02 | What is already available
Partial gross/lease stocks, without client handling/inventory profile.
03 | What this page will resolve
A traceable petrol/diesel result with source, period, units and explicit unassessed residual. Jet stays separate.
Next steps | proposed owners
Nigel: decide whether to prioritise investment analysis after the flow case. Manish and Henry: bridge incremental flows to usable stock and service constraints.
Notes: [
{
"id": "SA14",
"story": "Resolution",
"question": "New storage and investment scope",
"existing_work": "Partial gross/lease stocks, without client handling/inventory profile.",
"gap": "Incremental accessible flows, turnover/peak inventory, product compatibility, cost and commercial return criteria.",
"action": "Establish flow/access case first; then test service requirements and a separately scoped investment case.",
"closure_evidence": "Throughput-to-usable-stock bridge with seasonality, inventory days and dispatch limits; downside sensitivity; no investment claim from import deficit alone.",
"owner": "Nigel commercial gate; Manish; Henry review",
"timing": "W4-W6 only if prioritised",
"source_lead": "Client service/stock profiles and scoped cost evidence",
"refresh_method": "Manual client data; refresh on demand/access case changes.",
"model_connection": "Detailed service sizing deferred; infrastructure secondary to fuel integration.",
"priority": "P2",
"status": "Open; existing evidence does not establish closure"
}
]
SCR delivery order: page 15 of 16. Gap IDs and original evidence references retained in notes.

## Slide 16
Agree priorities
and next steps
Confirm demand, routes and access
6 October 2026
Internal working discussion
Photo source: Royal Vopak | Terminal Lesedi | vopak.com
Notes: Source note: Closing cover photograph: Royal Vopak, Terminal Lesedi. https://www.vopak.com/terminals/vopak-terminal-lesedi
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 16 of 16. Gap IDs and original evidence references retained in notes.