## Slide 1
South Africa
liquid fuels
market outlook
Demand, supply and routes — implications for Vopak
Durban and Lesedi | Market-sizing framework
14 October 2026
Planning estimates and illustrative capture. Customer access and usable capacity remain to be established.
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: South Africa fuel market outlook. Sources and assumptions are stated on the analytical pages. Cover photograph: Royal Vopak, Terminal Durban.

## Slide 2: In 2025 about 10bn litres of local production and 16.7bn litres of imports supplied a 25bn-litre market
Production: Sasol and Glencore reports, analytical workbook v02 shares (p10). Imports and exports: SARS customs, calendar 2025, litres. Consumption = production + imports − exports; stock change assumed nil. Levy: Road Accident Fund annual report 2024/25, gross levies at 218c a litre.
Strictly Confidential
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Billion litres | calendar 2025E
Supply: 10.2bn L estimated production + 16.7bn L recorded imports. Uses: 1.5bn L recorded exports, leaving 25.4bn L consumed: petrol 9.3, diesel 16.1. Consumption is production plus imports less exports. It is 4.4bn L above the earlier estimate from Department sales (21.0), almost all in diesel. Cross-check: the road-fuel levy was charged on 24.4bn L in the year to March 2025.
Imports meet about 66% of national petrol and diesel consumption.
2025E petrol and diesel balance
Recorded trade, estimated production
Chart: 
| Supply | Uses
Production | 10.2259 | 0
Imports | 16.7022 | 0
Consumption | 0 | 25.3796
Exports | 0 | 1.5485
Notes: Department national sales; SARS 2025 trade; analytical workbook v02. 2025 demand is estimated; 5.8bn L production is a planning assumption. Gross import need includes exports and assumes no stock change.
Figures reused from South Africa market story v37; no new model assumptions.

## Slide 3: Changes in demand, domestic supply and import routes could reduce flows through Durban
Demand baseline: p4. Driver evidence: pp5–11. Sizing: pp12–14. Drivers and outlook: pp15–17. Stats SA; Eskom; Sasol; Glencore; Galp; Petromoc; naamsa. Scenario outcomes are separate from observed evidence.
Strictly Confidential
Complication | Driver | What changes for fuel demand and Durban flows
Baseline | Baseline demand ¦ p4 | About 25.4bn-litre market in 2025 (production plus imports less exports); petrol/diesel history and the end-use split establish the starting point.
1 Demand | Sector activity ¦ p5 | Mining, manufacturing and agriculture drive equipment and freight demand along different growth paths.
 | Eskom recovery ¦ p6 | Reliable electricity reduces peaking and backup diesel at utilities, mines, factories and farms.
 | Road-to-rail ¦ p7 | Freight shifted from trucks reduces road diesel use; net savings depend on rail traction.
 | Vehicle sales p8 ¦ Efficiency p9 | Lower fuel consumption per kilometre reduces demand at a given level of road activity.
2 Domestic supply | Refinery history p10 ¦ Outlook p16 | Higher production displaces imports; outages or lower output increase import dependence.
3 Import routes | Ports and inland connections ¦ p11 | Matola competes for inland supply. Assess Walvis Bay, pipeline access and delivered cost; Walvis Bay diversion is unquantified.
4 Outlook | Sizing pp12–14 ¦ Drivers and outlook pp15–17 | Base case 2030, market of interest: demand 18.8bn L, of which 12.5bn L brought in. Illustrative capture 2.4bn L until Vopak’s throughput is supplied.
A large national import market does not automatically translate into growth for Vopak.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Notes: Stats SA sector activity and freight; Eskom Integrated Report 2025 p141; Sasol and Glencore production disclosures; Galp and Petromoc infrastructure disclosures. Detailed evidence: South Africa story v37 pp7–11.
Figures reused from South Africa market story v37; no new model assumptions.

## Slide 4: South Africa’s fuel market is about 25bn litres, dominated by road demand
Department annual sales, 2013–2021 (2022–2023 sales were 21.9 and 21.9bn L). 2022–2025: production (p10) + SARS imports − SARS exports, stock change nil. Demand by use: analytical workbook v02, Segments, which sums to its sales-based totals; the difference is shown as not allocated.
Strictly Confidential
Billion litres | to 2021 Department sales; 2022E–2025E production + imports − exports
Billion litres | legend shows 2025E values
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022E | 2023E | 2024E | 2025E
Petrol | 11.4399 | 10.8902 | 11.4757 | 11.4623 | 11.1741 | 11.1416 | 10.7732 | 8.7615 | 9.3016 | 8.7566 | 9.2049 | 9.1197 | 9.2928
Diesel | 12.1413 | 12.615 | 13.5201 | 12.0824 | 12.1472 | 12.5387 | 12.9086 | 11.69 | 12.9458 | 14.1328 | 16.5636 | 14.9418 | 16.0868
Totals: 25.8, 24.1 and 25.4bn litres. Uses are allocated up to the earlier sales-based estimate; the rest, mostly diesel, is not yet allocated.
Demand was about 25.4bn litres in 2025: petrol 9.3, diesel 16.1. Road uses account for most of the allocated demand.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Petrol and diesel demand, 2013–2025E
Demand by use, 2023E–2025E
Chart: 
| 2023E | 2024E | 2025E
Petrol road 8.59 | 8.7658 | 8.6775 | 8.5901
Other petrol 0.27 | 0.27111 | 0.26838 | 0.26567
Freight diesel 4.82 | 4.8414 | 4.8653 | 4.8245
Other road diesel 1.61 | 1.6138 | 1.6218 | 1.6082
Mining 1.41 | 1.396 | 1.4037 | 1.4063
Agriculture 1.13 | 1.0553 | 0.96334 | 1.1312
Manufacturing 0.17 | 0.1679 | 0.16721 | 0.16508
Power 0.88 | 1.2779 | 1.5973 | 0.88432
Other diesel 2.11 | 2.5553 | 2.5165 | 2.1119
Not allocated 4.39 | 3.8241 | 1.9805 | 4.3922
Notes: Department annual sales, 2013–2023. Estimated 2024–2025: analytical workbook v02. The Department series is used consistently. Segment split: analytical workbook v02, Segments. Displayed figures rounded; other diesel remains unallocated.
Demand is estimated at 20.99bn litres in 2025; road uses account for most allocated demand.

## Slide 5: Agricultural fuel demand rebounds and power fuel use falls by about a third, while mining and manufacturing remain broadly flat
Stats SA mining/manufacturing indices and agriculture real GVA; mean 2018–2021 fuel intensity. Sector diesel values after 2021 are estimates. Road freight and other road diesel: assumed 75% / 25% split of road diesel. Power: Eskom fiscal-year fuel use and independent-producer turbines; any private backup sits in other diesel. The seven uses add to estimated diesel demand. Analytical workbook v02, Segments.
Strictly Confidential
Billion litres
Chart: 
| 2023E | 2024E | 2025E
Road freight | 4.8414 | 4.8653 | 4.8245
Power | 1.2779 | 1.5973 | 0.88432
Other diesel | 2.5553 | 2.5165 | 2.1119
Other road | 1.6138 | 1.6218 | 1.6082
Mining | 1.396 | 1.4037 | 1.4063
Agriculture | 1.0553 | 0.96334 | 1.1312
Manufacturing | 0.1679 | 0.16721 | 0.16508
Road freight: 4.84 → 4.82bn L Power: 1.28 → 0.88bn L Agriculture: 1.06 → 1.13bn L Mining: 1.40 → 1.41bn L; manufacturing about 0.17bn L All uses are estimates. Road freight is an assumed 75% of road diesel; manufacturing is an industry residual, not a complete census.
Sector activity produces different demand paths; applying one GDP growth rate would hide these differences.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Estimated sector diesel demand
Estimated diesel use
Notes: Stats SA mining/manufacturing indices and agriculture real GVA; mean 2018–2021 fuel intensity. Sector diesel values after 2021 are estimates.
Sector activity produces different demand paths; applying one GDP growth rate would hide these differences.

## Slide 6: Eskom’s fuel use fell by 40% in FY2025 and a further 62% in FY2026 as electricity supply improved
Eskom Integrated Report 2025, p141. FY2026: Minister of Electricity and Energy, July 2026, as reported by MyBroadband, 25 August 2026; not in Eskom’s 2026 report. April–October 2026: Eskom statement, 9 October 2026. Fiscal years end in March. Reported series includes diesel and kerosene; private backup consumption is outside this series. Analytical workbook v02, Segments: IPP conversion.
Strictly Confidential
Billion litres
Chart: 
| FY2023 | FY2024 | FY2025 | FY2026
Eskom diesel and kerosene | 0.9375 | 1.1295 | 0.6791 | 0.2566
Eskom: 1.130bn L in FY2024 → 0.679bn L in FY2025 → 0.257bn L in FY2026 (diesel + kerosene).
1 April to 8 October 2026: turbine output 152 GWh, about 85% below a year earlier; diesel spend R1.16bn against R5.98bn.
2025 power-station estimate: 0.88bn L (Eskom and independent-producer turbines).
IPP conversion and fiscal-year proxies are estimates; private use is not measured by Eskom.
Improved electricity supply reduces peaking and backup fuel use; private backup use is not measured.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Eskom diesel and kerosene use
Power fuel use
Notes: Eskom Integrated Report 2025, p141. Fiscal years end in March. Reported series includes diesel and kerosene; private backup consumption is outside this series. Analytical workbook v02, Segments: IPP conversion and private-backup assumptions.
Improved electricity supply reduces peaking and backup fuel use; the private-backup contribution remains estimated.

## Slide 7: Even at Transnet’s 2030 rail target, road freight still grows; the shift to rail saves about 0.3bn litres of diesel a year
Stats SA P7162 (Dec 2025 p7; Jul 2026), all freight; * 2026 = Jan–Jul × 12/7. 2030: freight grows with real GDP (Treasury, 2026 Budget Review, Table 2.2: 1.6–2.0% a year; 2.0% held for 2029–30); rail = Transnet target (chief executive, Apr and Sep 2026); road = balance. Road: 4.82bn L freight diesel, 2025 (workbook v02; authored 75% of road diesel) ÷ road tonnes. Tonnes, not tonne-km.
Strictly Confidential
Million tonnes | * 2026 annualised from January–July | hatched 2030: rail = Transnet target, road = balance if freight grows with GDP
Chart: 
| 2024 | 2025 | 2026* | 2030
Road, million tonnes | 979.798 | 976.468 | 973.764 | 1006.4507
Rail, million tonnes | 160.745 | 168.263 | 173.3914 | 250
Rail: 168.3m tonnes in 2025, 173.4m in 2026* (January–July +5.3%). Reaching 250m by 2030 needs 8.2% a year.
If total freight grows with GDP, it reaches 1,256m tonnes in 2030. With rail at 250m, road is 1,006m: 3% above 2025.
Against 2025 mode shares, 65m tonnes move to rail. Road freight uses about 4.9 litres of diesel a tonne, so road saves 0.32bn L.
Rail growth slows road freight rather than shrinking it: diesel saved is about 0.3bn litres a year by 2030.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Reported road and rail freight
2030 freight and diesel
Notes: Stats SA P7162 December 2025 p7; all reported freight. Analytical workbook v02, Evidence.
Road remains the dominant freight mode; sustained rail recovery could change the diesel required to move goods.

## Slide 8: Hybrids dominate electrified new-vehicle sales; fleet fuel savings emerge as vehicles turn over
naamsa new energy vehicle sales, 2019–2025 (Quarterly Review of Business Conditions: Q3 2024 for 2019; Q2 2026 for 2020–2025); master workbook Vehicle history. 2026: naamsa Q1 and Q2 2026 reviews; naamsa notes new brands began reporting in 2026. Petrol: Department price history, 95 octane inland retail; highest monthly price in each year, 2026 to October.
Strictly Confidential
Vehicles sold | line: highest petrol price in the year, R/litre (right axis) | 2026 sales: annualised (January–June )
Electrified sales rose from 407 in 2019 to 16,716 in 2025. First half of 2026: 13,196, against 7,162 a year earlier (26,392 annualised).
The highest petrol price in each year rose from R16.76 a litre in 2019 to R26.74 in 2022, eased to R22.41 in 2025 and reached R30.25 in October 2026.
New sales are not fleet penetration. Efficiency and mileage must be modelled separately.
Electrified sales are growing fast but are still a small share of new vehicles; new sales alone do not show fuel saved.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Electrified vehicle sales and the petrol price, 2019–2026
Different fuel-use effects
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 annualised
BEV | 154 | 92 | 218 | 502 | 929 | 1257 | 1088 | 3794
Plug-in hybrid | 72 | 77 | 51 | 122 | 368 | 738 | 2810 | 9246
Conventional hybrid | 181 | 155 | 627 | 4070 | 6485 | 13616 | 12818 | 13352
Peak petrol, R/litre | 16.76 | 16.16 | 20.29 | 26.74 | 25.68 | 25.49 | 22.41 | 30.25
Notes: naamsa all-market sales 2025; master workbook Vehicle history S31:S36; evidence retained in market story v27 p11. Analytical workbook v02: efficiency is a planning assumption; avoid double-counting hybrid savings.
The model’s fuel-efficiency path is a planning assumption; new-vehicle sales alone do not quantify national fuel savings.

## Slide 9: Each year South Africa’s vehicles use about 0.5–0.8% less petrol and 0.4–0.7% less diesel per km
Chart: US EPA and Department of Energy, fueleconomy.gov vehicle file (downloaded 14 October 2026); combined label MPG converted per vehicle at 235.215 ÷ MPG; conventional petrol (no hybrids, flex-fuel, plug-ins) and diesel; each year’s change measured within vehicle classes present in both years, chained back from the 2026 average; not sales-weighted; diesel rests on 1–9 classes a year. Text: IEA/GFEI WP15 (2017); IEA (Dec 2021); eNaTIS 2022–25; Lightstone; Stone et al. (2018).
Strictly Confidential
Litres per 100 km of new vehicles, at the 2026 vehicle mix | US model years | same vehicle classes year to year
New vehicles use about 1% less fuel each year: since 2006, petrol from 13.6 to 11.2 litres per 100 km and diesel from 12.5 to 10.3 (US, chart). In South Africa, new light vehicles went from 8.8 to 7.4 litres, 2005–2019.
Fleet: new cars and LCVs are 4.4% of the fleet each year and 2.5% are scrapped (2023–25). Average age is 10.5 years.
So the whole fleet improves about half as fast as new vehicles. Petrol: 0.5–0.8% a year, depending on whether new-vehicle gains continued after 2019.
Diesel: 0.4–0.7% a year. Bakkies, SUVs and cars use 36% of road diesel (0.4–0.6%); trucks, buses and taxis 64% (0.4–0.75%). New diesels use 8.5% less than the fleet average.
New vehicles improve about 1% a year, but old vehicles stay on the road for a long time, so the fleet improves only about half as fast.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
New vehicles use 17% less fuel than in 2006: about 1% a year
From new vehicles to the whole fleet
Chart: 
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Petrol | 13.605 | 13.467 | 13.533 | 13.224 | 12.919 | 12.632 | 12.351 | 11.952 | 11.9 | 11.689 | 11.549 | 11.486 | 11.375 | 11.334 | 11.423 | 11.468 | 11.401 | 11.459 | 11.378 | 11.234 | 11.199
Diesel | 12.478 | 12.037 | 12.037 | 11.368 | 11.246 | 11.148 | 11.035 | 11.116 | 10.824 | 10.342 | 10.337 | 10.152 | 10.209 | 10.295 | 9.964 | 10.04 | 10.189 | 10.123 | 10.401 | 10.323 | 10.342
Notes: Analytical workbook v02: Driver bridge (Base), Assumptions (Base: efficiency). Effects are modelled, not observed savings. Efficiency applies to road fuel after activity growth; rail is applied afterwards. Do not add a separate EV saving to the same efficiency allowance.

## Slide 10: Three refineries produced about 10.2bn litres of petrol and diesel in 2025, half the 2014 level
Sasol production and sales metrics, years to June 2022–2025, p4 (Secunda total refined product; Natref production); Glencore annual reports 2023 p104, 2024 p85, 2025 p69 (Astron). Petrol and diesel shares and energy conversion: analytical workbook v02, Plant supply. Sasol’s years to June stand in for calendar years. 2014–2021: Department energy balances.
Strictly Confidential
Billion litres, petrol and diesel | estimated from operators’ reports | totals: 7.2, 10.3, 11.0, 10.2
10.2bn litres
Estimated from Sasol’s and Glencore’s reports; no national figure has been published since 2021. Reported combined production fell from 20.42bn L in 2014 to 11.67bn L in 2021. 2025: Secunda 3.9, Natref 2.4, Astron 3.9bn L; petrol 5.6, diesel 4.6.
How the estimates were calculated: Sasol’s reported fuels output for Secunda (chemicals already excluded) and Natref (scaled up from its 63.64% share), and Glencore’s reported output for Astron, converted to litres; then the share that is petrol and diesel: Secunda 90%, Natref 64%, Astron 80%. Astron was offline in 2022.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Estimated petrol and diesel production by refinery, 2022E–2025E
2025E production
Chart: 
| 2022E | 2023E | 2024E | 2025E
Secunda | 4.1782 | 4.2783 | 4.1639 | 3.9492
Natref | 3.0455 | 2.7715 | 2.8682 | 2.3687
Astron | 0 | 3.2493 | 3.9517 | 3.9079
Notes: Department energy balances 2014–2021; consolidated review workbook, DR01 national balance rows 8/17. Sasol FY2025/FY2026; Glencore 2024/2025. 2025: 5.8bn L planning assumption. Historical production ends in 2021; no interpolated observations.

## Slide 11: Durban lands almost all fuel for the market of interest; little comes in through Maputo, and exports to Botswana are falling
SARS customs, petrol and diesel, litres: imports by district office (offices add to the national total; Komatipoort is the Lebombo border post on the road from Maputo); exports by partner country. 2026 = January–August × 12/8. Records show where fuel is cleared, not where it is used. Base map: AIA board report, November 2025. Market of interest: p13.
Strictly Confidential
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Imports from Maputo
By road, cleared at Komatipoort | 0.09bn L in 2025
Chart: 
| 21 | 22 | 23 | 24 | 25 | 26*
Petrol | 0.039454 | 0.028806 | 0.00012542 | 0.0010096 | 0.0044165 | 0.0072506
Diesel | 0.20134 | 0.27416 | 0.25457 | 0.18582 | 0.082023 | 0.10627
Total | 0 | 0 | 0 | 0 | 0 | 0
Richards Bay
Imports | 0.7bn L in 2025
Chart: 
| 21 | 22 | 23 | 24 | 25 | 26*
Petrol | 0 | 0 | 0 | 0 | 0 | 0
Diesel | 0.23404 | 0.33132 | 0.32077 | 0.39078 | 0.65791 | 0.80341
Total | 0 | 0 | 0 | 0 | 0 | 0
Durban
Imports | 13.2bn L in 2025, 79% of SA
Chart: 
| 21 | 22 | 23 | 24 | 25 | 26*
Petrol | 2.4366 | 3.8827 | 4.1656 | 3.8047 | 4.229 | 3.8049
Diesel | 5.8349 | 7.8812 | 9.125 | 8.0329 | 8.9315 | 8.1966
Total | 0 | 0 | 0 | 0 | 0 | 0
Other SA ports
Mossel Bay, Gqeberha, East London | 1.3bn L in 2025
Chart: 
| 21 | 22 | 23 | 24 | 25 | 26*
Petrol | 0.10054 | 0.043438 | 0.083998 | 0.064029 | 0.034476 | 0.010151
Diesel | 1.1377 | 0.98171 | 1.7812 | 1.2249 | 1.2385 | 0.87386
Total | 0 | 0 | 0 | 0 | 0 | 0
Cape Town
Imports | 1.5bn L in 2025
Chart: 
| 21 | 22 | 23 | 24 | 25 | 26*
Petrol | 1.4319 | 1.5003 | 0.23305 | 0.13109 | 0.1856 | 0.50035
Diesel | 2.3507 | 2.4851 | 1.3876 | 0.95748 | 1.3354 | 1.1798
Total | 0 | 0 | 0 | 0 | 0 | 0
Exports to Botswana
1.05bn L in 2022 → 0.68 in 2025
Chart: 
| 21 | 22 | 23 | 24 | 25 | 26*
Petrol | 0.62104 | 0.56779 | 0.59844 | 0.50941 | 0.42406 | 0.35038
Diesel | 0.48076 | 0.48589 | 0.44779 | 0.28068 | 0.25296 | 0.22929
Total | 0 | 0 | 0 | 0 | 0 | 0
Market of interest
Gauteng, KZN, Mpumalanga, Free State, North West, Limpopo
18.2bn L used, 11.9bn L brought in, 2025E (p13)
Petrol
Diesel
Billion litres | 26* = 2026, annualised from January–August | each chart has its own scale
Durban landed 79% of South Africa’s imports in 2025; the NMPP pipeline carries it inland to Lesedi.
Maputo imports into South Africa come by road and are cleared at Komatipoort: down from 0.30bn L in 2022 to 0.09 in 2025.
Walvis Bay fuel is not recorded entering South Africa through Botswana or Namibia.
Botswana is buying less from South Africa: exports fell from 1.05bn L to 0.68.

## Slide 12: Durban and Lesedi market sizing and investment issue tree
Analytical workbook v02; SARS 2025; district sales 2022 grown to 2025; Transnet Pipelines FY2025. Production is estimated from operators’ reports; capture is illustrative. Shared Durban–Lesedi fuel is counted once. Historical catchments retain their stated years.
Strictly Confidential
1 NATIONAL DEMAND
2 SUPPLY AND DELIVERY
3 VOPAK OPPORTUNITY
4 INVESTMENT
National consumption 2025 estimate 25.4bn litres
Demand by product Petrol 9.3bn L Diesel 16.1bn L
Demand by use Road, mining, agriculture Manufacturing and power
Demand parameters
GDP and sectors
EVs, fleet, efficiency
Freight, prices, power
Gross imports, 2025
Petrol 4.45B L
Diesel 12.25B L
Domestic production 10.2bn L in 2025 Operators’ reports
Ports and alternatives Durban, Matola Assess Walvis Bay
Inland delivery
NMPP trunk line
Road and rail
Coastal demand
KZN, WC, EC
Port-adjacent markets
Inland demand
Gauteng and interior
Six inland provinces
Supply and route parameters
Refinery closures, restarts, gas
Delivered cost, routes, contracts
Port, pipeline, rail capacity
Market context
2025 Durban customs 13.16B L
Catchments and gateway overlap
Durban context
Imports 13.16B L
KZN need 5.04B L
Lesedi catchments
Inland 13.17B L
Net need 6.85B L
Conditional base capture
Total 2.38B L: Durban 1.01, Lesedi 1.37
20% of import requirement
Incremental opportunity
Needs existing throughput baseline
Access and commitments unverified
Additional capture
Customers, contracts
Competition
Existing assets
Tanks and turns
Receipt and dispatch
New investment
Volume, capex, returns
Alternatives, downside
Resolution
Vopak share by site
Scope for investment
2025 demand estimate
2025 estimates
2025 segment estimates
2025 gross 16.70B L
2025 estimate (p10)
2025 · Durban 13.2B L
FY25 use 5.46B L/yr
2022 · 10.0B L · proxy
2022 · 12.0B L · proxy
Gateway proxy; capture not observed
2025 · p13
2025 · p13
Illustrative capture
Pending · DR02/05
Pending · DR02/05
Pending · DR03
Pending · DR06
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Notes: Market-sizing issue tree reused from market-sizing v2000, slide 3. National demand/product estimates and production assumption aligned to analytical workbook v02. Provincial catchments retain 2022 source periods. Capture remains illustrative; Walvis Bay diversion unquantified.

## Slide 13: The market of interest used about 18.2bn litres in 2025, of which about 12bn litres had to be brought in
Department fuel sales by magisterial district, four quarters of 2022 (latest full year), grown to 2025 at national growth by product (2025 demand = production + imports − exports, p4). Market of interest as in the AIA board report of November 2025: Gauteng, Limpopo, North West, Free State, Mpumalanga, KwaZulu-Natal. Production: p10. Assumes Secunda and Natref output stays in the area. Sales are recorded where fuel is sold.
Strictly Confidential
Billion litres, 2025E | 2022 district shares applied to 2025 national demand | totals beside each name
By province | all 190 magisterial districts: pp21–22
Market of interest, 2025: 18.2bn L (72% of national 25.4): petrol 7.0, diesel 11.2. Gauteng and KwaZulu-Natal are 70%. Made inside the area: Secunda and Natref, 6.3bn L (petrol 3.7, diesel 2.6; p10). To be brought in: about 11.9bn L, petrol 3.3 and diesel 8.5, through Durban or other routes (p11). Method: each district's 2022 share of national sales, by product, applied to 2025 national demand (p4). On 2022 sales alone the area was 15.8bn L.
Local refineries cover about 35% of the market of interest; the other 65% must be imported or moved in.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Petrol and diesel demand in the market of interest, 2025E
From demand to import requirement
Chart: 
| Gauteng 7.7 | KwaZulu-Natal 5.0 | Mpumalanga 2.1 | Free State 1.6 | North West 1.2 | Limpopo 0.6
Petrol | 3.5719 | 1.5165 | 0.61946 | 0.59436 | 0.45342 | 0.27686
Diesel | 4.1478 | 3.5236 | 1.4483 | 0.98902 | 0.78415 | 0.2808

## Slide 14: How the national fuel market translates into Vopak’s addressable volume
Demand: production + imports − exports (p4); SARS customs imports, 2025; SARS customs, Durban office, 2025; Department district sales 2022 grown to 2025 (p13); market-sizing workbook. Bars are drawn to scale. Step 3 assumes Secunda and Natref output stays in the market of interest; Matola also supplies inland. Step 5: 146,000 m³ working fuel tanks (estimate) at Vopak’s stated target of 2–3 turns a month. Capture is an illustrative 20%, not a contracted share. Walvis Bay is a route to assess; no diversion volume is assigned.
Strictly Confidential
Step 5: Vopak’s Durban tanks handle about 3.5bn litres a year at two turns a month; volumes above that need new tanks.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Sizing step
Billion litres a year, 2025E
Basis
Petrol
Diesel
1 National demand
9.3
16.1
= 25.4
Petrol 9.3 and diesel 16.1: production plus imports less exports (p4).
2 Market of interest
7.0
11.2
= 18.2
Gauteng, KwaZulu-Natal, Mpumalanga, Free State, North West and Limpopo: 72% of national demand (p13).
3 Addressable market
3.3
8.5
= 11.9
Market of interest less Secunda and Natref (p13): KwaZulu-Natal 5.0, inland 6.8. National imports 16.7 (66% of demand); Durban lands 13.2 (79%).
4 Achievable capture
= 2.4 (petrol 0.7, diesel 1.7)
Illustrative 20% of step 3: 1.0 at Durban, 1.4 through Lesedi. Vopak’s actual share is not published.
Notes: Framework: analytical workbook v02 and market-sizing workbook. Gateway shares and customer access require validation. Walvis Bay is a route to assess; no diversion volume is assigned. Stock build increases import need; stock draw reduces it.
Figures reused from South Africa market story v37; no new model assumptions.

## Slide 15: Six drivers shape fuel demand: the economy, price, power, rail, electrified vehicles and efficiency
Stats SA (GDP; land transport survey P7162, July 2026 release); Department price history; Eskom Integrated Report 2025 and, for FY2026, the Minister of Electricity and Energy as reported by MyBroadband, 25 August 2026; naamsa quarterly reviews. Efficiency: US EPA and Department of Energy, fueleconomy.gov, like for like at the 2026 vehicle mix, as on p9. Detail: pp5–9.
Strictly Confidential
The economy lifts diesel demand; power recovery, rail, electrified vehicles and efficiency pull demand down.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
1 Economic activity
GDP, R trillion at constant 2015 prices
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
1 Economic activity | 3.9738 | 4.0997 | 4.198 | 4.3023 | 4.3631 | 4.4208 | 4.4502 | 4.5017 | 4.5718 | 4.5837 | 4.3009 | 4.5099 | 4.6027 | 4.6398 | 4.6646 | 4.7166
2 Petrol price
Rand a litre, annual average | 2026* = January–October
Chart: 
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026*
2 Petrol price | 11.5633 | 12.9217 | 13.8383 | 12.4133 | 12.5867 | 13.6233 | 15.4225 | 15.735 | 14.7492 | 17.56 | 22.7958 | 23.1358 | 23.1183 | 21.6567 | 24.805
3 Power recovery
Eskom diesel and kerosene, billion litres, years to March
Chart: 
| FY16 | FY17 | FY18 | FY19 | FY20 | FY21 | FY22 | FY23 | FY24 | FY25 | FY26
3 Power recovery | 1.2478 | 0.01 | 0.0378 | 0.385 | 0.4262 | 0.4587 | 0.5804 | 0.9375 | 1.1295 | 0.6791 | 0.2566
4 Road to rail
Rail freight, million tonnes | 2026* annualised from January–July
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026*
4 Road to rail | 181.156 | 193.782 | 205.428 | 211.402 | 219.982 | 219.026 | 215.012 | 225.228 | 216.542 | 214.03 | 190.267 | 177.155 | 155.913 | 160.1 | 160.745 | 168.259 | 173.3914
5 Electrified vehicles
New sales, all electrified types | 2026* = January–June × 2
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026*
5 Electrified vehicles | 407 | 324 | 896 | 4694 | 7782 | 15611 | 16716 | 26392
6 Vehicle efficiency
L/100 km, new vehicles (US, like for like): petrol (dark), diesel (light)
Chart: 
| 2006 | 2016 | 2026
Petrol | 13.605 | 13.467 | 13.533 | 13.224 | 12.919 | 12.632 | 12.351 | 11.952 | 11.9 | 11.689 | 11.549 | 11.486 | 11.375 | 11.334 | 11.423 | 11.468 | 11.401 | 11.459 | 11.378 | 11.234 | 11.199
Diesel | 12.478 | 12.037 | 12.037 | 11.368 | 11.246 | 11.148 | 11.035 | 11.116 | 10.824 | 10.342 | 10.337 | 10.152 | 10.209 | 10.295 | 9.964 | 10.04 | 10.189 | 10.123 | 10.401 | 10.323 | 10.342

## Slide 16: Demand in the market of interest reaches about 18.8bn litres by 2030 in the base case (17.6–20.2bn L)
History: Department sales to 2021; 2022E–2025E production + imports − exports (p4); market of interest at its 2022 district share by product (p13). Cases: 2025E uses from the analytical workbook v02 (Segments), scaled to the market of interest; drivers and sources on p19. Secunda and Natref held at 2025E output.
Strictly Confidential
Billion litres, market of interest | history to 2025E at 2022 district shares, then cases to 2030
Diesel
Petrol
Petrol, 2030: low 6.5bn L; base 6.9; high 7.4. In 2025E it is 7.0.
Diesel, 2030: low 11.2bn L; base 11.9; high 12.8. In 2025E it is 11.2.
To be brought in, 2030: low 11.3bn L; base 12.5; high 13.9, after Secunda and Natref (6.3bn L).
Petrol falls in 2026 as prices rise; the cases differ in GDP growth, petrol price, efficiency, rail, electric vehicles and peaker use (p19).
Demand grows slowly in the base case; diesel sets the range, from 11.2 to 12.8bn litres in 2030.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Market of interest: petrol and diesel demand, history and cases to 2030
2030 demand by case
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022E | 2023E | 2024E | 2025E | 2026 | 2027 | 2028 | 2029 | 2030
History | 8.6575 | 8.2415 | 8.6846 | 8.6744 | 8.4563 | 8.4317 | 8.1529 | 6.6305 | 7.0392 | 6.6268 | 6.9661 | 6.9016 | 7.0326
Low | 7.0326 | 6.8213 | 6.6857 | 6.5921 | 6.5205 | 6.4582
Base | 7.0326 | 6.856 | 6.7967 | 6.8058 | 6.8557 | 6.9297
High | 7.0326 | 6.8908 | 6.905 | 7.0174 | 7.1976 | 7.4298
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022E | 2023E | 2024E | 2025E | 2026 | 2027 | 2028 | 2029 | 2030
History | 8.4331 | 8.7622 | 9.3908 | 8.3922 | 8.4373 | 8.7092 | 8.9661 | 8.1196 | 8.9919 | 9.8164 | 11.5048 | 10.3783 | 11.1736
Low | 11.1736 | 11.1763 | 11.1791 | 11.1817 | 11.184 | 11.1854
Base | 11.1736 | 11.3126 | 11.4536 | 11.5965 | 11.7412 | 11.8874
High | 11.1736 | 11.4736 | 11.7812 | 12.0968 | 12.4203 | 12.7519
Notes: Restored from South Africa story v37; analytical workbook v02, Scenarios and Driver bridge. Gross imports = demand − domestic supply + fixed 2025 exports; zero stock change. 2025 production: 5.8bn L assumption. Restart volumes and timing are scenario assumptions.

## Slide 17: Substantial imports sustain the market, while customer capture determines Vopak’s expansion
Base case, pp16 and 19; market-sizing workbook and working-capacity assessment. Capture is illustrative. Contracted share, product balance and usable capacity remain to be established. Capture base: market-of-interest import requirement 2025, KwaZulu-Natal 5.0bn L and inland provinces 6.8bn L (p13).
Strictly Confidential
12.5bn L
2030 import requirement, market of interest
Base case: demand of 18.8bn litres less Secunda and Natref output (6.3bn litres, held at 2025E). Growth broadly offsets efficiency, rail, power and electric-vehicle reductions (p16).
2.4bn L
Illustrative capture, Durban and Lesedi
Assumes 20% of the 11.9bn litres the market of interest had to bring in, in 2025 (p13–14): 1.0bn litres at Durban and 1.4bn litres through Lesedi.
Illustrative share; no explicit deduction for Matola or Walvis Bay diversion.
Expansion follows
secured incremental flow
The illustrative flow fits the preliminary working-tank calculation.
Secure additional customer volumes, establish usable capacity, and identify the constraint that investment would solve.
Invest where secured additional volumes create a demonstrated capacity shortfall.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Notes: Analytical workbook v02 base scenario; market-sizing workbook and working-capacity assessment. Capture is illustrative; Lesedi is included within Durban flow. Contracted share, product balance and usable capacity remain to be established.
Figures reused from South Africa market story v37; no new model assumptions.

## Slide 18
Thank you
South Africa fuel market and Vopak opportunity
Discussion
14 October 2026
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: Closing discussion. Cover photograph: Royal Vopak, Terminal Durban.

## Slide 19: Appendix: assumptions behind the Low, Base and High demand cases
Full references: IMF World Economic Outlook, October 2026; National Treasury 2026 Budget Review, Table 2.2; Medium-Term Development Plan 2024–2029; Akinboade, Ziramba and Kumo (2008), Energy Economics; Brons et al. (2008), Energy Economics; draft National Rail Master Plan (April 2026); system operator Medium-Term System Adequacy Outlook 2026–2030; Eskom 0.31 L/kWh (FY2024–25).
Strictly Confidential
Each case applies the same calculation to 2025E demand in the market of interest; only the rates differ. They are cases, not forecasts.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Assumption | Low | Base | High | What it applies to | Source
PETROL |  |  |  |  | 
Starting point, 2025E | 7.0bn L | 7.0bn L | 7.0bn L | Market of interest (p13) | Sasol, Glencore, SARS; Department district sales (pp4, 13)
GDP growth a year, 2026–30 | 1.0% | 2.0% | 3.0% | Petrol +0.36% per 1% of GDP | IMF WEO Oct 2026; Treasury 2026 Budget Review; MTDP 2024–29
Real petrol price in 2030 vs 2025 | +15% | Same | −13% | 2026 is 15% above 2025; low holds it, base eases back, high mirrors low; effect −0.47, phased | Department prices to Oct 2026; Akinboade et al. (2008); Brons et al. (2008); high: AIA
Efficiency gain a year | 0.8% | 0.65% | 0.5% | Road petrol | IEA/GFEI; eNaTIS; Lightstone; Stone et al. (2018) (p9)
EV share of new sales, 2030 | 4.3% | 2.7% | 1.0% | Displaces road petrol | S-curves: AIA analysis (2025); eNaTIS fleet and sales
Petrol demand in 2030 | 6.5bn L | 6.9bn L | 7.4bn L | Result of the rows above | 
DIESEL |  |  |  |  | 
Starting point, 2025E | 11.2bn L | 11.2bn L | 11.2bn L | Market of interest (p13) | Sasol, Glencore, SARS; Department district sales (pp4, 13)
GDP growth a year, 2026–30 | 1.0% | 2.0% | 3.0% | All diesel use except power, in line with GDP | IMF WEO Oct 2026; Treasury 2026 Budget Review; MTDP 2024–29
Efficiency gain a year | 0.7% | 0.55% | 0.4% | Road diesel | IEA/GFEI; eNaTIS; Stone et al. (2018) (p9)
EV share of new sales, 2030 | 4.3% | 2.7% | 1.0% | Bakkies, SUVs and cars | S-curves: AIA analysis (2025); eNaTIS fleet and sales
Rail freight in 2030 | 262m t | 250m t | 215m t | Road freight diesel; 7.2 / 6.1 / 2.8% of road freight moved, phased evenly | Rail master plan (262m t); Transnet target; Stats SA P7162 (5% a year)
Peaker load factor, 2030 | 1.4% | 4.5% | 10% | Avon (670 MW, KwaZulu-Natal) | Eskom 2026 turbine output; system operator outlook 2026–30; high case: AIA
Diesel demand in 2030 | 11.2bn L | 11.9bn L | 12.8bn L | Result of the rows above | 
Total demand in 2030 | 17.6bn L | 18.8bn L | 20.2bn L | Petrol plus diesel, market of interest | 
No data on installed capacity of backup generators or diesel consumed

## Slide 20: Appendix: in the market of interest, this year’s 2030 base case is 2.9bn litres above the November 2025 mid case
November 2025: AIA Vopak board report, 25 November 2025, slides 10 (diesel) and 16 (petrol), market-of-interest low, mid and high forecasts; method from its slides 5 (drivers), 7 (peakers) and 12 (price). This year: market-of-interest cases (pp16 and 19). Mid and base are compared as the central cases.
Strictly Confidential
Billion litres, market of interest, demand in 2030
Diesel
Petrol
The 2.9bn litre gap is mostly the higher diesel starting point (2.8bn L); petrol is 0.5bn L lower because of prices, efficiency and electric vehicles.
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Market of interest, 2030: November 2025 against this year
What each forecast includes
Chart: 
| Low | Mid / Base | High
November 2025 report | 7.0006 | 7.4028 | 7.805
This year (October 2026) | 6.4582 | 6.9297 | 7.4298
Chart: 
| Low | Mid / Base | High
November 2025 report | 7.5572 | 8.5305 | 9.5038
This year (October 2026) | 11.1854 | 11.8874 | 12.7519
 | November 2025 | This year
Starting point, 2025 | Department sales; diesel 8.4bn L, petrol 7.0 | Production + imports − exports; diesel 11.2bn L, petrol 7.0
GDP growth | Treasury MTBPS, 1.0–1.6% a year | IMF / Treasury / 3% target: 1.0 / 2.0 / 3.0% a year
Petrol price | Current prices, adjusted for inflation | 2026 rise; demand response −0.47, phased in
Efficiency | 0.5–1.0% a year | SA fleet: petrol 0.5–0.8%, diesel 0.4–0.7%
Electric vehicles | Fixed penetration rates (UNDP) | S-curve of new sales, run through the vehicle fleet
Rail | 2025 growth rates; no shift assumed | Rail at 215–262m t by 2030
Power stations | Eskom improving; peakers subdued | Avon peaker at 1.4–10% load factor

## Slide 21: Appendix: demand in every magisterial district of the market of interest (1 of 2)
Department fuel sales by magisterial district, four quarters of 2022, grown to 2025 at national growth by product (2025 demand = production + imports − exports, p4); method as p13. Sales are recorded where fuel is sold, which may differ from where it is used.
Strictly Confidential
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Million litres, 2025E | largest district first within each province | province totals match p13
Gauteng: 22 districts, 7.7bn L
District | Petrol | Diesel | Total
Johannesburg | 1,128 | 1,726 | 2,854
Pretoria | 678 | 786 | 1,464
Randburg | 376 | 227 | 603
Kempton Park | 248 | 203 | 451
Alberton | 129 | 237 | 366
Germiston | 144 | 140 | 284
Vereeniging | 83 | 167 | 250
Krugersdorp | 83 | 149 | 232
Roodepoort | 138 | 76 | 214
Benoni | 109 | 59 | 168
Boksburg | 96 | 53 | 149
Vanderbijlpark | 69 | 62 | 132
Randfontein | 28 | 79 | 107
Brakpan | 58 | 29 | 87
Wonderboom | 53 | 33 | 86
Springs | 50 | 25 | 75
Bronkhorstspruit | 19 | 33 | 52
Soshanguve | 33 | 7 | 40
Nigel | 10 | 24 | 34
Westonaria | 16 | 14 | 30
Oberholzer | 16 | 11 | 27
Cullinan | 7 | 8 | 15
Gauteng total | 3,572 | 4,148 | 7,720
KwaZulu-Natal: 45 districts, 5.0bn L (1 of 2)
District | Petrol | Diesel | Total
Durban | 701 | 2,204 | 2,905
Pinetown | 111 | 380 | 492
Pietermaritzburg | 119 | 311 | 430
Inanda | 111 | 61 | 172
Lower Umfolozi | 62 | 92 | 153
Newcastle | 43 | 57 | 100
Lower Tugela | 45 | 47 | 91
Port Shepstone | 31 | 48 | 79
Chatsworth | 46 | 28 | 74
Mount Currie | 18 | 45 | 62
Kliprivier | 23 | 23 | 46
Umzinto | 22 | 24 | 45
Camperdown | 16 | 24 | 40
Estcourt | 16 | 23 | 39
Vryheid | 15 | 17 | 33
Umlazi | 21 | 10 | 30
Lions River | 8 | 19 | 27
Eshowe | 13 | 12 | 25
Hlabisa | 7 | 14 | 21
Mtunzini | 11 | 9 | 20
Umbumbulu | 10 | 9 | 19
Ubombo | 8 | 9 | 17
Kranskop | 9 | 7 | 16
KwaZulu-Natal: 45 districts, 5.0bn L (2 of 2)
District | Petrol | Diesel | Total
Dundee | 7 | 7 | 14
Mahlabatini | 5 | 5 | 11
Umvoti | 5 | 3 | 8
Mooirivier | 3 | 5 | 7
Ingwavuma | 4 | 3 | 7
Alfred | 3 | 4 | 7
Nongoma | 4 | 3 | 7
Mtonjaneni | 3 | 4 | 6
Ixopo | 3 | 3 | 6
Nqutu | 4 | 2 | 6
Bergville | 3 | 2 | 5
Paulpietersburg | 2 | 2 | 5
Nkandla | 2 | 2 | 5
Underberg | 2 | 2 | 4
Glencoe | 1 | 1 | 2
Dannhauser | 1 | 1 | 2
Richmond (KZN) | 0 | 2 | 2
Polela | 0 | 0 | 1
New Hanover | 0 | 0 | 1
Ndwedwe | 0 | 0 | 0
Ngotshe | 0 | 0 | 0
Impendle | 0 | 0 | 0
KwaZulu-Natal total | 1,517 | 3,524 | 5,040
Mpumalanga: 28 districts, 2.1bn L
District | Petrol | Diesel | Total
Middelburg (MP) | 66 | 355 | 420
Highveld Ridge | 157 | 233 | 390
Witbank | 95 | 138 | 232
Nelspruit | 58 | 76 | 134
Volksrust | 13 | 105 | 117
Standerton | 13 | 103 | 116
Delmas | 10 | 96 | 107
Piet Retief | 18 | 56 | 74
White River | 33 | 38 | 72
Lydenburg | 22 | 47 | 68
Letaba | 20 | 28 | 48
Ermelo | 17 | 25 | 42
Belfast | 5 | 36 | 41
Barberton | 17 | 23 | 40
Bethal | 13 | 20 | 33
Kriel | 6 | 22 | 28
Groblersdal | 11 | 10 | 20
Balfour | 8 | 12 | 20
Kwamhlanga | 8 | 6 | 14
Pilgrims Rest | 5 | 7 | 12
Mdutjana (Siyabuswa) | 8 | 3 | 12
Nsikazi (Kangwane) | 4 | 2 | 6
Nkomazi (Kamhulshwa) | 4 | 2 | 6
Molopo | 3 | 1 | 5
Carolina | 2 | 3 | 5
Moutse | 3 | 1 | 4
Waterval-Boven | 1 | 1 | 1
Eerstehoek | 1 | 1 | 1
Mpumalanga total | 619 | 1,448 | 2,068

## Slide 22: Appendix: demand in every magisterial district of the market of interest (2 of 2)
Department fuel sales by magisterial district, four quarters of 2022, grown to 2025 at national growth by product (2025 demand = production + imports − exports, p4); method as p13. Sales are recorded where fuel is sold, which may differ from where it is used.
Strictly Confidential
1 Overview
2 Market baseline
3 Market changes
4 Vopak outlook
Million litres, 2025E | largest district first within each province | province totals match p13
Free State: 41 districts, 1.6bn L (1 of 2)
District | Petrol | Diesel | Total
Sasolburg | 231 | 286 | 517
Bloemfontein | 122 | 292 | 414
Kroonstad | 92 | 128 | 221
Welkom | 35 | 37 | 72
Harrismith | 15 | 43 | 58
Bethlehem | 17 | 32 | 49
Reitz | 7 | 32 | 39
Koppies | 4 | 29 | 33
Witsieshoek | 18 | 11 | 29
Bothaville | 4 | 25 | 28
Virginia | 10 | 7 | 17
Ladybrand | 4 | 12 | 16
Parys | 5 | 6 | 10
Bethulie | 1 | 5 | 6
Odendaalsrus | 4 | 2 | 6
Viljoenskroon | 1 | 5 | 6
Botshabelo | 5 | 2 | 6
Bultfontein | 2 | 5 | 6
Ficksburg | 2 | 3 | 5
Ventersburg | 2 | 3 | 5
Heilbron | 2 | 3 | 4
Free State: 41 districts, 1.6bn L (2 of 2)
District | Petrol | Diesel | Total
Senekal | 2 | 2 | 4
Frankfort | 2 | 2 | 4
Marquard | 0 | 4 | 4
Thaba'nchu | 2 | 1 | 3
Clocolan | 1 | 1 | 2
Rouxville | 1 | 1 | 2
Brandfort | 1 | 1 | 2
Trompsburg | 1 | 1 | 2
Wesselsbron | 1 | 1 | 2
Theunissen | 0 | 1 | 2
Vrede | 0 | 1 | 1
Hoopstad | 0 | 1 | 1
Boshof | 1 | 1 | 1
Fauresmith | 0 | 1 | 1
Lindley | 0 | 1 | 1
Petrusburg | 0 | 1 | 1
Smithfield | 0 | 1 | 1
Zastron | 0 | 1 | 1
Winburg | 0 | 0 | 0
Hennenman | 0 | 0 | 0
Free State total | 594 | 989 | 1,583
North West: 26 districts, 1.2bn L
District | Petrol | Diesel | Total
Klerksdorp | 136 | 259 | 395
Rustenburg | 98 | 161 | 259
Brits | 41 | 88 | 129
Potchefstroom | 44 | 30 | 74
Molopo | 14 | 57 | 70
Lichtenburg | 17 | 41 | 58
Vryburg (south) | 12 | 33 | 44
Odi | 34 | 6 | 40
Mankwe | 5 | 27 | 32
Wolmaranstad | 7 | 15 | 23
Marico | 10 | 9 | 20
Schweizer-Reneke | 4 | 16 | 19
Moretele 1 | 14 | 6 | 19
Bloemhof | 0 | 19 | 18
Christiana | 3 | 4 | 6
Swartruggens | 3 | 2 | 6
Taung | 4 | 2 | 6
Vryburg (west) | 3 | 2 | 4
Ventersdorp | 2 | 2 | 4
Delareyville | 1 | 2 | 3
Coligny | 0 | 3 | 3
Lehurutshe | 2 | 1 | 3
Koster | 1 | 1 | 2
Ditsobotla | 0 | 1 | 1
Vryburg (north-east) | 0 | 0 | 0
Kudumane | 0 | 0 | 0
North West total | 453 | 784 | 1,238
Limpopo: 28 districts, 0.6bn L
District | Petrol | Diesel | Total
Polokwane (south) | 87 | 94 | 181
Soutpansberg (central) | 20 | 24 | 44
Polokwane (north) | 19 | 17 | 36
Thohoyandou (west) | 18 | 12 | 30
Phalaborwa | 16 | 13 | 28
Waterberg | 11 | 14 | 26
Mokopane (south) | 15 | 10 | 25
Giyani | 14 | 10 | 24
Musina (east) | 9 | 14 | 23
Thabazimbi (east) | 8 | 13 | 21
Thabamoopo | 11 | 6 | 17
Lephalale (Ellisras) | 5 | 11 | 16
Bela-Bela (Warmbad) | 8 | 5 | 13
Musina (west) | 0 | 12 | 12
Malamulele | 7 | 4 | 11
Mokopane (north) | 4 | 6 | 10
Mhala | 5 | 3 | 8
Thohoyandou (east) | 4 | 3 | 6
Seshego | 4 | 1 | 5
Thabazimbi (west) | 1 | 3 | 4
Soutpansberg (east) | 2 | 2 | 4
Namakgale | 3 | 1 | 4
Lulekani | 2 | 1 | 3
Bochum | 1 | 1 | 3
Mapulaneng | 1 | 1 | 2
Ritavi | 1 | 0 | 2
Sekhukhuneland | 1 | 0 | 1
Mokerong 1 (east) | 0 | 0 | 0
Limpopo total | 277 | 281 | 558