## Slide 1
South Africa
liquid fuels
market story
Inland supply, corridor capture and tank turnover
Durban–Lesedi corridor into Gauteng
11 October 2026
Public evidence and illustrative capture cases. Customer access, operating limits and returns remain provisional.
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: South Africa fuel-market analysis. Sources and assumptions appear on the relevant analytical pages.

## Slide 2: South Africa remains an import-led fuel market, making customer capture Vopak’s priority
Analytical workbook v02 and market-sizing analysis. Demand is estimated; production and capture are planning assumptions. Product reconciliation remains open;
Strictly Confidential
SITUATION
A large fuel market relies on substantial imports
pp3–6, 23
2025 demand is estimated at 21.0bn litres: 8.9bn petrol and 12.1bn diesel, down from 21.9bn in 2023. Road use dominates. At the assumed 5.8bn litres of domestic production, gross import need is about 16.7bn litres.
COMPLICATION
Sector growth supports demand, but fuel use, supply and routes are changing
Deep dive
Mining, manufacturing
and agriculture
Production, exports and harvests drive diesel use in equipment and freight; sector growth paths differ.
p7
Eskom and power
generation
Recovery reduces peaking and backup diesel at utilities, mines, factories and farms, while supporting activity.
p8
Road-to-rail shift and
vehicle efficiency
Moving goods from trucks to rail and improving vehicle efficiency reduce fuel consumed per unit of activity.
pp9, 22
Refineries and domestic
fuel production
Higher output or restarts displace imports relative to the 5.8bn-litre assumption; lower output increases import need.
p10
Matola and inland routes
Matola provides an alternative gateway for inland supply; delivered cost, reliability and access determine its reach.
p11
RESOLUTION
Vopak should secure customer capture before expanding
pp12–15
Base imports remain about 16.6bn litres in 2030. Illustrative capture is 2.63bn litres through Durban, including 1.32bn onward through Lesedi within the same flow; this fits the preliminary working-tank screen.
Expansion requires secured incremental volumes and a demonstrated capacity shortfall.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02 and market-sizing analysis. Demand is estimated; production and capture are planning assumptions. Product reconciliation remains open;
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 3: Fuel demand has eased to 21.0bn litres and stays broadly flat through 2030 in the base case
Department sales 2013–2023; analytical workbook v02. E = estimated 2024–2025. 2030 is the base scenario, not an observed outcome.
Strictly Confidential
National fuel demand, 2013–2025
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024E | 2025E
Total | 23.5812 | 23.5052 | 24.9958 | 23.5446 | 23.3213 | 23.6804 | 23.6818 | 20.4514 | 22.2474 | 21.9022 | 21.9445 | 22.0811 | 20.9874
Petrol | 11.4399 | 10.8902 | 11.4757 | 11.4623 | 11.1741 | 11.1416 | 10.7732 | 8.7615 | 9.3016 | 9.1849 | 9.037 | 8.9459 | 8.8558
Diesel | 12.1413 | 12.615 | 13.5201 | 12.0824 | 12.1472 | 12.5387 | 12.9086 | 11.69 | 12.9458 | 12.7173 | 12.9075 | 13.1352 | 12.1316
Billion litres
Five drivers of the outlook
Sectors: activity supports demand.
Eskom: recovery lowers power fuel use.
Road-to-rail and efficiency reduce road fuel use.
Refineries: recovery displaces imports.
Matola: an alternative gateway competes for inland flows.
2030 base: 20.9bn L demand; 16.6bn L gross imports.
Demand determines consumption, domestic production determines import need, and competing gateways determine Durban’s share.
Executive summary
Situation
Complication
Resolution
Notes: Department sales 2013–2023; analytical workbook v02. E = estimated 2024–2025. 2030 is the base scenario, not an observed outcome.
Demand determines consumption, domestic production determines import need, and competing gateways determine Durban’s share.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 4: Petrol has declined since 2013, while diesel has sustained the market
Department annual sales, 2013–2023. Estimated 2024–2025: analytical workbook v02. The Department series is used consistently.
Strictly Confidential
Petrol and diesel demand, 2013–2025
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024E | 2025E
Petrol | 11.4399 | 10.8902 | 11.4757 | 11.4623 | 11.1741 | 11.1416 | 10.7732 | 8.7615 | 9.3016 | 9.1849 | 9.037 | 8.9459 | 8.8558
Diesel | 12.1413 | 12.615 | 13.5201 | 12.0824 | 12.1472 | 12.5387 | 12.9086 | 11.69 | 12.9458 | 12.7173 | 12.9075 | 13.1352 | 12.1316
Billion litres
Petrol demand outlook
Petrol: 9.04bn L in 2023 to 8.86bn L in 2025E.
Assumed efficiency and fleet changes outweigh activity growth.
Diesel: 12.13bn L in 2025E.
2013–23: reported Department series. 2024–25: estimates.
Petrol remains below its earlier level; diesel demand responds more directly to freight, industry and power.
Executive summary
Situation
Complication
Resolution
Notes: Department annual sales, 2013–2023. Estimated 2024–2025: analytical workbook v02. The Department series is used consistently.
Petrol remains below its earlier level; diesel demand responds more directly to freight, industry and power.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 5: Road use dominates the baseline, with meaningful diesel demand outside transport
Analytical workbook v02, Segments. 2021 energy-balance road volume; 75% of road diesel allocated to freight. Historical sector intensities at current activity.
Strictly Confidential
2025 estimated demand by use
Chart: 
| Manufacturing | Other petrol | Power | Agriculture | Mining | Other road diesel | Other diesel | Freight diesel | Petrol road
2025 estimated bn litres | 0.16508 | 0.26567 | 1.0843 | 1.1312 | 1.4063 | 1.6082 | 1.9119 | 4.8245 | 8.5901
Billion litres
Demand allocation
Road freight: 4.82bn L
Mining: 1.41bn L
Agriculture: 1.13bn L
Other diesel: 1.91bn L remains unallocated to a specific end use.
Sector-attributed vehicle fuel stays in its sector; the road split is an explicit allocation assumption.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Segments. 2021 energy-balance road volume; 75% of road diesel allocated to freight. Historical sector intensities at current activity.
Sector-attributed vehicle fuel stays in its sector; the road split is an explicit allocation assumption.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 6: The 5.8bn-litre production assumption leaves a gross import requirement of about 16.7bn litres
Analytical workbook v02, Balance and Supply assumption. National production planning assumption. Original plant-based estimate 10.23bn L retained in appendix.
Strictly Confidential
2025 national balance | bn litres | Basis
Demand | 20.99 | Estimated from the 2023 sales baseline
Domestic production | 5.80 | National planning assumption
Gross imports | 16.70 | SARS recorded customs litres
Exports | 1.55 | SARS recorded customs litres
Production + net imports | 20.95 | Availability before stock / statistical differences
Availability less demand | -0.03 | Aggregate near-balance; product differences remain
5.8bn litres sets the planning case. Aggregate closure does not validate domestic output or its petrol/diesel split.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Balance and Supply assumption. National production planning assumption. Original plant-based estimate 10.23bn L retained in appendix.
5.8bn litres sets the planning case. Aggregate closure does not validate domestic output or its petrol/diesel split.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 7: Agricultural demand rebounds in 2025 while mining and manufacturing remain broadly flat
Stats SA mining/manufacturing indices and agriculture real GVA; mean 2018–2021 fuel intensity. Sector diesel values after 2021 are estimates.
Strictly Confidential
Estimated sector diesel demand
Chart: 
| 2023 | 2024 | 2025
Mining | 1.396 | 1.4037 | 1.4063
Agriculture | 1.0553 | 0.96334 | 1.1312
Manufacturing | 0.1679 | 0.16721 | 0.16508
Billion litres
Estimated diesel use
Mining: 1.40 → 1.41bn L
Agriculture: 1.06 → 1.13bn L
Manufacturing: about 0.17bn L
Manufacturing covers the energy-balance industry residual, not a complete industrial census.
Sector activity produces different demand paths; applying one GDP growth rate would hide these differences.
Executive summary
Situation
Complication
Resolution
Notes: Stats SA mining/manufacturing indices and agriculture real GVA; mean 2018–2021 fuel intensity. Sector diesel values after 2021 are estimates.
Sector activity produces different demand paths; applying one GDP growth rate would hide these differences.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 8: Eskom’s fuel use fell by 40% in FY2025 as electricity supply improved
Eskom Integrated Report 2025, p141. Fiscal years end in March. Reported series includes diesel and kerosene; private backup consumption is outside this series.
Strictly Confidential
Eskom diesel and kerosene use
Chart: 
| FY2023 | FY2024 | FY2025
Eskom diesel + kerosene, bn litres | 0.9375 | 1.1295 | 0.6791
Billion litres
Lower power-related fuel use
Eskom diesel and kerosene fell from 1.130bn L in FY2024 to 0.679bn L in FY2025.
Better supply can also reduce backup diesel at mines, factories and farms.
Private backup use is estimated separately; it is not measured by this Eskom series.
Power recovery reduces a source of diesel demand created by electricity shortages; the 2030 assumptions are in the appendix.
Executive summary
Situation
Complication
Resolution
Notes: Eskom Integrated Report 2025, p141. Fiscal years end in March. Reported series includes diesel and kerosene; private backup consumption is outside this series.
Power recovery reduces a source of diesel demand created by electricity shortages; the 2030 assumptions are in the appendix.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 9: Rail volumes are recovering, creating scope to reduce road diesel use
Stats SA P7162 December 2025 p7; all reported freight. Analytical workbook v02, Evidence.
Strictly Confidential
Reported road and rail freight
Chart: 
| 2024 | 2025
Road, million tonnes | 979.798 | 976.468
Rail, million tonnes | 160.745 | 168.263
Million tonnes
Recovery and displacement
Rail: 160.7m tonnes in 2024 to 168.3m in 2025. Road: 979.8m to 976.5m tonnes.
A shift of mining, agricultural and manufactured goods to rail can reduce truck fuel use.
Rail growth alone does not prove road displacement; distance, cargo and traction mix matter.
Road remains the dominant freight mode; sustained rail recovery could change the diesel required to move goods.
Executive summary
Situation
Complication
Resolution
Notes: Stats SA P7162 December 2025 p7; all reported freight. Analytical workbook v02, Evidence.
Road remains the dominant freight mode; sustained rail recovery could change the diesel required to move goods.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 10: Changes in refinery output alter the volume that imports must supply
Sasol production metrics FY2025 and FY2026; Glencore annual reports 2024 and 2025; 2025 plant assessment. Fiscal and calendar periods and reporting scopes differ. Restart sensitivities are in the appendix.
Strictly Confidential
Domestic supply | Reported evidence | Implication for imports
Secunda | Refined-products output: 29.1m barrels in FY2024; 27.6m in FY2025; 30.6m in FY2026 | Operating recovery can increase domestic supply; petrol and diesel yields determine import displacement.
Natref | Sasol-reported output: 17.8m barrels in FY2024; 14.7m in FY2025; 25.8m in FY2026 | FY2026 includes above-share production, so the latest reported change cannot be treated as a like-for-like change in whole-plant output.
Astron | Reported refined products: 166,204 billion Btu in 2024; 164,365 billion Btu in 2025 | Output and product mix affect supply; energy units require conversion before comparison with customs litres.
SAPREF and PetroSA | No refining contribution included in the 2025 production assessment | Restored refining would displace imports only when plants produce saleable products. Terminal handling is not refinery output.
Domestic production can recover or fall independently of demand; actual output and product yields determine the import requirement.
Executive summary
Situation
Complication
Resolution
Notes: Sasol production metrics FY2025 and FY2026; Glencore annual reports 2024 and 2025; 2025 plant assessment. Fiscal and calendar periods and reporting scopes differ. Restart sensitivities are in the appendix.
Domestic production can recover or fall independently of demand; actual output and product yields determine the import requirement.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 11: Matola provides an existing alternative gateway for inland fuel supply
Galp Matola commissioning release, 3 December 2020; Petromoc logistics disclosures; Sasol Mozambique operations; SARS customs, 2022 and 2025. Storage is not annual throughput.
Strictly Confidential
Node | Evidence | Implication for South African fuel routes
Galp/IPG Matola | 60,000m³ petrol/diesel storage; opened 2020 | Existing import and distribution infrastructure
Petromoc Língamo / Matola | 390,000m³ across liquid fuels | Broader storage base; product allocation and overlap need confirmation
Beira, Nacala and Pemba | Existing central / northern logistics nodes | Regional supply; no additional SA flow assigned in the base case
Temane PSA | Light oil, gas and LPG; production began December 2025 | No direct finished petrol/diesel output credited
Komatipoort recorded imports | 0.303bn L in 2022 → 0.086bn L in 2025 | Current cross-border flow is far smaller than gross storage suggests
Matola’s infrastructure creates an alternative supply route; recorded cross-border flows remain much smaller than storage capacity.
Executive summary
Situation
Complication
Resolution
Notes: Galp Matola commissioning release, 3 December 2020; Petromoc logistics disclosures; Sasol Mozambique operations; SARS customs, 2022 and 2025. Storage is not annual throughput.
Matola’s infrastructure creates an alternative supply route; recorded cross-border flows remain much smaller than storage capacity.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 12: The base case leaves imports near 16.6bn litres in 2030, with refinery recovery driving the downside
Analytical workbook v02, Scenarios. Demand-implied gross imports = demand − domestic supply + 2025 exports. Zero stock change; 5.8bn L assumed opening supply.
Strictly Confidential
Gross import requirement, 2025–2030
Chart: 
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Low imports | 16.7359 | 16.165 | 15.5984 | 15.0359 | 11.6443 | 8.2568
Base | 16.7359 | 16.708 | 16.681 | 16.6549 | 16.6295 | 16.6051
High imports | 16.7359 | 17.3083 | 17.8888 | 18.4777 | 19.0749 | 19.6808
Billion litres
2030 gross import need
Low imports: 8.26bn L
Base: 16.61bn L
High imports: 19.68bn L
Cases are sensitivities, not assigned probabilities.
The base case balances activity growth against efficiency, rail and power reductions; supply assumptions drive the widest spread.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Scenarios. Demand-implied gross imports = demand − domestic supply + 2025 exports. Zero stock change; 5.8bn L assumed opening supply.
The base case balances activity growth against efficiency, rail and power reductions; supply assumptions drive the widest spread.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 13: Vopak’s capture depends on the accessible share of Durban imports
Market-sizing analysis, October 2026. Capture is total conditional flow, not incremental sales; domestic and other-terminal Lesedi receipts are outside this screen.
Strictly Confidential
Market / flow measure | Annual volume | Meaning for Vopak
National demand, 2025 estimate | 20.99bn litres | Total consumption context
National gross imports, 2025 | 16.70bn litres | All recorded import gateways
Durban customs imports, 2025 | 13.16bn litres | Gateway proxy before customer and route allocation
Illustrative Durban capture | 2.63bn litres | 20% of Durban gateway volume; no contracted share inferred
Illustrative onward Lesedi flow | 1.32bn litres | 50% of captured Durban flow; counted within the same fuel volume
The illustrative unique flow is 2.63bn litres. Adding Lesedi would double-count fuel handled at both sites.
Executive summary
Situation
Complication
Resolution
Notes: Market-sizing analysis, October 2026. Capture is total conditional flow, not incremental sales; domestic and other-terminal Lesedi receipts are outside this screen.
The illustrative unique flow is 2.63bn litres. Adding Lesedi would double-count fuel handled at both sites.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 14: The illustrative capture case fits the tank-turn screen, making usable capacity the next test
Terminal working-capacity assessment, October 2026. Durban working subset is not the full terminal; access, peaks and current throughput remain open.
Strictly Confidential
Site | Illustrative flow bn L/year | Handling screen bn L/year | Operating basis
Durban | 2.63 | 3.50 | 146,000m³ estimated working subset; two turns/month
Lesedi | 1.32 | 2.98 | 124,000m³ working capacity, partly estimated; two turns/month
Investment test | Incremental contracts | Actual constraint | Receipt, product segregation, dispatch, pipeline access and peak demand
Working-tank arithmetic screens feasibility. Engineering limits and current customer flows determine actual headroom.
Executive summary
Situation
Complication
Resolution
Notes: Terminal working-capacity assessment, October 2026. Durban working subset is not the full terminal; access, peaks and current throughput remain open.
Working-tank arithmetic screens feasibility. Engineering limits and current customer flows determine actual headroom.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 15: The market supports an import platform; customer capture and capacity constraints govern investment
2025 analytical workbook v02: demand assumptions and 5.8bn L domestic production case. Estimates are not reported actuals.
Strictly Confidential
Conclusion | Evidence from this story | Decision implication
A substantial demand base | 2025 estimated demand of 21.0bn litres | Prioritise identifiable customer segments and destinations
Base imports remain substantial | About 16.6bn litres in 2030 under the 5.8bn supply case | Plan for ongoing imports; retain refinery sensitivities
Gateways compete for the same fuel | Mozambique base diversion of 0.20bn L is a route assumption | Validate delivered cost, service and customer access
Expansion follows incremental capture | Illustrative 2.63bn L unique flow fits the tank-turn screen | Secure additional volumes, prove the bottleneck, then compare improvement and expansion returns
Next decisions: review the product balance, obtain route quotes and customer commitments, and establish usable capacity at both sites.
Executive summary
Situation
Complication
Resolution
Notes: 2025 analytical workbook v02: demand assumptions and 5.8bn L domestic production case. Estimates are not reported actuals.
Next decisions: review the product balance, obtain route quotes and customer commitments, and establish usable capacity at both sites.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 16
Strictly Confidential
Appendix
Supporting analysis and assumptions
Power and freight sensitivities • Refinery and route assumptions
Product balance • Demand methodology • Sources
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 17: Further power recovery halves fuel demand to 0.54bn litres in the 2030 base case
Analytical workbook v02: calculated power baseline and 2030 retention assumptions. Estimated utility/private scope includes FY proxies and IPP conversion. Scenario endpoints, not forecasts of annual dispatch.
Strictly Confidential
Power fuel demand across scenarios
Chart: 
| 2025 estimate | 2030 base | 2030 lower use | 2030 unchanged use
Utility and private power | 1.0843 | 0.54216 | 0.37951 | 1.0843
Billion litres
Base case and sensitivities
2025 estimate: 1.08bn L, including 0.20bn L assumed private backup.
Base: 50% retained in 2030; a 0.54bn L reduction.
Lower-use case: 35% retained. Unchanged-use case: 100% retained.
Improved electricity supply lowers peaking and backup fuel use, even where transport and industrial activity continue to grow.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Analytical workbook v02: calculated power baseline and 2030 retention assumptions. Estimated utility/private scope includes FY proxies and IPP conversion. Scenario endpoints, not forecasts of annual dispatch.
Improved electricity supply lowers peaking and backup fuel use, even where transport and industrial activity continue to grow.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 18: A 7.5% shift of road-freight activity to rail saves 0.33bn litres in the base case
Analytical workbook v02, Driver bridge and scenario assumptions. Shift interpreted as freight tonne-km share. Distances and eligibility remain assumed; cases also vary growth and efficiency.
Strictly Confidential
2030 case | Road-freight shift | Net diesel reduction
Low imports | 15.0% | 0.62bn litres
Base | 7.5% | 0.33bn litres
High imports | 2.5% | 0.12bn litres
Calculation order | Activity → efficiency → modal shift | 10% diesel rebound allowance for rail
These shifts apply to road-freight activity, not the entire diesel market; sector demand and power remain separate.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Analytical workbook v02, Driver bridge and scenario assumptions. Shift interpreted as freight tonne-km share. Distances and eligibility remain assumed; cases also vary growth and efficiency.
These shifts apply to road-freight activity, not the entire diesel market; sector demand and power remain separate.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 19: Refinery restart assumptions drive the lower-import sensitivity
Refinery production and restart scenario assumptions. Capacity inputs: SAPREF 180kb/d, PetroSA 45kb/d; 70% petrol/diesel yield in restart sensitivities. Dates are not project commitments.
Strictly Confidential
Supply lever | Base case | Low-import sensitivity
Operating domestic supply | 5.8bn L through 2030 | 15% increase in the national planning volume
SAPREF | No refining restart through 2030 | Assumed 2029 start; 65% utilisation after a two-year ramp
PetroSA / Mossel Bay | No refining restart through 2030 | Assumed 2029 start; 50% utilisation after a two-year ramp
Combined restart contribution | Zero | 5.67bn L petrol/diesel in 2030
Restart dates and ramp-up settings are scenario assumptions. Import-terminal operations can compete before refining resumes.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Refinery production and restart scenario assumptions. Capacity inputs: SAPREF 180kb/d, PetroSA 45kb/d; 70% petrol/diesel yield in restart sensitivities. Dates are not project commitments.
Restart dates and ramp-up settings are scenario assumptions. Import-terminal operations can compete before refining resumes.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 20: Illustrative route costs put Matola at a R0.19-per-litre logistics premium
Analytical workbook v02, Mozambique. Distances, tariffs, border charges, financing and allocation are illustrative sensitivities, not carrier quotes or confirmed access.
Strictly Confidential
Route sensitivity | Result | Assumptions behind the result
Durban → same inland destination | R0.95 per litre logistics | 600km one way; round trip; R25/truck-km; 40,000L payload
Matola → same inland destination | R1.14 per litre logistics | 550km one way; terminal and border costs; one-day delay
Matola premium | R0.19 per litre | Required landed-product discount under these illustrative costs
Border-delay sensitivity | R0.09–R0.40 per litre premium | Zero to three delay days
Base incremental Mozambique flow | 0.20bn L by 2030 | About 15 additional loaded trucks/day over 330 days
Mozambique diversion changes the gateway serving demand. It does not reduce South Africa’s national import requirement.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Analytical workbook v02, Mozambique. Distances, tariffs, border charges, financing and allocation are illustrative sensitivities, not carrier quotes or confirmed access.
Mozambique diversion changes the gateway serving demand. It does not reduce South Africa’s national import requirement.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 21: The national supply assumption closes the total balance but leaves the product mix unresolved
Analytical workbook v02, Supply assumption and Balance. Original plant estimate: Secunda 3.95, Natref 2.37, Astron 3.91bn L; 10.23bn total. These do not govern the planning case.
Strictly Confidential
2025 measure | Petrol bn L | Diesel bn L | Total bn L
2025 demand | 8.86 | 12.13 | 20.99
Domestic production | 3.20 | 2.60 | 5.80
Gross customs imports | 4.45 | 12.25 | 16.70
Customs exports | 0.80 | 0.75 | 1.55
Supply plus net imports | 6.85 | 14.10 | 20.95
Unexplained availability less demand | -2.00 | 1.97 | -0.03
The 5.8bn L planning case uses the original estimated production mix. Offsetting product differences remain visible; no product allocation is claimed as verified.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Analytical workbook v02, Supply assumption and Balance. Original plant estimate: Secunda 3.95, Natref 2.37, Astron 3.91bn L; 10.23bn total. These do not govern the planning case.
The 5.8bn L planning case uses the original estimated production mix. Offsetting product differences remain visible; no product allocation is claimed as verified.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 22: Efficiency offsets activity growth in the petrol baseline
Department 2023 sales; analytical workbook v02, Assumptions and Demand history. Activity and efficiency settings are illustrative planning assumptions.
Strictly Confidential
Demand component | Assumption / result | How it enters the estimate
Petrol activity | +0.5% per year in 2024–2025 | More vehicle use supports consumption
Petrol fuel intensity | −1.5% per year in 2024–2025 | A combined efficiency / fleet-mix assumption reduces fuel per unit of activity
Petrol demand | 9.04bn L in 2023 → 8.86bn L in 2025 | Compounding activity and intensity yields a modest decline
2030 road outlook | Base: 1% annual efficiency improvement | Applied after activity growth; rail displacement is then applied to freight only
The assumptions are explicit and editable; EV uptake is not counted again as a separate reduction.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Department 2023 sales; analytical workbook v02, Assumptions and Demand history. Activity and efficiency settings are illustrative planning assumptions.
The assumptions are explicit and editable; EV uptake is not counted again as a separate reduction.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 23: Our 2025 baseline is 21.0bn litres, with road use accounting for most demand
Department sales through 2023; energy balances and Stats SA activity; Eskom/IPP evidence. All 2025 segment allocations are estimates; other diesel retains an explicit residual.
Strictly Confidential
Demand segment | 2025 estimate bn litres | Change since 2023 bn litres
Petrol road use | 8.59 | -0.18
Mining | 1.41 | 0.01
Manufacturing | 0.17 | 0.00
Agriculture | 1.13 | 0.08
Utility and private power | 1.08 | -0.99
Road freight diesel | 4.82 | -0.02
Other road diesel | 1.61 | -0.01
Other petrol | 0.27 | -0.01
Other diesel / unallocated | 1.91 | 0.16
Petrol: 8.86bn L. Diesel: 12.13bn L. Total demand falls from 21.94bn L in 2023 to an estimated 20.99bn L in 2025.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Department sales through 2023; energy balances and Stats SA activity; Eskom/IPP evidence. All 2025 segment allocations are estimates; other diesel retains an explicit residual.
Petrol: 8.86bn L. Diesel: 12.13bn L. Total demand falls from 21.94bn L in 2023 to an estimated 20.99bn L in 2025.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 24: Source definitions and explicit assumptions underpin the demand and import outlook
Sources: Department energy statistics; Stats SA; Eskom; Sasol; Glencore; SARS; Galp; Petromoc. Supporting calculations: analytical workbook v02 and market-sizing workbook.
Strictly Confidential
Evidence / assumption | Pages | Source and analytical treatment
National sales and sector activity | 3–7, 22–23 | Department sales, energy balances and Stats SA activity. Demand after 2023 is estimated; segment boundaries retain an unallocated residual.
Power and freight | 8–9, 17–18 | Eskom fuel and Stats SA freight observations. Private backup, future rail shift and efficiency remain explicit planning assumptions.
Domestic supply and imports | 6, 10, 12, 19, 21 | Sasol and Glencore plant disclosures; SARS trade. The 5.8bn-litre national production case is an assumption; product reconciliation remains open.
Matola infrastructure and costs | 11, 20 | Operator infrastructure disclosures and SARS customs. Logistics costs are illustrative, rather than carrier quotations.
Vopak capture and capacity | 13–15 | Illustrative gateway capture and working-tank turnover. Customer commitments and engineering constraints determine achievable volumes.
Observed data, estimates and scenario assumptions are labelled separately throughout the analysis.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Sources: Department energy statistics; Stats SA; Eskom; Sasol; Glencore; SARS; Galp; Petromoc. Supporting calculations: analytical workbook v02 and market-sizing workbook.
Observed data, estimates and scenario assumptions are labelled separately throughout the analysis.
Planning baseline: assumed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations