## Slide 1
South Africa
liquid fuels
market story
Inland supply, corridor capture and tank turnover
Durban–Lesedi corridor into Gauteng
11 October 2026
Public evidence and illustrative capture cases. Customer access, operating limits and returns remain provisional.
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: 10 October revision
Sources and assumptions: output/delivered/market_review_2026_10_10/market_review.json; assumptions/2026/market_review.yaml; terminal_site_assumptions.csv; Manish Master_data_book.xlsx and DR01/04/07/08 handback through 9 October. Investment outputs: output/delivered/vopak_illustration_2026_10_10/results.json. Public observations, estimates and authored sensitivities retain their stated scopes. Pipeline source: https://www.transnet.net/getFile.ashx?id=6121, printed p8. No independent approval inferred.
Previous revision notes retained for source history; revised slide values take precedence:
Speaker note: Walk through four sections: the project question, the analytical
requirements, the model-build problem and the delivery approach. The purpose is to
connect the analyst's tasks to the decisions the engagement needs to support.
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
Final structure: baseline pp3–6; changes pp7–11 (forecast framework p9); outlook pp12–17 (market choices p16, inventory p17). Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
Final structure: baseline pp3–6; changes pp7–11 (forecast framework p9); outlook pp12–17 (market choices p16, inventory p17). Current page 1.

## Slide 2: Our 2025 baseline is 21.0bn litres, with road use accounting for most demand
Department sales through 2023; energy balances and Stats SA activity; Eskom/IPP evidence. All 2025 segment allocations are estimates; other diesel retains an explicit residual.
Strictly Confidential
Demand segment | 2025 estimate bn litres | Change since 2023 bn litres
Petrol road use | 8.59 | -0.18
Mining | 1.41 | 0.01
Manufacturing | 0.17 | -0.00
Agriculture | 1.13 | 0.08
Utility and private power | 1.08 | -0.99
Road freight diesel | 4.82 | -0.02
Other road diesel | 1.61 | -0.01
Other petrol | 0.27 | -0.01
Other diesel / unallocated | 1.91 | 0.16
Petrol: 8.86bn L. Diesel: 12.13bn L. Total demand falls from 21.94bn L in 2023 to an estimated 20.99bn L in 2025.
Executive summary
Situation
Complication
Resolution
Notes: Department sales through 2023; energy balances and Stats SA activity; Eskom/IPP evidence. All 2025 segment allocations are estimates; other diesel retains an explicit residual.
Petrol: 8.86bn L. Diesel: 12.13bn L. Total demand falls from 21.94bn L in 2023 to an estimated 20.99bn L in 2025.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 3: Demand stays broadly flat in our base case; supply and routes determine where imports enter
2025 analytical workbook v02: registered demand assumptions and user-directed 5.8bn L domestic production case. Estimates are not reported actuals.
Strictly Confidential
Driver and deep dive | Evidence / planning assumption | Base-case implication by 2030
Power ¦ pp8–9 | Eskom fuel fell from 1.13bn L in FY2024 to 0.68bn in FY2025 | Power demand reduction: 0.54bn L; includes assumed private backup
Freight and vehicles ¦ pp7, 10–11 | 7.5% road-freight shift to rail; 1% annual road-fuel efficiency gain | Rail saves 0.33bn L; road efficiency saves 0.79bn L
Domestic production ¦ pp12–14 | 5.8bn L directed planning baseline; no restart in base case | Demand-implied gross imports remain about 16.6bn L in 2030
Mozambique routes ¦ pp15–16 | Existing Matola infrastructure and an assumed 0.20bn L additional SA flow | Imports change gateway; national fuel demand stays unchanged
Activity adds 1.54bn L by 2030, broadly offsetting power, efficiency and rail reductions. Customer access determines Vopak capture.
Executive summary
Situation
Complication
Resolution
Notes: 2025 analytical workbook v02: registered demand assumptions and user-directed 5.8bn L domestic production case. Estimates are not reported actuals.
Activity adds 1.54bn L by 2030, broadly offsetting power, efficiency and rail reductions. Customer access determines Vopak capture.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 4: Petrol has declined since 2013, while diesel has sustained the market
Department annual sales, 2013–2023. Estimated 2024–2025: analytical workbook v02. Earlier deck FIASA comparison figures are not spliced into this series.
Strictly Confidential
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Petrol | 11.4399 | 10.8902 | 11.4757 | 11.4623 | 11.1741 | 11.1416 | 10.7732 | 8.7615 | 9.3016 | 9.1849 | 9.037 | 8.9459 | 8.8558
Diesel | 12.1413 | 12.615 | 13.5201 | 12.0824 | 12.1472 | 12.5387 | 12.9086 | 11.69 | 12.9458 | 12.7173 | 12.9075 | 13.1352 | 12.1316
Billion litres
2025 estimate
Petrol 8.86bn litres
Diesel 12.13bn litres
2024–25 are estimates; 2013–23 use one consistent Department series.
Petrol remains below its earlier level; diesel demand responds more directly to freight, industry and power.
Executive summary
Situation
Complication
Resolution
Notes: Department annual sales, 2013–2023. Estimated 2024–2025: analytical workbook v02. Earlier deck FIASA comparison figures are not spliced into this series.
Petrol remains below its earlier level; diesel demand responds more directly to freight, industry and power.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 5: Road use dominates the baseline, with meaningful diesel demand outside transport
Analytical workbook v02, Segments. 2021 energy-balance road volume; 75% of road diesel allocated to freight. Historical sector intensities at current activity.
Strictly Confidential
Chart: 
| Petrol road | Freight diesel | Other road diesel | Mining | Agriculture | Power | Manufacturing | Other petrol | Other diesel
2025 estimated bn litres | 8.5901 | 4.8245 | 1.6082 | 1.4063 | 1.1312 | 1.0843 | 0.16508 | 0.26567 | 1.9119
Billion litres
Demand allocation
Road freight: 4.82bn L
Mining: 1.41bn L
Agriculture: 1.13bn L
Other diesel: 1.91bn L remains unallocated to a specific end use.
Sector-attributed vehicle fuel stays in its sector; the road split is an explicit allocation assumption.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Segments. 2021 energy-balance road volume; 75% of road diesel allocated to freight. Historical sector intensities at current activity.
Sector-attributed vehicle fuel stays in its sector; the road split is an explicit allocation assumption.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 6: Agricultural demand rebounds in 2025 while mining and manufacturing remain broadly flat
Stats SA mining/manufacturing indices and agriculture real GVA; mean 2018–2021 fuel intensity. Sector diesel values after 2021 are estimates.
Strictly Confidential
Chart: 
| 2023 | 2024 | 2025
Mining | 1.396 | 1.4037 | 1.4063
Agriculture | 1.0553 | 0.96334 | 1.1312
Manufacturing | 0.1679 | 0.16721 | 0.16508
Billion litres
Estimated diesel use
Mining: 1.40 → 1.41bn L
Agriculture: 1.06 → 1.13bn L
Manufacturing: about 0.17bn L
Manufacturing covers the energy-balance industry residual, not a complete industrial census.
Sector activity produces different demand paths; applying one GDP growth rate would hide these differences.
Executive summary
Situation
Complication
Resolution
Notes: Stats SA mining/manufacturing indices and agriculture real GVA; mean 2018–2021 fuel intensity. Sector diesel values after 2021 are estimates.
Sector activity produces different demand paths; applying one GDP growth rate would hide these differences.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 7: Efficiency offsets activity growth in the petrol baseline
Department 2023 sales; analytical workbook v02, Assumptions and Demand history. Activity and efficiency settings are authored planning assumptions.
Strictly Confidential
Demand component | Assumption / result | How it enters the estimate
Petrol activity | +0.5% per year in 2024–2025 | More vehicle use supports consumption
Petrol fuel intensity | −1.5% per year in 2024–2025 | A combined efficiency / fleet-mix assumption reduces fuel per unit of activity
Petrol demand | 9.04bn L in 2023 → 8.86bn L in 2025 | Compounding activity and intensity yields a modest decline
2030 road outlook | Base: 1% annual efficiency improvement | Applied after activity growth; rail displacement is then applied to freight only
The assumptions are explicit and editable; EV uptake is not counted again as a separate reduction.
Executive summary
Situation
Complication
Resolution
Notes: Department 2023 sales; analytical workbook v02, Assumptions and Demand history. Activity and efficiency settings are authored planning assumptions.
The assumptions are explicit and editable; EV uptake is not counted again as a separate reduction.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 8: Eskom fuel use fell by about 40% in FY2025 as supply performance improved
Eskom Integrated Report 2025 p141; staged source series. 679.1m L diesel + kerosene supersedes the earlier slide’s 677.9m figure for this scope.
Strictly Confidential
Chart: 
| FY2023 | FY2024 | FY2025
Eskom diesel + kerosene, bn litres | 0.9375 | 1.1295 | 0.6791
Billion litres
Observed utility trend
FY2024: 1.130bn L
FY2025: 0.679bn L
The utility series includes kerosene. Fiscal years end in March.
The demand baseline replaces annual power consumption explicitly, so the decline is not hidden in a generic growth rate.
Executive summary
Situation
Complication
Resolution
Notes: Eskom Integrated Report 2025 p141; staged source series. 679.1m L diesel + kerosene supersedes the earlier slide’s 677.9m figure for this scope.
The demand baseline replaces annual power consumption explicitly, so the decline is not hidden in a generic growth rate.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 9: Further power recovery removes 0.54bn litres in the 2030 base case
Analytical workbook v02, Segments / Driver bridge. Private backup 2023/24/25: 0.8/0.6/0.2bn L. IPP conversion: 0.31 L/kWh. FY-to-calendar and fuel-mix assumptions apply.
Strictly Confidential
Power measure | Volume / assumption | Interpretation
2025 utility + private baseline | 1.08bn litres | Eskom FY proxy, IPP generation conversion and private backup
Private backup within 2025 baseline | 0.20bn litres assumed | Separate from reported Eskom fuel; not a measured national census
Base case to 2030 | 50% retained; 0.54bn L reduction | Recovery persists across utility and backup requirements
Sensitivity cases | 0.00–0.70bn L reduction | High-import case retains power use; low-import case retains 35%
Power demand can fall without an equivalent decline in transport or industrial demand.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Segments / Driver bridge. Private backup 2023/24/25: 0.8/0.6/0.2bn L. IPP conversion: 0.31 L/kWh. FY-to-calendar and fuel-mix assumptions apply.
Power demand can fall without an equivalent decline in transport or industrial demand.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 10: Road still carries most reported freight despite the recent recovery in rail volumes
Stats SA P7162 December 2025 p7; all reported freight. Analytical workbook v02, Evidence.
Strictly Confidential
Chart: 
| 2024 | 2025
Road, million tonnes | 979.798 | 976.468
Rail, million tonnes | 160.745 | 168.263
Million tonnes
Reported freight
Road: 979.8 → 976.5m tonnes
Rail: 160.7 → 168.3m tonnes
Tonnes measure payload, not tonne-kilometres or directly displaced diesel.
Rail recovery changes fuel demand through eligible freight, distance, truck efficiency and the rail traction mix.
Executive summary
Situation
Complication
Resolution
Notes: Stats SA P7162 December 2025 p7; all reported freight. Analytical workbook v02, Evidence.
Rail recovery changes fuel demand through eligible freight, distance, truck efficiency and the rail traction mix.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 11: A 7.5% shift of road-freight activity to rail saves 0.33bn litres in the base case
Analytical workbook v02, Driver bridge and scenario assumptions. Shift interpreted as freight tonne-km share. Distances and eligibility remain assumed; cases also vary growth and efficiency.
Strictly Confidential
2030 case | Road-freight shift | Net diesel reduction
Low imports | 15.0% | 0.62bn litres
Base | 7.5% | 0.33bn litres
High imports | 2.5% | 0.12bn litres
Calculation order | Activity → efficiency → modal shift | 10% diesel rebound allowance for rail
These shifts apply to road-freight activity, not the entire diesel market; sector demand and power remain separate.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Driver bridge and scenario assumptions. Shift interpreted as freight tonne-km share. Distances and eligibility remain assumed; cases also vary growth and efficiency.
These shifts apply to road-freight activity, not the entire diesel market; sector demand and power remain separate.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 12: The 5.8bn-litre production assumption leaves a gross import requirement of about 16.7bn litres
Analytical workbook v02, Balance and Supply assumption. User direction 11 October 2026. Original plant-based estimate 10.23bn L retained in appendix.
Strictly Confidential
2025 national balance | bn litres | Basis
Demand | 20.99 | Estimated from the 2023 sales baseline
Domestic production | 5.80 | User-directed national planning assumption
Gross imports | 16.70 | SARS recorded customs litres
Exports | 1.55 | SARS recorded customs litres
Production + net imports | 20.95 | Availability before stock / statistical differences
Availability less demand | -0.03 | Aggregate near-balance; product differences remain
5.8bn litres sets the planning case. Aggregate closure does not validate domestic output or its petrol/diesel split.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Balance and Supply assumption. User direction 11 October 2026. Original plant-based estimate 10.23bn L retained in appendix.
5.8bn litres sets the planning case. Aggregate closure does not validate domestic output or its petrol/diesel split.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 13: Refinery recovery is the largest downside risk to the import requirement
Registered scenario assumptions; DR08 refinery evidence. Capacity inputs: SAPREF 180kb/d, PetroSA 45kb/d; 70% petrol/diesel yield in restart sensitivities. Dates are not project commitments.
Strictly Confidential
Supply lever | Base case | Low-import sensitivity
Operating domestic supply | 5.8bn L through 2030 | 15% increase in the national planning volume
SAPREF | No refining restart through 2030 | Assumed 2029 start; 65% utilisation after a two-year ramp
PetroSA / Mossel Bay | No refining restart through 2030 | Assumed 2029 start; 50% utilisation after a two-year ramp
Combined restart contribution | Zero | 5.67bn L petrol/diesel in 2030
Restart dates and ramp-up settings are scenario assumptions. Import-terminal operations can compete before refining resumes.
Executive summary
Situation
Complication
Resolution
Notes: Registered scenario assumptions; DR08 refinery evidence. Capacity inputs: SAPREF 180kb/d, PetroSA 45kb/d; 70% petrol/diesel yield in restart sensitivities. Dates are not project commitments.
Restart dates and ramp-up settings are scenario assumptions. Import-terminal operations can compete before refining resumes.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 14: Base-case imports remain near 16.6bn litres; refinery recovery creates a much lower outcome
Analytical workbook v02, Scenarios. Demand-implied gross imports = demand − domestic supply + 2025 exports. Zero stock change; 5.8bn L directed opening supply.
Strictly Confidential
Chart: 
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Low imports | 16.7359 | 16.165 | 15.5984 | 15.0359 | 11.6443 | 8.2568
Base | 16.7359 | 16.708 | 16.681 | 16.6549 | 16.6295 | 16.6051
High imports | 16.7359 | 17.3083 | 17.8888 | 18.4777 | 19.0749 | 19.6808
Billion litres
2030 gross import need
Low imports: 8.26bn L
Base: 16.61bn L
High imports: 19.68bn L
Cases are sensitivities, not assigned probabilities.
The base case balances activity growth against efficiency, rail and power reductions; supply assumptions drive the widest spread.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Scenarios. Demand-implied gross imports = demand − domestic supply + 2025 exports. Zero stock change; 5.8bn L directed opening supply.
The base case balances activity growth against efficiency, rail and power reductions; supply assumptions drive the widest spread.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 15: Matola provides an existing alternative gateway; new gas projects have a different role
Galp Matola announcement (3 Dec 2020); Petromoc logistics; Sasol Mozambique operations; SARS customs. URLs retained in notes / workbook.
Strictly Confidential
Node | Evidence | Implication for South African fuel routes
Galp/IPG Matola | 60,000m³ petrol/diesel storage; opened 2020 | Existing import and distribution infrastructure
Petromoc Língamo / Matola | 390,000m³ across liquid fuels | Broader storage base; product allocation and overlap need confirmation
Beira, Nacala and Pemba | Existing central / northern logistics nodes | Regional supply; no additional SA flow assigned in the base case
Temane PSA | Light oil, gas and LPG; production began December 2025 | No direct finished petrol/diesel output credited
Komatipoort recorded imports | 0.303bn L in 2022 → 0.086bn L in 2025 | Current cross-border flow is far smaller than gross storage suggests
Storage capacity, berth capacity and delivered South African volumes measure different things and are not added together.
Executive summary
Situation
Complication
Resolution
Notes: Galp Matola announcement (3 Dec 2020); Petromoc logistics; Sasol Mozambique operations; SARS customs. URLs retained in notes / workbook.
Storage capacity, berth capacity and delivered South African volumes measure different things and are not added together.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 16: Matola needs a landed-price or service advantage to offset border and logistics costs
Analytical workbook v02, Mozambique. Distances, tariffs, border charges, financing and allocation are authored sensitivities, not carrier quotes or confirmed access.
Strictly Confidential
Route sensitivity | Result | Assumptions behind the result
Durban → same inland destination | R0.95 per litre logistics | 600km one way; round trip; R25/truck-km; 40,000L payload
Matola → same inland destination | R1.14 per litre logistics | 550km one way; terminal and border costs; one-day delay
Matola premium | R0.19 per litre | Required landed-product discount under these illustrative costs
Border-delay sensitivity | R0.09–R0.40 per litre premium | Zero to three delay days
Base incremental Mozambique flow | 0.20bn L by 2030 | About 15 additional loaded trucks/day over 330 days
Mozambique diversion changes the gateway serving demand. It does not reduce South Africa’s national import requirement.
Executive summary
Situation
Complication
Resolution
Notes: Analytical workbook v02, Mozambique. Distances, tariffs, border charges, financing and allocation are authored sensitivities, not carrier quotes or confirmed access.
Mozambique diversion changes the gateway serving demand. It does not reduce South Africa’s national import requirement.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 17: Vopak’s capture depends on the accessible share of Durban imports
Registered market_review.yaml and market_review.json, 10 October. Capture is total conditional flow, not incremental sales; domestic and other-terminal Lesedi receipts are outside this screen.
Strictly Confidential
Market / flow measure | Annual volume | Meaning for Vopak
National demand, 2025 estimate | 20.99bn litres | Total consumption context
National gross imports, 2025 | 16.70bn litres | All recorded import gateways
Durban customs imports, 2025 | 13.16bn litres | Gateway proxy before customer and route allocation
Illustrative Durban capture | 2.63bn litres | 20% of Durban gateway volume; no contracted share inferred
Illustrative onward Lesedi flow | 1.32bn litres | 50% of captured Durban flow; counted within the same fuel volume
The illustrative unique flow is 2.63bn litres. Adding Lesedi would double-count fuel handled at both sites.
Executive summary
Situation
Complication
Resolution
Notes: Registered market_review.yaml and market_review.json, 10 October. Capture is total conditional flow, not incremental sales; domestic and other-terminal Lesedi receipts are outside this screen.
The illustrative unique flow is 2.63bn litres. Adding Lesedi would double-count fuel handled at both sites.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 18: The illustrative capture case fits the tank-turn screen, making usable capacity the next test
Registered terminal_site_assumptions.csv and market_review.json. Durban working subset is not the full terminal; access, peaks and current throughput remain open.
Strictly Confidential
Site | Illustrative flow bn L/year | Handling screen bn L/year | Operating basis
Durban | 2.63 | 3.50 | 146,000m³ estimated working subset; two turns/month
Lesedi | 1.32 | 2.98 | 124,000m³ working capacity, partly estimated; two turns/month
Investment test | Incremental contracts | Actual constraint | Receipt, product segregation, dispatch, pipeline access and peak demand
Working-tank arithmetic screens feasibility. Engineering limits and current customer flows determine actual headroom.
Executive summary
Situation
Complication
Resolution
Notes: Registered terminal_site_assumptions.csv and market_review.json. Durban working subset is not the full terminal; access, peaks and current throughput remain open.
Working-tank arithmetic screens feasibility. Engineering limits and current customer flows determine actual headroom.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 19: The market supports an import platform; customer capture and capacity constraints govern investment
2025 analytical workbook v02: registered demand assumptions and user-directed 5.8bn L domestic production case. Estimates are not reported actuals.
Strictly Confidential
Conclusion | Evidence from this story | Decision implication
A substantial demand base | 2025 estimated demand of 21.0bn litres | Prioritise identifiable customer segments and destinations
Base imports remain substantial | About 16.6bn litres in 2030 under the 5.8bn supply case | Plan for ongoing imports; retain refinery sensitivities
Gateways compete for the same fuel | Mozambique base diversion of 0.20bn L is a route assumption | Validate delivered cost, service and customer access
Expansion follows incremental capture | Illustrative 2.63bn L unique flow fits the tank-turn screen | Secure additional volumes, prove the bottleneck, then compare improvement and expansion returns
Next decisions: review the product balance, obtain route quotes and customer commitments, and establish usable capacity at both sites.
Executive summary
Situation
Complication
Resolution
Notes: 2025 analytical workbook v02: registered demand assumptions and user-directed 5.8bn L domestic production case. Estimates are not reported actuals.
Next decisions: review the product balance, obtain route quotes and customer commitments, and establish usable capacity at both sites.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 20: HG’s South Africa storyline
Source: HG’s supplied storyboard, slides 30–32 (6 October 2026). Condensed framing; propositions and questions to investigate. Pages 2-19 present the current analytical response.
Strictly Confidential
SITUATION ¦ The market and its drivers | COMPLICATION ¦ Trends begin to reverse | RESOLUTION ¦ Vopak’s outlook
Outline South African demand development and Vopak’s market of interest: eastern South Africa within economic reach of its storage infrastructure and NMPP. Explain the demand drivers: greater diesel use in power generation; rail to road; fuel prices; more efficient vehicles; and slow GDP growth. Outline the supply picture: refinery closures, challenges at Secunda and closure of Mossgas. Show growth in imports and where they enter. | A number of trends that supported demand growth have started to reverse: road to rail; the end of loadshedding and spare generation capacity; EVs/HEVs; and higher fuel prices affecting kilometres travelled. Explore supply changes: a SAPREF restart; Secunda’s coal-derived gas, MRG sales and potential extension to 2032; and Natref’s future. Compare Durban storage–NMPP–Lesedi with road/rail from Durban, transport from Matola and transport from Walvis Bay. | Market share of Vopak in Durban and Lesedi Potential scope for new investment?
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Condensed from the supplied HG/Henry storyboard, external/partner_story_20261006/situation.png, complication.png and resolution.png. This page preserves the original analytical brief without inserting subsequent answers, capture assumptions or progress claims. Demand mechanism detail in the original: use Stats SA land transport and project private-sector rail participation; project EV/HEV penetration and its effect on litres per kilometre; assess higher fuel prices and kilometres travelled. Secunda original proposition: improved pure gas production from coal, potential diversion from fuel production due to MRG sales and possible extension to 2032. These are HG's propositions for analysis, not independently established outcomes. Full original wording is traced in workstreams/WS3_reporting_delivery/henry_verbatim_trace_2026-10-06.md and pptx/story/henry_question_answers_2026_10_06.json.

## Slide 21: The national supply assumption closes the total balance but leaves the product mix unresolved
Analytical workbook v02, Supply assumption and Balance. Original plant estimate: Secunda 3.95, Natref 2.37, Astron 3.91bn L; 10.23bn total. These do not govern the directed case.
Strictly Confidential
2025 measure | Petrol bn L | Diesel bn L | Total bn L
2025 demand | 8.86 | 12.13 | 20.99
Domestic production | 3.20 | 2.60 | 5.80
Gross customs imports | 4.45 | 12.25 | 16.70
Customs exports | 0.80 | 0.75 | 1.55
Supply plus net imports | 6.85 | 14.10 | 20.95
Unexplained availability less demand | -2.00 | 1.97 | -0.03
The 5.8bn L override uses the original estimated production mix. Offsetting product differences remain visible; no product allocation is claimed as verified.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Analytical workbook v02, Supply assumption and Balance. Original plant estimate: Secunda 3.95, Natref 2.37, Astron 3.91bn L; 10.23bn total. These do not govern the directed case.
The 5.8bn L override uses the original estimated production mix. Offsetting product differences remain visible; no product allocation is claimed as verified.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations

## Slide 22: The conclusions are traceable to sources and a small set of explicit planning assumptions
Source register: REG-SA-ANALYTICS-202510 and REG-SA-STORY-CASE-2025. Exception EXC-SA-ANALYTICS-202510; review before external use, expiry 12 November 2026.
Strictly Confidential
Evidence / assumption | Used on pages | Basis / next validation
National sales and sector activity | 2, 4–7 | Department sales; energy balances; Stats SA. Manish: sales coverage and segment boundaries
Power and freight | 3, 8–11 | Eskom / IPP and Stats SA. Nigel: backup demand, eligible rail shift and efficiency
Domestic supply and imports | 12–14, 21 | 5.8bn L user-directed supply; SARS trade. Manish: product-level reconciliation
Mozambique infrastructure and costs | 15–16 | Operator disclosures; authored cost sensitivities. Nigel: comparable quotes and access
Vopak capture and handling | 17–19 | Registered illustrative capture and working tanks. Vopak/Nigel: contracts and operating limits
Planning assumptions remain editable in workbook v02. Source observations, estimates and sensitivities retain separate labels.
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Source register: REG-SA-ANALYTICS-202510 and REG-SA-STORY-CASE-2025. Exception EXC-SA-ANALYTICS-202510; review before external use, expiry 12 November 2026.
Planning assumptions remain editable in workbook v02. Source observations, estimates and sensitivities retain separate labels.
Planning baseline: user-directed 5.8bn litres of domestic petrol/diesel production; not reported output. Workbook: SA_Fuel_Analytics_2025_Baseline_2026-10-11_v02.xlsx.
Mozambique sources: https://www.galp.com/corp/pt/media/comunicados-de-imprensa/comunicado/id/1172 ; https://www.petromoc.co.mz/product-service/logistica/ ; https://sasol.com/our-businesses/energy/gas-sourcing-and-operations