## Slide 1
Liquid fuels
demand and supply
model
Week 1 analytical pack
South Africa | Petrol and diesel
6 October 2026
Internal working discussion
Photo source: Royal Vopak | Terminal Durban | vopak.com
Notes: Speaker note: Walk through four sections: the project question, the analytical
requirements, the model-build problem and the delivery approach. The purpose is to
connect the analyst's tasks to the decisions the engagement needs to support.
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.

## Slide 2: Locate fuel demand alongside the infrastructure serving it
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Natural Earth 1:50m; kickoff appendix / schematic networks; illustrative regional CSV. 6 Oct 2026.
Infrastructure and regional demand | illustrative, bn litres/year
Key takeaways
01 · Seven infrastructure layers
Production, pipes, ports, roads, rail, storage and corridors establish the physical context.
02 · Demand volumes are illustrative
Inland demand is 10.0 bn litres; eastern/coastal demand is 4.5 bn litres. These are example volumes.
03 · Durban–Lesedi links the markets
Link coastal receipts, inland transfers and final deliveries without counting the same fuel twice.
04 · Proximity does not establish access
Routes, compatible capacity, delivered cost, contracts and competitors determine reachable demand.
N
0
500 km
NATREF
Sasol CTL
Astron
Cape Town
Gqeberha
Richards Bay
Durban
Lesedi*
Eastern / coastal
4.5 bn L
Inland
10.0 bn L
Western / coastal
4.0 bn L
Other regions
2.5 bn L
Production
Port
Vopak storage*
Road
Product pipe
Rail
Marker area = illustrative demand. Not a catchment boundary.
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No operational service-area polygon or evidence-calibrated cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. The graduated surface is illustrative delivered road transport cost: R0.15/litre dispatch plus R0.002/litre/km times shortest schematic-road distance and straight-line terminal/grid connections. These are authored example parameters, not carrier quotes or validated cost evidence. 25 km cells; cost classes <=0.75, 0.75-1.25, 1.25-1.75, 1.75-2.25 and >2.25 R/litre. Cells more than 100 km from the sampled road geometry or without a connected path remain unassessed. Fuel purchase price, tax, storage and pipeline tariffs are excluded. Operational speeds, capacity, permissions and commercial access are not evaluated. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson

## Slide 3: Map conditional market access from Durban and Lesedi
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Existing appendix routes; illustrative candidate connections, not verified catchments. Natural Earth 1:50m.
Road-delivery accessibility | illustrative transport cost, R/litre
Key takeaways
01 · Durban: coastal and inland links
Road candidates connect coastal customers and inland transfers. Pipelines are separate supply connections.
02 · Lesedi: inland dispatch
Test receipt, dispatch, tanker cycles and customer destinations for connected inland markets.
03 · Lower cost means higher accessibility
Darker cells show lower example road-delivery cost from either facility. Pipe and rail lines remain context.
04 · Customer access is unverified
Contracts and competitors define the commercial envelope. Actual customer catchments are not supplied.
N
0
500 km
Durban
Lesedi*
≤0.75
0.75–1.25
1.25–1.75
1.75–2.25
>2.25
R/litre
Example rate: R0.15/L dispatch + R0.002/L/km. Grey = unassessed.
Illustrative road cost only. Pipeline/rail access and commercial rights are not priced.
Unassessed
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No operational service-area polygon or evidence-calibrated cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. The graduated surface is illustrative delivered road transport cost: R0.15/litre dispatch plus R0.002/litre/km times shortest schematic-road distance and straight-line terminal/grid connections. These are authored example parameters, not carrier quotes or validated cost evidence. 25 km cells; cost classes <=0.75, 0.75-1.25, 1.25-1.75, 1.75-2.25 and >2.25 R/litre. Cells more than 100 km from the sampled road geometry or without a connected path remain unassessed. Fuel purchase price, tax, storage and pipeline tariffs are excluded. Operational speeds, capacity, permissions and commercial access are not evaluated. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson

## Slide 4: Separate demand, accessible volume and Vopak flows
1 About
2 Analytical specifications
3 Model build
4 Delivery approach
Source: Illustrative CSVs and road transport rates; no actual Vopak throughput or quoted transport costs supplied.
Cost accessibility and market volumes | illustrative
Key takeaways
01 · National balance sets import needs
Demand of 21.0 less domestic production of 7.0 gives required imports of 14.0 in this illustration.
02 · Count unique customer demand once
Receipts of 2.8 at Durban and 2.0 at Lesedi include a shared 1.8 transfer. Unique demand served is 3.0.
03 · Candidate opportunity is conditional
The example commercial envelope is 8.5; current unique demand served is 3.0, leaving a candidate 5.5.
04 · Replace examples with evidence
Match regional demand, route constraints, customer flows and contracts by product, period and units.
N
0
500 km
Durban
Lesedi*
Inland market | illustrative
Demand 10.0 | envelope 6.0
Current 2.0 | candidate 4.0
Eastern/coastal | illustrative
Demand 4.5 | envelope 2.5
Current 1.0 | candidate 1.5
≤0.75
0.75–1.25
1.25–1.75
1.75–2.25
>2.25
R/litre
Receipts 2.8 + 2.0 − transfer 1.8 = unique demand 3.0
Example rates: R0.15/L + R0.002/L/km. Grey = unassessed. Volumes: bn L/year.
Unassessed
Notes: Map uses WGS84 / Lambert azimuthal equal-area, centred 25°E, 29°S. Natural Earth 1:50m countries; schematic transport from the kickoff appendix. Scale is nominal at map centre. Facility points are approximate, inherited from the appendix, not surveyed GPS. Lesedi uses the inherited Jameson Park-area point. No operational service-area polygon or evidence-calibrated cost/time threshold is computed. Demand positions are regional annotations, not provincial centroids. All numerical volumes are illustrative and are not model outputs or actual Vopak flows. The graduated surface is illustrative delivered road transport cost: R0.15/litre dispatch plus R0.002/litre/km times shortest schematic-road distance and straight-line terminal/grid connections. These are authored example parameters, not carrier quotes or validated cost evidence. 25 km cells; cost classes <=0.75, 0.75-1.25, 1.25-1.75, 1.75-2.25 and >2.25 R/litre. Cells more than 100 km from the sampled road geometry or without a connected path remain unassessed. Fuel purchase price, tax, storage and pipeline tariffs are excluded. Operational speeds, capacity, permissions and commercial access are not evaluated. Natural Earth source: https://github.com/nvkelso/natural-earth-vector/blob/master/geojson/ne_50m_admin_0_countries.geojson

## Slide 5
Agree priorities
and next steps
Confirm demand, routes and access
6 October 2026
Internal working discussion
Photo source: Royal Vopak | Terminal Lesedi | vopak.com
Notes: Source note: Closing cover photograph: Royal Vopak, Terminal Lesedi. https://www.vopak.com/terminals/vopak-terminal-lesedi
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.