## Slide 1
South Africa liquid fuels market story
Inland supply, corridor capture and tank turnover
Durban–Lesedi corridor into Gauteng
8 October 2026
Investment conditions, nine-world priorities and targeted data requests; commercial thresholds remain open
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: Speaker note: Walk through four sections: the project question, the analytical
requirements, the model-build problem and the delivery approach. The purpose is to
connect the analyst's tasks to the decisions the engagement needs to support.
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
Final structure: baseline pp3–6; changes pp7–11 (forecast framework p9); outlook pp12–17 (market choices p16, inventory p17). Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
Final structure: baseline pp3–6; changes pp7–11 (forecast framework p9); outlook pp12–17 (market choices p16, inventory p17). Current page 1.

## Slide 2: Slow demand growth and greater import reliance set the baseline; road-to-rail shifts, EV adoption, power recovery and refinery changes could reshape the outlook
Executive summary — baseline and changes. Comparable historical periods differ: Department sales 2013–2023; SARS imports 2020–2025; Eskom FY2025 vs FY2024 (own diesel + kerosene). M/M is a reference framework, not a calibrated forecast.
Baseline / reference | What the evidence establishes | What changes the outlook
Fuel demand and power | 2013–2023 CAGR: petrol −2.08%; diesel +0.82%. Eskom OCGT fuel use fell 40% in FY2025. | Growth, rail, EVs and efficiency alter transport demand; fleet recovery and new generation alter diesel dispatch.
Domestic supply and imports | 2020–2025 imports rose by 5.43bn litres of diesel and 2.73bn of petrol. The sourcing mix has shifted. | SAPREF and PetroSA restart paths, Secunda gas/MRG and Natref output can change domestic supply.
Corridor position and tank turnover | Durban and Lesedi provide coastal and inland assets serving Gauteng. Working capacity and turns are open. | Route costs, access and customer capture determine flow; achievable turnover determines handling headroom.
Medium / Medium reference world | M/M anchors the nine-world matrix. Historical evidence is assembled; numerical calibration remains open. | Vary demand and supply around M/M, then test capture, turnover and returns to identify investment triggers.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Notes: Executive summary — baseline and changes. Comparable historical periods differ: Department sales 2013–2023; SARS imports 2020–2025; Eskom FY2025 vs FY2024 (own diesel + kerosene). M/M is a reference framework, not a calibrated forecast.

## Slide 3: Prioritise capture and turnover through existing assets; expand where profitable demand exceeds achievable capacity
Working recommendation, not an approved investment. Four numeric decision tests follow on p4; nine-world investment priorities on p5. Customer, operating and commercial inputs remain open.
Working recommendation | Investment logic | Condition for commitment
Capture inland supply | Win accessible customer flows from imported and domestic sources. | Prove delivered competitiveness and sufficient customer volume.
Use existing assets first | Increase turnover where tanks and receipt/dispatch allow. | Confirm working capacity and the actual operating constraint.
Stage corridor and capacity spend | Compare access improvements, rail loading, debottlenecking and new tanks. | Fund the least-cost viable option that removes the proven constraint.
Keep strategic options open | Test all nine worlds and emerging gateways; screen EV adjacencies separately. | Apply p4 to fuel-capacity expansion; assess operational and EV options on their own economics.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Notes: Working recommendation, not an approved investment. Four numeric decision tests follow on p4; nine-world investment priorities on p5. Customer, operating and commercial inputs remain open.

## Slide 4: Expand fuel-logistics capacity only when four investment tests pass
Decision rules for fuel-capacity expansion, not measured results. Gross turns indicate scale, not achievable working capacity; Durban includes mixed products. Full NPV requires project cash flows. Cost-saving improvements need their own incremental-return test; EV investment is assessed separately. SCR synthesis: p34.
Decision test | Numeric condition | What we know now | Investment consequence
Customer volume | Secured incremental m³/year ≥ break-even m³/year. | Volume threshold: pending customer commitments, rates and project costs. | Size and phase the option to the volume that can actually be won.
Route economics | Delivered-cost headroom ≥ R0/m³ after the required margin. | Headroom: pending matched quotes for the same product and destination. | Include emerging Maputo and Walvis Bay routes and domestic alternatives.
Capacity constraint | Captured m³/year − achievable m³/year > 0. | Actual shortfall: unknown. Each 1bn L/year equals 0.23 Durban / 0.60 Lesedi gross monthly turns. | Improve access or dispatch first where they bind; add tanks only if storage binds.
Incremental return | NPV > R0 at the agreed hurdle rate. | NPV and hurdle: pending finance inputs. Test ramp-up and downside volumes. | Select a viable option and stage commitment against contracts and delivery.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Notes: Decision rules for fuel-capacity expansion, not measured results. Gross turns indicate scale, not achievable working capacity; Durban includes mixed products. Full NPV requires project cash flows. Cost-saving improvements need their own incremental-return test; EV investment is assessed separately. SCR synthesis: p34.

## Slide 5: Nine worlds identify investment priorities; capacity expansion must pass the four tests
Qualitative priorities, not calculated recommendations. Rail options need volume, access and returns; rail freight recovery also changes fuel demand. EV adjacencies require a separate customer case and are not implied by low demand. Lever definitions remain in the appendix; original import-direction matrix retained in v22 and slide notes.
Fuel demand / domestic supply | HIGH supply | MEDIUM supply | LOW supply
LOW demand | L / H DEFEND UTILISATION Prioritise low-capex efficiency. Screen rail access / EV adjacencies. | L / M PHASE COMMITMENTS Debottleneck proven constraints. Screen EV adjacencies separately. | L / L REPLACE LOST SUPPLY Test import corridor / rail access. Add tanks only after the four tests.
MEDIUM demand | M / H CAPTURE DOMESTIC FLOWS Test inland / rail connections. Defer unsupported import expansion. | M / M BASELINE CHOICE Use tanks better; price rail access. Stage capacity behind contracts. | M / L SECURE IMPORT ACCESS Test corridor / rail debottlenecks. Expand only at binding limits.
HIGH demand | H / H EXPAND DISTRIBUTION Test inland links and rail access. Tank growth follows captured flow. | H / M UNLOCK THROUGHPUT Debottleneck corridor / dispatch. Add tanks if shortfall persists. | H / L TEST STAGED EXPANSION Secure import / corridor capacity. Test rail access and extra tanks.
Strictly Confidential
Each world: captured volume → route economics → required turns / bottleneck → investment option → return.
Executive summary
Situation
Complication
Resolution
Notes: Qualitative priorities, not calculated recommendations. Rail options need volume, access and returns; rail freight recovery also changes fuel demand. EV adjacencies require a separate customer case and are not implied by low demand. Lever definitions remain in the appendix; original import-direction matrix retained in v22 and slide notes.
Original import-direction framework: [["LOW demand\nD1–D5", "L / H\nLOWEST IMPORT PRESSURE\nDomestic routing and customer capture still determine terminal turns.", "L / M\nLower imports than baseline.\nTest utilisation and customer capture.", "L / L\nDemand and supply both fall.\nNet import effect depends on their relative change."], ["MEDIUM demand\nD1–D5", "M / H\nLower imports than baseline.\nSupply recovery reduces import needs.", "M / M\nBASELINE\nReference sourcing, captured throughput, required turns and headroom.", "M / L\nHigher imports than baseline.\nSupply losses increase import needs."], ["HIGH demand\nD1–D5", "H / H\nDemand and supply both rise.\nNet import effect depends on their relative change.", "H / M\nHigher imports than baseline.\nDemand growth increases import needs.", "H / L\nHIGHEST IMPORT PRESSURE\nTest the captured flow against working capacity and achievable turns."]]

## Slide 6: Petrol demand has declined while diesel has grown slowly, limiting the case for demand-led expansion outlook
Department sales 2013–2023. CAGR from comparable endpoints: petrol −2.08%, diesel +0.82%. FIASA 2024 is excluded from the trend calculation; its observations remain in the evidence data.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
The demand history supports a selective investment case: growth must translate into captured corridor throughput and sufficient tank turns.
Demand trend
Change over 2013–2023
Notes: Department sales 2013–2023. CAGR from comparable endpoints: petrol −2.08%, diesel +0.82%. FIASA 2024 is excluded from the trend calculation; its observations remain in the evidence data.

## Slide 7: Power shortages and road freight have supported diesel consumption, but that support can change with increased support for rail reform and improved Eskom
Eskom Integrated Report 2025 pp100,141: own-fleet diesel + kerosene; *cost includes storage/demurrage. Stats SA P7162 Dec 2025 p7: both years from the revised vintage. Stats SA P0441 Q2 2026 annual real GVA: agriculture includes forestry/fishing. FY and calendar-year periods shown separately. Bars start at zero; scales are common within each panel, not across different units. Light blue = 2024; navy = 2025.
Demand support | 2024 vs 2025 | Implication for demand
Power generation |  | 450m fewer litres in one year. Sustained recovery reduces diesel demand; retirements and replacement timing could reverse it.
Road freight |  | Road still carries 85.3% of tonnes. Rail recovery reduces diesel use only where freight transfers and net fuel savings follow.
Sector activity |  | Agriculture grew; mining was flat and manufacturing declined. Sector activity matters more than one GDP assumption.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Own OCGT fuel · million litres · financial years
Reported payload · million tonnes · calendar years
Real GVA · Rbn, 2015 prices · calendar years
Notes: Eskom Integrated Report 2025 pp100,141: own-fleet diesel + kerosene; *cost includes storage/demurrage. Stats SA P7162 Dec 2025 p7: both years from the revised vintage. Stats SA P0441 Q2 2026 annual real GVA: agriculture includes forestry/fishing. FY and calendar-year periods shown separately. Bars start at zero; scales are common within each panel, not across different units. Light blue = 2024; navy = 2025.

## Slide 8: The shut down of domestic refining capacity has lowered domestic production and has increased imports shifting how inland demand is supplied
SARS litre-reported petrol/diesel codes, complete calendar years. 2020–2025 changes are historical comparisons, not plant-level causal attribution. Export histories retained in the source report; unit/blend exclusions remain.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Additional imported litres create handling demand. Vopak benefits where it captures inland flows and can increase turnover or profitably remove a constraint.
Import trend
Change since 2020
Notes: SARS litre-reported petrol/diesel codes, complete calendar years. 2020–2025 changes are historical comparisons, not plant-level causal attribution. Export histories retained in the source report; unit/blend exclusions remain.

## Slide 9: Emerging Maputo and Walvis Bay routes must be tested alongside Durban and domestic supply
© OpenStreetMap contributors (ODbL; osm.org/copyright) / Geofabrik; Natural Earth; geoBoundaries. Shared LAEA projection. Paths test road connectivity, not tanker access. Secunda uses a city reference; Natref a mapped site. Terminal access, turn restrictions and operating rail/pipeline services remain unvalidated. Emerging alternatives are in scope; relative competitiveness is not yet quantified.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Maputo and Walvis Bay are emerging alternatives to include by destination. Compare delivered cost, capacity and reliable access before estimating how much inland demand Vopak can capture.
Competing supply corridors
Same product, same destination
Notes: © OpenStreetMap contributors (ODbL; osm.org/copyright) / Geofabrik; Natural Earth; geoBoundaries. Shared LAEA projection. Paths test road connectivity, not tanker access. Secunda uses a city reference; Natref a mapped site. Terminal access, turn restrictions and operating rail/pipeline services remain unvalidated. Emerging alternatives are in scope; relative competitiveness is not yet quantified.

## Slide 10: Increasing asset utilisation through higher turnover could let Durban and Lesedi serve more demand through existing tanks and corridor growth opportunities
Registered REG-TERMINAL-HANDLING-TURNS: 1/2/3 turns per month, authored operational sensitivity, not the demand–supply worlds or measured limits. Gross Durban mixed-product tankage; no assumed eligible fraction. Do not sum inter-terminal transfers as unique demand.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Required working-capacity turns must be compared with achievable turns at each terminal. Gross handling equivalents do not establish spare capacity or actual market share.
Gross handling sensitivity
Investment test
Notes: Registered REG-TERMINAL-HANDLING-TURNS: 1/2/3 turns per month, authored operational sensitivity, not the demand–supply worlds or measured limits. Gross Durban mixed-product tankage; no assumed eligible fraction. Do not sum inter-terminal transfers as unique demand.

## Slide 11: Accelerated rail recovery, EV adoption and ICE technology efficiency could reduce transport fuel demand in the medium to long term
Stats SA freight payload; staged naamsa BEV/PHEV annual sales 2019–2025; existing engine petrol-ICE efficiency diagnostics. Dashed efficiency paths are assumptions, not historical OEM evidence. Medium and causal fuel impacts remain uncalibrated.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
The time series establish the starting points. Rail, adoption and efficiency levers must be calibrated into the same three demand paths before the matrix is quantified.
Notes: Stats SA freight payload; staged naamsa BEV/PHEV annual sales 2019–2025; existing engine petrol-ICE efficiency diagnostics. Dashed efficiency paths are assumptions, not historical OEM evidence. Medium and causal fuel impacts remain uncalibrated.

## Slide 12: Power generation recovery could lower diesel use further, while outages and replacement delays could sustain domestic demand
Eskom FY ending March. Fuel/EAF: 2025 report; GWh: staged 2024–2026 reports. Own Eskom and IPP generation separated. Private backup and load-shedding histories are missing; no assumed annual generation gap is assigned entirely to diesel.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Eskom recovery has lowered diesel dispatch. Wind, solar and gas timing must be tested against demand, fleet retirements and dependable output before forecasting residual diesel.
Diesel use
Fleet availability
Peaking generation
Notes: Eskom FY ending March. Fuel/EAF: 2025 report; GWh: staged 2024–2026 reports. Own Eskom and IPP generation separated. Private backup and load-shedding histories are missing; no assumed annual generation gap is assigned entirely to diesel.

## Slide 13: SAPREF could expand the supply footprint, while Natref unavailability would reduce it
FIASA 2025 p49; registered review_capacity_scenarios.yaml and review_supply_worlds.yaml. Illustrative 2036 sensitivities, not calibrated production forecasts. Other plants held at 2025 reported values; Secunda gas/MRG and PetroSA restart effects remain unquantified. Low is not a Natref closure prediction.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
These capacity cases anchor the supply-axis discussion. Translate them into product output, then test imports, corridor capture and required tank turns in each of the nine worlds.
Reported history
Illustrative 2036 capacity cases
Notes: FIASA 2025 p49; registered review_capacity_scenarios.yaml and review_supply_worlds.yaml. Illustrative 2036 sensitivities, not calibrated production forecasts. Other plants held at 2025 reported values; Secunda gas/MRG and PetroSA restart effects remain unquantified. Low is not a Natref closure prediction.

## Slide 14: Emerging gateways could redirect inland growth; delivered cost and reliable access determine capture
Compare common product, destination, price date and tax basis. Emerging gateways must be considered; no relative cost ranking is asserted without quotes and verified access. Landlocked SADC opportunities require separate market/access evidence.
Competing route | What changes the choice | Investment implication
Durban–Lesedi | Pipeline, rail and road costs; reliable receipt and inland dispatch. | Test access and handling improvements that protect competitive customer supply.
Maputo / Matola | Delivered cost, border time and capacity into each inland destination. | Include as an emerging alternative; test customer exposure and corridor responses.
Walvis Bay | Distance, transit, border costs and feasible destination coverage. | Consider emerging inland opportunities; compare reach customer by customer.
Domestic sources | Secunda / Natref availability, product output and distribution access. | Test inland handling and connections as well as import infrastructure.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Notes: Compare common product, destination, price date and tax basis. Emerging gateways must be considered; no relative cost ranking is asserted without quotes and verified access. Landlocked SADC opportunities require separate market/access evidence.

## Slide 15: Choose the investment that removes the proven constraint—and earns a return
Investment menu, not approved projects. Network rail recovery is an external fuel-demand driver; Vopak rail loading/access is a distinct investment option. EV uptake reduces some fuel demand; it does not itself prove an EV investment case. Project costs, contracts and returns remain open.
Investment option | When it becomes relevant | Decision / commitment trigger
Existing assets / debottlenecking | Customer growth can be served through better tank turns, scheduling or receipt/dispatch. | Use available working capacity; invest in the specific bottleneck where incremental value is positive.
Corridor / rail access | Competitive customer flows are constrained by transport capacity, cost or reliability. | Secure service and volume commitments. Compare access contracts, loading assets and partnership investment.
Additional tank capacity | Profitable captured flows exceed achievable handling and storage remains the binding constraint. | Size and stage tanks against contracted demand; pass the four tests and downside cases.
EV-related adjacencies | Identified charging / fleet-energy customers offer a viable opportunity as transport electrifies. | Screen partnerships or dedicated assets separately: demand, power access, strategic fit and return must be proven.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Notes: Investment menu, not approved projects. Network rail recovery is an external fuel-demand driver; Vopak rail loading/access is a distinct investment option. EV uptake reduces some fuel demand; it does not itself prove an EV investment case. Project costs, contracts and returns remain open.

## Slide 16: Resolve customer volume, working capacity and project economics first to determine the investment
Request prepared, not sent. Sequence is proposed, not a quantified sensitivity ranking. Nigel to coordinate Vopak data; Manish to reconcile public evidence. Latest 36 complete months where available. Detailed requests and decision triggers logged; owners and commercial inputs remain to be confirmed.
Data request | Required detail | Decision it unlocks
FIRST ¦ Volume DR02 / DR05 | Monthly unique deliveries, customer destination, contract term and contestable volumes; separate terminal transfers. | Establish the m³/year Vopak can secure and the revenue it supports.
FIRST ¦ Capacity DR03 | Eligible working m³, actual turns, committed capacity, stock policy and receipt/dispatch limits. | Calculate the throughput shortfall and identify whether tanks, access or dispatch bind.
FIRST ¦ Economics DR04 / DR06 | Matched delivered costs, access, rates, incremental costs and capex; hurdle, ramp-up and working capital. | Calculate route headroom, break-even volume and incremental return by option.
THEN ¦ Stress tests DR01 / DR07 / DR08 | Reconciled product balance; annual demand, power and plant-output paths. | Test how far demand or supply must change before the preferred investment changes.
SEPARATE ¦ EV case DR09 | Customer energy demand, charging utilisation, power connection, delivery partner, capex and contribution. | Decide whether an EV adjacency merits development on its own economics.
Strictly Confidential
Executive summary
Situation
Complication
Resolution
Notes: Request prepared, not sent. Sequence is proposed, not a quantified sensitivity ranking. Nigel to coordinate Vopak data; Manish to reconcile public evidence. Latest 36 complete months where available. Detailed requests and decision triggers logged; owners and commercial inputs remain to be confirmed.

## Slide 17
Appendix
Supporting evidence and calibration
Durban–Lesedi corridor into Gauteng
8 October 2026
Detailed evidence, assumptions and remaining calibration requirements
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
17
Notes: Speaker note: Walk through four sections: the project question, the analytical
requirements, the model-build problem and the delivery approach. The purpose is to
connect the analyst's tasks to the decisions the engagement needs to support.
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
Final structure: baseline pp3–6; changes pp7–11 (forecast framework p9); outlook pp12–17 (market choices p16, inventory p17). Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
Final structure: baseline pp3–6; changes pp7–11 (forecast framework p9); outlook pp12–17 (market choices p16, inventory p17). Current page 1.

## Slide 18: The supporting evidence calibrates demand, supply and the terminal investment tests
The main story runs from the opening thesis to the investment tests. The added lever register and power/supply calibration pages record what remains to be populated.
Evidence group | Detail retained | Connection to the story
Demand | Activity, freight, EVs, efficiency and power | D1–D5 create the three demand paths.
Supply | Plant output, gas availability and restart timing | S1–S4 create the three domestic-supply paths.
Capture and operations | Routes, customer share, working tankage and turnover | T1–T5 translate each world into terminal flows and constraints.
Returns | Rates, costs, capex and funding; separate EV adjacency economics. | F1 translates each investment option into cash flow and returns.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: The main story runs from the opening thesis to the investment tests. The added lever register and power/supply calibration pages record what remains to be populated.

## Slide 19: Fuel demand has diverged from GDP, so sector activity and fuel intensity need separate treatment
Staged GDP and department fuel sales, indices 2013=100. Sector attribution remains open; COVID distorts short-period comparisons.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Economic weakness means limited growth in real activity and investment. Structural change means a different mix of output, travel and fuel use; this chart alone cannot attribute causality.
Notes: Staged GDP and department fuel sales, indices 2013=100. Sector attribution remains open; COVID distorts short-period comparisons.

## Slide 20: Fixed investment has weakened while FDI fluctuates, limiting a simple growth-led fuel argument
World Bank WDI, FDI net inflows and gross fixed capital formation as % of GDP, 2010–2025. Confidence series remains an evidence gap.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Fixed investment helps frame productive capacity. FDI can include large transactions; neither series is a direct investor-confidence measure or an additional fuel-demand multiplier.
Notes: World Bank WDI, FDI net inflows and gross fixed capital formation as % of GDP, 2010–2025. Confidence series remains an evidence gap.

## Slide 21: Mining, agriculture and aviation expose fuel demand to different activity drivers
Analytical framework following user comments. Sector-specific exhibits and causal attribution remain to be completed.
Evidence | Interpretation | Implication for Vopak
Mining | Output, commodity mix and haul distance influence diesel use and freight. | Separate mine activity from the fuel impact of changing freight mode.
Agriculture | Crop cycles, weather, irrigation and logistics can shift seasonal diesel use. | Establish sector activity and fuel exposure before assigning a headwind.
Aviation | Traffic, distance, load factors and aircraft efficiency drive jet-fuel demand. | Keep jet fuel separate from petrol/diesel shares and verify terminal eligibility.
Manufacturing | Real output and industrial composition help explain the economic backdrop. | Test changes using sector data; a national fuel chart does not prove deindustrialisation.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Analytical framework following user comments. Sector-specific exhibits and causal attribution remain to be completed.

## Slide 22: Higher fuel prices strengthen EV running-cost incentives, but ownership economics determine uptake
Department fuel-price history, nominal R/litre. No quantified geopolitical premium or calibrated EV adoption response is asserted.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Shipping disruption, crude prices and FX can move fuel costs temporarily. EV adoption depends on sustained total ownership cost, purchase affordability, charging access and fleet replacement.
Notes: Department fuel-price history, nominal R/litre. No quantified geopolitical premium or calibrated EV adoption response is asserted.

## Slide 23: New-vehicle efficiency gains affect fuel demand gradually as older vehicles leave the fleet
Mechanism supported by existing cohort architecture. OEM historical and future efficiency evidence is still missing; no new forecast shown.
Evidence | Interpretation | Implication for Vopak
Fleet growth | More vehicles or distance travelled can raise demand. | Measure activity before attributing lower fuel volumes to efficiency.
Efficiency | New-cohort consumption gains enter the fleet over successive replacement cycles. | Obtain OEM and real-world evidence by segment; do not apply new-vehicle gains to every vehicle.
EV substitution | EVs remove some combustion-engine vehicle activity from the fuel calculation. | Count each vehicle transition once, then calculate efficiency on the remaining combustion fleet.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Mechanism supported by existing cohort architecture. OEM historical and future efficiency evidence is still missing; no new forecast shown.

## Slide 24: Eskom’s own OCGT fuel use fell 40% in FY2025 as availability improved
Eskom integrated report 2025: FY March, own-fleet diesel + kerosene. EAF association is not a dispatch model; private backup use excluded.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Reported fuel fell from 1,129.5 to 679.1 million litres as EAF improved from 54.56% to 60.60%. This removes part of the recent diesel-demand support.
Notes: Eskom integrated report 2025: FY March, own-fleet diesel + kerosene. EAF association is not a dispatch model; private backup use excluded.

## Slide 25: Road carries most reported freight tonnage, making transferable haul distance a key diesel lever
Stats SA monthly freight payload, complete calendar years. National tonnes are not corridor tonne-kilometres or transferable freight.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Payload establishes the historical direction. Diesel displacement requires corridor tonne-kilometres, road fuel intensity, rail traction and last-mile activity.
Notes: Stats SA monthly freight payload, complete calendar years. National tonnes are not corridor tonne-kilometres or transferable freight.

## Slide 26: Rail funding and reliable service determine how much road freight can return to rail
User-supplied AIA Transnet Funding Brief, Sep 2026, pp1–2; cites FY2026 AFS and Network Statement v4 Annexure 17. Primary figures not independently reconciled.
Evidence | Interpretation | Implication for Vopak
Network ambition | The supplied brief reports a 250 Mt target dependent on a funding plan. | Do not treat every additional rail tonne as road displacement. Commodity, corridor and origin matter.
Funding constraint | Brief: R46.34bn approved over five years, including R1.71bn expansion. | Maintenance and sustaining spend dominate. A published plan is insufficient evidence of delivered capacity.
Container corridor | Brief: R2.11bn in 2026/27–2028/29; private funding expected thereafter. | Prioritise Durban–Gauteng road/rail competition and reconcile the corridor to Network Statement v4.
Two fuel effects | Rail can displace truck diesel while improved infrastructure also changes fuel-distribution economics. | Keep freight-demand effects separate from the route delivering fuel to Gauteng.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: User-supplied AIA Transnet Funding Brief, Sep 2026, pp1–2; cites FY2026 AFS and Network Statement v4 Annexure 17. Primary figures not independently reconciled.

## Slide 27: Gauteng demand establishes market scale, while Lesedi capture and turnover determine throughput
Department provincial sales, latest complete staged year 2022; Vopak Lesedi current capacity. Cross-vintage scale test only, not current observed market share.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
2022 petrol + diesel sales total 6.81bn litres. Lesedi’s 140,000m³ equals 2.06% of that annual market per effective gross-capacity turn. Actual turns and Gauteng allocation remain unknown.
Notes: Department provincial sales, latest complete staged year 2022; Vopak Lesedi current capacity. Cross-vintage scale test only, not current observed market share.

## Slide 28: Every market world passes through explicit demand, supply, capture and operating levers
Medium is the reference market world; operational sensitivities are separate. Owner: Nigel / analyst and commercial teams. Resolve each missing input before numeric adoption or investment reliance.
Lever IDs | Inputs to calibrate | Output / remaining evidence
D1–D5 demand | D1 sector growth; D2 rail; D3 EV adoption; D4 efficiency; D5 power. | Historical volumes and time series feed L/M/H demand. OEM, corridor tonne-km and backup evidence remain open.
S1–S4 supply | S1 SAPREF; S2 Secunda gas/MRG; S3 Natref; S4 PetroSA. | Dates, utilisation, availability and yields produce L/M/H domestic output. Medium and plant marginal effects require calibration.
T1–T2 capture | T1 delivered route economics/access; T2 customer/product/destination capture. | Allocate domestic and imported fuel to unique terminal deliveries. Tariffs, rights and commercial allocation remain open.
T3–T5 operations | T3 eligible working tankage; T4 turnover; T5 receipt/dispatch, peaks and stock policy. | Compare required with achievable turns, occupancy and headroom. Existing 1/2/3-turn sensitivity is illustrative only.
F1 finance | Storage/handling terms, costs, capex, tax, working capital and hurdle rate. | Translate constrained throughput into cash flow, NPV, IRR and investment triggers. Commercial inputs remain open.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Medium is the reference market world; operational sensitivities are separate. Owner: Nigel / analyst and commercial teams. Resolve each missing input before numeric adoption or investment reliance.

## Slide 29: Generation timing must close the power balance before residual diesel can be forecast
Requested generation-balance exhibit remains quantitatively incomplete. Owner: Nigel / power analyst; trigger: before D5 adoption. Do not convert installed renewable MW directly into dependable diesel displacement.
Time series | Assumption / lever | Evidence status and next use
Recovery history | EAF, unserved energy / load-shedding hours, OCGT GWh and litres. | EAF, Eskom fuel and Eskom/IPP GWh staged. Comparable load-shedding and private backup series still needed.
Generation supply by year | Existing fleet and retirement profile; wind, solar and gas commissioning; availability and utilisation. | Obtain dated Eskom / approved planning schedules. Report annual GWh alongside dependable capacity and dispatch constraints.
Residual dispatch | Electricity demand, hourly/seasonal shape, storage, imports, reserve needs and fuel constraints. | An annual GWh shortfall alone cannot determine diesel use. Calibrate feasible peaking dispatch, then apply consumption rates.
L/M/H demand contribution | Sustained recovery, reference and setback assumptions across the same planning horizon. | Output generation and diesel time series with solid actuals / dashed assumptions. No uncalibrated future values are drawn.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Requested generation-balance exhibit remains quantitatively incomplete. Owner: Nigel / power analyst; trigger: before D5 adoption. Do not convert installed renewable MW directly into dependable diesel displacement.

## Slide 30: SAPREF and Natref define capacity sensitivities; plant output must complete the supply paths
Illustrative footprint cases: 250 / 358 / 758 kbpd; not a complete low/base/high production range. Owner: Manish; Nigel review. Resolve dates, operating factors, yields and gas effects before nine-world output adoption or investment use.
Plant lever | Required time-series inputs | Scenario treatment
S1 SAPREF | High illustration adds 400 kbpd: assumed 2029 FID plus 48 months gives 2033 availability. Low/Medium add none. | Separate the import phase from refinery commissioning; establish ramp-up, availability and product yields.
S3 Natref | 108 kbpd retained in Medium/High; excluded in the Low stress case at 2036. No closure date assumed. | This is a hypothetical availability test. Confirm operating outlook; do not infer closure from an outage.
S2 Secunda | 150 kbpd reported crude-equivalent footprint held in all three capacity illustrations. | Gas decline and MRG diversion can reduce liquid output without changing nameplate. Quantify the gas balance and liquids penalty.
S4 PetroSA | No restart addition included in these three capacity illustrations. | Test funded restart scope, feedstock, timing and yields separately; zero reported contribution is not proof of dismantled capacity.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Illustrative footprint cases: 250 / 358 / 758 kbpd; not a complete low/base/high production range. Owner: Manish; Nigel review. Resolve dates, operating factors, yields and gas effects before nine-world output adoption or investment use.

## Slide 31: Public capacity ratios establish scale but cannot substitute for realised terminal throughput
Operator capacities: Vopak Durban 360,246m³, Bidvest Durban 439,306m³, Lesedi 140,000m³. Department Gauteng sales 2022; appendix p27. Transfers between terminals must not be double-counted.
Catchment | Initial inference | What the result can support
Durban | 45.1% of the combined published gross capacity of Vopak and Bidvest in Durban. | A two-operator footprint proxy with mixed products and an incomplete market denominator. It does not establish Durban throughput share.
Gauteng / Lesedi | 2022 petrol + diesel sales: 6.81bn litres. Lesedi’s gross capacity equals 2.06% of that market per effective annual turn. | A cross-vintage scale test. Current sales, eligible working capacity, actual turns and Gauteng allocation are needed for a throughput estimate.
Investment implication | Convert eligible tankage and realised turns into unique customer deliveries, then compare with existing capacity. | A large market can coexist with spare terminal capacity. Market scale alone does not establish a need for additional tanks.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Operator capacities: Vopak Durban 360,246m³, Bidvest Durban 439,306m³, Lesedi 140,000m³. Department Gauteng sales 2022; appendix p27. Transfers between terminals must not be double-counted.

## Slide 32: A matched demand snapshot is available, but the domestic supply balance still needs reconciliation
Department sales: four quarters; SARS trade: 12 months and litre units only, blends/other units excluded. 2021 energy-balance consumption differs from sales; statistical differences are not stock changes. Source hashes and exact values: investment_bridge_2026_10_08/evidence.json.
Evidence / bn litres | Petrol | Diesel
2022 national sales | 9.18 | 12.72
2022 Gauteng sales | 3.53 | 3.28
2022 imports / exports | 5.46 / 0.85 | 11.95 / 0.89
2021 balance diagnostic | 0.51 statistical difference needed to reconcile reported supply and final consumption. | 2.10 statistical difference needed to reconcile reported supply and final consumption.
Decision consequence | Sales less net imports is a residual, not measured domestic output. Confirm product and stock boundaries. | Provincial sales establish demand scale, not source allocation or flows captured by Vopak.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Department sales: four quarters; SARS trade: 12 months and litre units only, blends/other units excluded. 2021 energy-balance consumption differs from sales; statistical differences are not stock changes. Source hashes and exact values: investment_bridge_2026_10_08/evidence.json.

## Slide 33: The six-step bridge is implemented for screening; calibration now depends on the requested inputs
Screening functions tested with synthetic cases; commercial outputs remain unpopulated. Not integrated into the forecast engine or independently reviewed. Owners, request IDs and expiry triggers: workstreams/WS0_governance/workplan/sa_investment_bridge_2026_10_08.csv.
Work package | Implemented now | Input needed to complete the decision
1 ¦ Baseline | Matched 2022 sales/trade; 2021 balance diagnostic. | Reconcile production, stocks and source definitions.
2 ¦ Route competition | Delivered cost and bearable-charge calculation; route readiness register. | Matched quotes, service capacity and access.
3 ¦ Vopak capture | Capture calculation constrained by accessible market and route capacity. | Customer allocation and unique terminal deliveries.
4 ¦ Existing assets | Required-turn and operating-bottleneck calculation; gross-turn screen. | Working capacity, achievable turns and peak limits.
5 ¦ Investment options | Pre-tax break-even volume calculation. | Commercial inputs and full incremental cash flows.
6 ¦ Nine worlds | Nine-cell output register and demand/supply balance calculation. | Annual L/M/H paths; rerun routes, capture and returns.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Screening functions tested with synthetic cases; commercial outputs remain unpopulated. Not integrated into the forecast engine or independently reviewed. Owners, request IDs and expiry triggers: workstreams/WS0_governance/workplan/sa_investment_bridge_2026_10_08.csv.

## Slide 34: Demand, supply and corridor access translate into captured throughput and required tank turns
Lever IDs are mapped in the appendix. All nine market worlds use explicit routing, capture and operational assumptions. Tank occupancy, turnover and throughput utilisation are separate measures. Competitiveness varies by destination; neither alternative gateway is yet established as competitive into Gauteng.
Argument | Situation | Complication | Resolution / decision
Transport demand | Subdued aggregate growth masks different product trends. Road freight supports diesel use. | Sector growth, rail recovery, EVs and efficiency change fuel demand. | D1–D4 define activity, rail, EV and efficiency paths. Translate them into capturable product demand.
Power demand | Power shortages supported diesel use; Eskom consumption has recently fallen. | Recovery may persist or reverse through outages and replacement delays. | D5 adds fleet recovery, replacement timing and diesel dispatch to the same demand paths.
Domestic supply | Reduced local production has increased reliance on imports. | SAPREF, Natref and Secunda can change domestic fuel output materially. | S1–S4 define plant output and sourcing mix. Imports are one consequence of the domestic balance.
Corridor competition | Durban connects imported fuel to inland customers. | Alternative gateways, delivered costs, reliability and access alter flows. | T1–T2 compare delivered economics and capture for domestic and imported fuel serving common destinations.
Vopak investment | Durban and Lesedi provide connected assets whose throughput can rise through higher turnover. | Working tankage, receipt/dispatch, peaks and stock requirements constrain achievable turnover. | T3–T5 compare working capacity, required/achievable turns and dispatch limits. F1 tests incremental returns.
Strictly Confidential
Appendix
Supporting evidence
Calibration
Reference detail
Notes: Lever IDs are mapped in the appendix. All nine market worlds use explicit routing, capture and operational assumptions. Tank occupancy, turnover and throughput utilisation are separate measures. Competitiveness varies by destination; neither alternative gateway is yet established as competitive into Gauteng.