## Slide 1
South Africa liquid fuels market story
Investment thesis, scenario worlds and supporting evidence
Durban and Gauteng (Lesedi catchment)
7 October 2026
Top-down review draft; calibration pending
Photo source: Royal Vopak | Terminal Durban | vopak.com
Strictly Confidential
Notes: Speaker note: Walk through four sections: the project question, the analytical
requirements, the model-build problem and the delivery approach. The purpose is to
connect the analyst's tasks to the decisions the engagement needs to support.
Week 1 analytical pack, 6 October 2026. Existing kickoff cover/closing reused at user request.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
Final structure: baseline pp3–6; changes pp7–11 (forecast framework p9); outlook pp12–17 (market choices p16, inventory p17). Current page 1.
SCR delivery order: page 1 of 16. Gap IDs and original evidence references retained in notes.
6 October SCR editorial pass: presentation copy and map hierarchy only. Source observations, example volumes and model inputs unchanged.
Convergence order: national accounting p3; provincial map p4; history/estimates p5. Current page 1.
Final structure: baseline pp3–6; changes pp7–11 (forecast framework p9); outlook pp12–17 (market choices p16, inventory p17). Current page 1.

## Slide 2: Vopak’s investment case rests on capturing imports through its Durban–Gauteng chain
Working investment thesis, not an approved expansion recommendation. Supporting logic: p3; nine-world framework: p4; evidence and implications: pp5–14. Numerical calibration and commercial inputs remain open.
Investment thesis | Supporting reason | What determines the choice
Capture imported fuel | Limited demand growth can coexist with greater import needs as domestic production changes. | Establish how much of that import requirement is accessible through Durban and can be captured by Vopak.
Use the coastal–inland position | Durban and Lesedi give Vopak assets along the supply chain into Gauteng. | Delivered cost, reliable access and customer allocation determine throughput at each terminal.
Make expansion conditional | The relevant investment is the capacity or handling constraint that prevents profitable customer volumes being served. | Use existing assets, debottleneck or add storage according to capturable flow, usable capacity and incremental returns.
Test the thesis in nine worlds | Medium / Medium anchors the baseline. Low demand / High supply and High demand / Low supply frame contrasting import environments. | Choose an option that is justified across the relevant worlds, or phase commitment against explicit volume and return triggers.
Strictly Confidential
Situation
Complication
Resolution
Notes: Working investment thesis, not an approved expansion recommendation. Supporting logic: p3; nine-world framework: p4; evidence and implications: pp5–14. Numerical calibration and commercial inputs remain open.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 3: The investment thesis depends on imports, route access and profitable capacity use
SCR synthesis supporting the opening investment thesis. L/M/H = Low/Medium/High; M/M is baseline. Matrix follows on p4. Each resolution is conditional on the evidence and calibration described in the pack.
Argument | Situation | Complication | Resolution / decision
Transport demand | Subdued aggregate growth masks different product trends. Road freight supports diesel use. | Sector growth, rail recovery, EVs and efficiency change fuel demand. | Demand growth alone cannot establish expansion. L/M/H paths test the product volumes Vopak could serve.
Power demand | Power shortages supported diesel use; Eskom consumption has recently fallen. | Recovery may persist or reverse through outages and replacement delays. | Power recovery can remove diesel support. The same demand paths must include explicit power assumptions.
Domestic supply | Reduced local production has increased reliance on imports. | SAPREF, Natref and Secunda can change domestic fuel output materially. | Domestic supply changes can create import needs even with flat demand. Cross L/M/H supply with demand.
Corridor competition | Durban connects imported fuel to inland customers. | Alternative gateways, delivered costs, reliability and access alter flows. | Vopak benefits only from accessible flows. Delivered economics and access translate imports into Durban volumes.
Vopak investment | Durban and Lesedi provide a coastal–inland asset position. | Capture, usable capacity and commercial returns determine expansion needs. | Expand where capturable flows exceed usable capacity at an adequate return. Compare options across the nine worlds.
Strictly Confidential
Situation
Complication
Resolution
Notes: SCR synthesis supporting the opening investment thesis. L/M/H = Low/Medium/High; M/M is baseline. Matrix follows on p4. Each resolution is conditional on the evidence and calibration described in the pack.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 4: Nine demand–supply worlds frame the choice, with Medium / Medium as baseline
Qualitative framework, not calculated results. Import directions hold exports and stock movements comparable. The diagonal contrasts investment worlds; routing, capture and returns determine the actual choice. M/M calibration remains open.
Fuel demand / domestic supply | HIGH supply | MEDIUM supply | LOW supply
LOW demand | L / H LOWEST IMPORT PRESSURE Test existing-capacity use before expansion. | L / M Lower imports than baseline. Test utilisation and customer capture. | L / L Demand and supply both fall. Net import effect depends on their relative change.
MEDIUM demand | M / H Lower imports than baseline. Supply recovery reduces import needs. | M / M BASELINE Reference imports, terminal throughput and capacity headroom. | M / L Higher imports than baseline. Supply losses increase import needs.
HIGH demand | H / H Demand and supply both rise. Net import effect depends on their relative change. | H / M Higher imports than baseline. Demand growth increases import needs. | H / L HIGHEST IMPORT PRESSURE Test debottlenecking or expansion if capturable flows exceed capacity.
Strictly Confidential
Situation
Complication
Resolution
Each cell will report imports, Vopak Durban / Lesedi throughput, capacity headroom and investment choice.
Notes: Qualitative framework, not calculated results. Import directions hold exports and stock movements comparable. The diagonal contrasts investment worlds; routing, capture and returns determine the actual choice. M/M calibration remains open.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 5: Demand growth alone provides a weak foundation for Vopak’s investment case
Department fuel sales, 2013–2023, same-series comparison. FIASA 2024 shown separately; source definitions require reconciliation. Economic context and sector mechanisms: appendix pp16–18.
Strictly Confidential
Situation
Complication
Resolution
Petrol fell 19% and diesel rose 9% over 2013–2023. This supports the opening thesis: import requirements and accessible customer flows must establish the investment case alongside demand growth.
Notes: Department fuel sales, 2013–2023, same-series comparison. FIASA 2024 shown separately; source definitions require reconciliation. Economic context and sector mechanisms: appendix pp16–18.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 6: Power shortages and road freight have supported parts of diesel demand
Eskom 2025 integrated report (own-fleet diesel + kerosene); Stats SA freight payload. No causal diesel attribution from tonnes alone. Details: appendix pp18, 21–22.
Demand support | Historical evidence | What this establishes
Power generation | Eskom’s own OCGT fuel use rose to 1,129.5m litres in FY2024, then fell to 679.1m in FY2025 as EAF improved. | The historical diesel market includes a material power-system component whose scale can change.
Road freight | The national payload series shows road carrying substantially more tonnage than rail. | Diesel use depends on how freight moves as well as how much the economy produces.
Demand interpretation | Mining and agriculture add sector-specific diesel exposure; aviation has a separate jet-fuel market. | A national GDP forecast alone cannot explain the product and activity mix that terminals serve.
Strictly Confidential
Situation
Complication
Resolution
Notes: Eskom 2025 integrated report (own-fleet diesel + kerosene); Stats SA freight payload. No causal diesel attribution from tonnes alone. Details: appendix pp18, 21–22.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 7: Reduced domestic production has increased the importance of imported supply
SARS litre-reported petrol/diesel trade; CEF 10 Sep 2026 roadmap; PetroSA recommissioning scope; Sasol reporting. Excluded units/blends and stock changes prevent a complete balance.
Strictly Confidential
Situation
Complication
Resolution
Domestic supply context
Mossgas GTL has not operated since December 2020. SAPREF’s current roadmap starts with finished-product imports. Secunda and Natref output remains material to the domestic balance.
The import opportunity can expand even with limited consumption growth. The trade trend and plant evidence support this mechanism; a reconciled product balance is still needed to quantify each plant’s contribution.
Notes: SARS litre-reported petrol/diesel trade; CEF 10 Sep 2026 roadmap; PetroSA recommissioning scope; Sasol reporting. Excluded units/blends and stock changes prevent a complete balance.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 8: The import opportunity is distributed across competing routes into inland markets
Vopak terminal pages and existing corridor evidence. Alternative gateway coverage is a scope for comparison, not a finding that each route is competitive into Gauteng.
Route | Position in the supply chain | Market implication
Durban–Gauteng | Vopak’s coastal and inland terminals are linked through the Transnet multi-product pipeline. Durban also has road and rail access. | The relevant market extends beyond the port into inland customer demand.
Matola / Maputo | An alternative gateway in the review’s corridor comparison. Reach depends on destination and border logistics. | Compare the same product delivered to the same customer location.
Walvis Bay | A further gateway to test for reachable inland destinations. Distance and transit time constrain the comparison. | National imports cannot all be treated as volumes accessible through Durban.
Strictly Confidential
Situation
Complication
Resolution
Notes: Vopak terminal pages and existing corridor evidence. Alternative gateway coverage is a scope for comparison, not a finding that each route is competitive into Gauteng.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 9: Vopak has assets at both ends of the Durban–Gauteng supply chain
Vopak operator inventory checked 6–7 Oct 2026; Gauteng catchment adopted provisionally by user. Gross capacity is not customer throughput or effective working capacity.
Asset | Established position | Implication
Durban | 360,246 m³ published gross capacity; vessel, pipeline, road and rail access. Petroleum products and other liquids. | The coastal asset can serve imported-product handling and onward distribution; eligible fuel tankage needs to be isolated.
Lesedi | 140,000 m³ published capacity for clean petroleum products; connected to Durban via the Transnet pipeline. | The inland asset provides a distribution position in the provisional Gauteng catchment.
Commercial question | Assets establish a physical position. Customer allocation, working capacity and realised turnover determine volumes. | The investment question is how much demand these assets can capture and whether existing capacity can serve it.
Strictly Confidential
Situation
Complication
Resolution
Notes: Vopak operator inventory checked 6–7 Oct 2026; Gauteng catchment adopted provisionally by user. Gross capacity is not customer throughput or effective working capacity.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 10: Rail recovery, EVs and efficiency could weaken transport fuel demand
Mechanisms drawn from the reviewed scope and current cohort architecture. Rail funding evidence: appendix p23; fuel prices and efficiency: pp19–20. Demand and supply paths require calibration.
Potential reversal | Condition for change | Fuel-demand implication
Road to rail | A funded and reliable rail service can transfer suitable freight from trucks. | Displaced road tonne-kilometres reduce diesel use, after rail traction and last-mile fuel. The 250 Mt ambition is not a direct diesel forecast.
EV adoption | Sustained ownership-cost advantages and charging access can influence new-vehicle purchases. | Fuel-price volatility alone does not establish adoption. Replacement cycles govern the effect on the whole fleet.
Vehicle efficiency | More efficient incoming vehicles lower combustion-fleet fuel intensity over time. | Efficiency can offset part of fleet and mileage growth. Apply it only to combustion activity that remains after EV switching.
Strictly Confidential
Situation
Complication
Resolution
Notes: Mechanisms drawn from the reviewed scope and current cohort architecture. Rail funding evidence: appendix p23; fuel prices and efficiency: pp19–20. Demand and supply paths require calibration.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 11: Power recovery can persist, but availability and replacement timing remain risks
Standalone power complication retained as requested. EAF, retirement and commissioning assumptions require later scenario calibration.
Evidence | Interpretation | Implication for Vopak
Recovery persists | A more available coal fleet and replacement generation reduce residual diesel dispatch. | Recent Eskom fuel consumption should not be extrapolated as a permanent growth source.
Recovery reverses | Major breakdowns or retirements before dependable replacement create a generation gap. | Quantify dispatch and operating constraints before translating a gap into fuel litres.
Load shedding | Grid shortages can also affect private backup generation. | Separate Eskom OCGT use from private generators. Ending load shedding does not imply zero Eskom diesel use.
Strictly Confidential
Situation
Complication
Resolution
Notes: Standalone power complication retained as requested. EAF, retirement and commissioning assumptions require later scenario calibration.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 12: Plant-specific uncertainty can change the import requirement in either direction
CEF 10 Sep 2026 roadmap; Sasol 6 Nov 2025 MRG and 1 Sep 2026 Natref releases; PetroSA recommissioning scope. URLs and qualifications in evidence report.
Evidence | Interpretation | Implication for Vopak
SAPREF | CEF describes an import phase followed by a proposed large refinery development. | Import infrastructure can precede any local production recovery. Timing, financing and yields remain conditional.
Secunda | Declining gas supply and potential MRG diversion could reduce liquid output. | MRG bridge is conditional. A quantified liquids penalty requires a gas balance and marginal conversion yield.
Natref | Sasol reported an operational disruption in September 2026. | An outage is not evidence of permanent closure. Confirm recovery and the longer-term investment outlook.
Mossgas / PetroSA | GTL has not operated since December 2020; a recommissioning proposal exists. | Separate stopped historical production from a funded future restart.
Strictly Confidential
Situation
Complication
Resolution
Notes: CEF 10 Sep 2026 roadmap; Sasol 6 Nov 2025 MRG and 1 Sep 2026 Natref releases; PetroSA recommissioning scope. URLs and qualifications in evidence report.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 13: Competing corridors could divert inland volumes away from Durban
Submodel specification adopted from the annotated review. No route winner is asserted without matched costs, access and capacity.
Evidence | Interpretation | Implication for Vopak
Durban–Gauteng | Compare road, rail and pipeline to the same receiving point and product specification. | Include handling, transport, losses, inventory finance and service constraints.
Matola / Maputo | Include inland haul and border costs for each reachable destination. | A port-level cost comparison cannot establish Gauteng competitiveness.
Walvis Bay | Test distance, transit time and corridor capacity into each target market. | Do not assume that every inland customer is economically addressable.
Price bearability | Maximum affordable logistics cost = destination netback less origin product and other delivered costs. | The route with price headroom must also offer capacity and reliable access. Higher national imports do not automatically become Vopak volumes.
Strictly Confidential
Situation
Complication
Resolution
Notes: Submodel specification adopted from the annotated review. No route winner is asserted without matched costs, access and capacity.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 14: Capacity proxies establish scale; customer throughput must establish the investment need
Operator capacities: Vopak Durban 360,246m³, Bidvest Durban 439,306m³, Lesedi 140,000m³. Department Gauteng sales 2022; appendix p24. Transfers between terminals must not be double-counted.
Catchment | Initial inference | What the result can support
Durban | 45.1% of the combined published gross capacity of Vopak and Bidvest in Durban. | A two-operator footprint proxy with mixed products and an incomplete market denominator. It does not establish Durban throughput share.
Gauteng / Lesedi | 2022 petrol + diesel sales: 6.81bn litres. Lesedi’s gross capacity equals 2.06% of that market per effective annual turn. | A cross-vintage scale test. Current sales, eligible working capacity, actual turns and Gauteng allocation are needed for a throughput estimate.
Investment implication | Convert eligible tankage and realised turns into unique customer deliveries, then compare with existing capacity. | A large market can coexist with spare terminal capacity. Market scale alone does not establish a need for additional tanks.
Strictly Confidential
Situation
Complication
Resolution
Notes: Operator capacities: Vopak Durban 360,246m³, Bidvest Durban 439,306m³, Lesedi 140,000m³. Department Gauteng sales 2022; appendix p24. Transfers between terminals must not be double-counted.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 15: Supporting evidence for the main argument
Opening argument: thesis p2, SCR p3, matrix p4. Supporting analysis: pp5–14. Appendix exhibits provide detail for those arguments.
Evidence group | Detail retained | Connection to the story
Demand context | GDP, investment and sector activity | Pages 16–18 support demand arguments on pages 5–6.
Transport change | Fuel prices and vehicle efficiency | Pages 19–20 support the transport complication on page 10.
Historical diesel support | Eskom fuel use and freight payload | Pages 21–22 support historical diesel demand on page 6 and power risk on page 11.
Delivery and market reach | Rail funding constraints and Gauteng demand | Pages 23–24 support corridor and share questions on pages 10, 13 and 14.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Notes: Opening argument: thesis p2, SCR p3, matrix p4. Supporting analysis: pp5–14. Appendix exhibits provide detail for those arguments.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 16: GDP and fuel volumes need separate explanations of activity and sector mix
Staged GDP and department fuel sales, indices 2013=100. Sector attribution remains open; COVID distorts short-period comparisons.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Economic weakness means limited growth in real activity and investment. Structural change means a different mix of output, travel and fuel use; this chart alone cannot attribute causality.
Notes: Staged GDP and department fuel sales, indices 2013=100. Sector attribution remains open; COVID distorts short-period comparisons.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 17: Investment evidence informs the growth outlook but does not establish extra fuel demand
World Bank WDI, FDI net inflows and gross fixed capital formation as % of GDP, 2010–2025. Confidence series remains an evidence gap.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Fixed investment helps frame productive capacity. FDI can include large transactions; neither series is a direct investor-confidence measure or an additional fuel-demand multiplier.
Notes: World Bank WDI, FDI net inflows and gross fixed capital formation as % of GDP, 2010–2025. Confidence series remains an evidence gap.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 18: Mining, agriculture and aviation require distinct demand explanations
Analytical framework following user comments. Sector-specific exhibits and causal attribution remain to be completed.
Evidence | Interpretation | Implication for Vopak
Mining | Output, commodity mix and haul distance influence diesel use and freight. | Separate mine activity from the fuel impact of changing freight mode.
Agriculture | Crop cycles, weather, irrigation and logistics can shift seasonal diesel use. | Establish sector activity and fuel exposure before assigning a headwind.
Aviation | Traffic, distance, load factors and aircraft efficiency drive jet-fuel demand. | Keep jet fuel separate from petrol/diesel shares and verify terminal eligibility.
Manufacturing | Real output and industrial composition help explain the economic backdrop. | Test changes using sector data; a national fuel chart does not prove deindustrialisation.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Notes: Analytical framework following user comments. Sector-specific exhibits and causal attribution remain to be completed.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 19: Fuel-price shocks affect running costs; sustained economics influence EV uptake
Department fuel-price history, nominal R/litre. No quantified geopolitical premium or calibrated EV adoption response is asserted.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Shipping disruption, crude prices and FX can move fuel costs temporarily. EV adoption depends on sustained total ownership cost, purchase affordability, charging access and fleet replacement.
Notes: Department fuel-price history, nominal R/litre. No quantified geopolitical premium or calibrated EV adoption response is asserted.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 20: More efficient new vehicles reduce fuel intensity gradually as the fleet turns over
Mechanism supported by existing cohort architecture. OEM historical and future efficiency evidence is still missing; no new forecast shown.
Evidence | Interpretation | Implication for Vopak
Fleet growth | More vehicles or distance travelled can raise demand. | Measure activity before attributing lower fuel volumes to efficiency.
Efficiency | New-cohort consumption gains enter the fleet over successive replacement cycles. | Obtain OEM and real-world evidence by segment; do not apply new-vehicle gains to every vehicle.
EV substitution | EVs remove some combustion-engine vehicle activity from the fuel calculation. | Count each vehicle transition once, then calculate efficiency on the remaining combustion fleet.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Notes: Mechanism supported by existing cohort architecture. OEM historical and future efficiency evidence is still missing; no new forecast shown.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 21: Eskom’s reported OCGT fuel use fell 40% in FY2025
Eskom integrated report 2025: FY March, own-fleet diesel + kerosene. EAF association is not a dispatch model; private backup use excluded.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Reported fuel fell from 1,129.5 to 679.1 million litres as EAF improved from 54.56% to 60.60%. This removes part of the recent diesel-demand support.
Notes: Eskom integrated report 2025: FY March, own-fleet diesel + kerosene. EAF association is not a dispatch model; private backup use excluded.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 22: Road-to-rail recovery matters through transferable freight and haul distance
Stats SA monthly freight payload, complete calendar years. National tonnes are not corridor tonne-kilometres or transferable freight.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Payload establishes the historical direction. Diesel displacement requires corridor tonne-kilometres, road fuel intensity, rail traction and last-mile activity.
Notes: Stats SA monthly freight payload, complete calendar years. National tonnes are not corridor tonne-kilometres or transferable freight.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 23: Rail recovery on the Durban corridor depends on funding and reliable service
User-supplied AIA Transnet Funding Brief, Sep 2026, pp1–2; cites FY2026 AFS and Network Statement v4 Annexure 17. Primary figures not independently reconciled.
Evidence | Interpretation | Implication for Vopak
Network ambition | The supplied brief reports a 250 Mt target dependent on a funding plan. | Do not treat every additional rail tonne as road displacement. Commodity, corridor and origin matter.
Funding constraint | Brief: R46.34bn approved over five years, including R1.71bn expansion. | Maintenance and sustaining spend dominate. A published plan is insufficient evidence of delivered capacity.
Container corridor | Brief: R2.11bn in 2026/27–2028/29; private funding expected thereafter. | Prioritise Durban–Gauteng road/rail competition and reconcile the corridor to Network Statement v4.
Two fuel effects | Rail can displace truck diesel while improved infrastructure also changes fuel-distribution economics. | Keep freight-demand effects separate from the route delivering fuel to Gauteng.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
Notes: User-supplied AIA Transnet Funding Brief, Sep 2026, pp1–2; cites FY2026 AFS and Network Statement v4 Annexure 17. Primary figures not independently reconciled.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.

## Slide 24: Gauteng provides a demand denominator for testing Lesedi’s potential reach
Department provincial sales, latest complete staged year 2022; Vopak Lesedi current capacity. Cross-vintage scale test only, not current observed market share.
Strictly Confidential
Appendix
Supporting evidence
Reference detail
2022 petrol + diesel sales total 6.81bn litres. Lesedi’s 140,000m³ equals 2.06% of that annual market per effective gross-capacity turn. Actual turns and Gauteng allocation remain unknown.
Notes: Department provincial sales, latest complete staged year 2022; Vopak Lesedi current capacity. Cross-vintage scale test only, not current observed market share.
Evidence: output/delivered/sa_review_2026_10_07_v3/index.html. Comment dispositions: workstreams/WS0_governance/workplan/sa_review_comment_disposition_2026_10_07.csv. Review draft; scenario and commercial calibration pending.